## Slide 1: fd.io Intro
Ed Warnicke

## Slide 2: Evolution of Programmable Networking
Many industries are transitioning to a more dynamic model to deliver network services
The great unsolved problem is how to deliver network services in this more dynamic environment
Inordinate attention has been focused on the non-local network control plane (controllers)
  Necessary, but insufficient
There is a giant gap in the capabilities that foster delivery of dynamic Data Plane Services
Programmable Data Plane
CLOUD
NFV
SDN

## Slide 3: Issues/Limitations with Existing Data Plane Solutions
Known issues with Performance, Scalability & Stability
Overly Complex Architectures
  Hard to evolve
  Slow rate of innovation
  Steep learning curve
Hard to deploy/upgrade/operate
  slow cycles, too many kernel dependencies
Lack of :
  automated end-to-end system testing frameworks
    leads to unpredictable system behavior
  support for diverse/custom hardware
  portability across compute platforms
  optimal use of compute microarchitectures
  network level instrumentation
    Few debugability features
    Few if any Statistics/Counters exposed

## Slide 4: Introducing Fast Data: fd.io
New project in Linux Foundation
  Multi-party
  Multi-project
What does multi-party mean?
  Multiple members - Open to all
What does multi-project mean?
  Multiple subprojects
  Subproject autonomy
  Cross project synergy
  Open to new subprojects
  Anyone can propose a subproject
  Allows for innovation
Create a Platform that enables Data Plane Services that are:
  Highly performant
  Modular and extensible
  Open source
  Interoperable
  Multi-Vendor
Platform fosters innovation and synergistic interoperability between Data Plane Services
Source of Continuous Integration resources for Data Plane services based on the Consortium’s project/subprojects
Meet the functionality needs of developers, deployers, datacenter operators
fd.io Charter

## Slide 5: Fast Data Scope
Fast Data Scope:
    IO
      Hardware/vHardware <-> cores/threads
  Processing
    Classify
    Transform
    Prioritize
    Forward
    Terminate
  Management Agents
    Control/manage IO/Processing
IO
Processing
Management Agent
Bare Metal/VM/Container

## Slide 6: Introducing Vector Packet Processor - VPP
VPP is a rapid packet processing development platform for highly performing network applications.
It runs on commodity CPUs and leverages DPDK
It creates a vector of packet indices and processes them using a directed graph of nodes – resulting in a highly performant solution.
Runs as a Linux user-space application
Ships as part of both embedded & server products, in volume
Active development since 2002
Network IO
Packet Processing
Data Plane Management Agent
Bare Metal/VM/Container

## Slide 7: VPP in the Overall Stack
Hardware
Application Layer / App Server
VM/VIM Management Systems
Network Controller
Operating Systems
Data Plane Services
Orchestration
Network IO
VPP
Packet Processing

## Slide 8: VPP Feature Summary
  14+ MPPS, single core
  Multimillion entry FIBs
  Source RPF
  Thousands of VRFs
  Controlled cross-VRF lookups
  Multipath – ECMP and Unequal Cost
  Multiple million Classifiers –
  Arbitrary N-tuple
  VLAN Support – Single/Double tag
  Counters for everything
  Mandatory Input Checks:
  TTL expiration
  header checksum
  L2 length < IP length
  ARP resolution/snooping
  ARP proxy
  IPv4/IPv6
  IPv4
  GRE, MPLS-GRE, NSH-GRE,
  VXLAN
  IPSEC
  DHCP client/proxy
  CG NAT
  IPv6
  Neighbor discovery
  Router Advertisement
  DHCPv6 Proxy
  L2TPv3
  Segment Routing
  MAP/LW46 – IPv4aas
  iOAM
  MPLS
  MPLS-o-Ethernet –
  Deep label stacks supported
  L2
  VLAN Support
  Single/ Double tag
  L2 forwarding with EFP/BridgeDomain concepts
  VTR – push/pop/Translate (1:1,1:2, 2:1,2:2)
  Mac Learning – default limit of 50k addresses
  Bridging – Split-horizon group support/EFP Filtering
  Proxy Arp
  Arp termination
  IRB – BVI Support with RouterMac assignment
  Flooding
  Input ACLs
  Interface cross-connect
Notes: The input checks included by VPP include mandatory networking checks.
Some solutions today either don’t perform these or don’t have them leading to questionable performance numbers

## Slide 9: Examples of Other possible subprojects
Loadbalancer
Firewall
IDS
Host Stack
Hardware Accelerators
RFC Support
  BFD
  OAM
Control plane – support your favorite SDN Protocol Agent
Spanning Tree
DPI
Test tools
Cloud Foundry Integration
Container Integration
Packaging
Testing

## Slide 10: VPP Architecture - Modularity Enabling Flexible Plugins
Plugins == Subprojects
Plugins can:
  Introduce new graph nodes
  Rearrange packet processing graph
  Can be built independently of VPP source tree
  Can be added at runtime (drop into plugin directory)
  All in user space
Enabling:
  Ability to take advantage of diverse hardware when present
  Support for multiple processor architectures (x86, ARM, PPC)
  Few dependencies on the OS (clib) allowing easier ports to other Oses/Env
ethernet-input
ip6-input
ip4input
mpls-ethernet-input
arp-input
llc-input
…
ip6-lookup
ip6-rewrite-transmit
ip6-local
…
Packet vector
Plug-in to create new nodes
Custom-A
Custom-B
Plug-in to enable new HW input Nodes

## Slide 11: vNet-SLA benchmarking at scale: IPv6 VPP-based vSwitch
Chart: 
| 12 routes | 1k routes | 100k routes | 500k routes | 1M routes | 2M routes
64B | 210 | 210 | 210 | 210 | 210 | 210
IMIX | 160 | 160 | 160 | 160 | 160 | 160
1518B | 39 | 39 | 39 | 39 | 39 | 39
Chart: 
| 12 routes | 1k routes | 100k routes | 500k routes | 1M routes | 2M routes
64B | 108 | 108 | 108 | 108 | 108 | 108
IMIX | 480 | 480 | 480 | 480 | 480 | 480
1518B | 480 | 480 | 480 | 480 | 480 | 480
FD.io VPP data plane throughput not impacted by large size of IPv6 FIB
VPP tested on UCS 4-CPU-socket server with 4 of Intel “Haswell" x86-64 processors E7-8890v3 18C 2.5GHz
24 Cores used – Another 48 cores can be used for other network services!
[Gbps]
Phy-VS-Phy
Zero-packet-loss Throughput for 12 port 40GE, 24 cores, IPv6
[Mpps]
VPP vSwitch IPv4 routed forwarding FIB with 2 milion IPv6 entries 12x40GE (480GE) 64B frames
200Mpps zero frame loss
NIC and PCIe is the limit not VPP
VPP vSwitch IPv4 routed forwarding FIB with 2 milion IPv6 entries
12x40GE (480GE) IMIX frames
480Gbps zero frame loss
“Sky” is the limit not VPP
Zero-packet-loss Throughput for 12 port 40GE, 24 cores, IPv6

## Slide 12
VPP Cores Not Completely Busy
VPP Vectors Have Space For More Services and More Packets!!
PCIe 3.0 and NICs Are The Limit
And How Do We Know This?
Simples – A Well Engineered Telemetry
In Linux and VPP Tells Us So
========
TC5 120ge.vpp.24t24pc.ip4.cop
TC5.0 120ge.2pnic.6nic.rss2.vpp.24t24pc.ip4.cop
d. testcase-vpp-ip4-cop-scale
120ge.2pnic.6nic.rss2.vpp.24t24pc.ip4.2m.cop.2.copip4dst.2k.match.100
64B, 138.000Mpps, 92,736Gbps
IMIX, 40.124832Mpps, 120.000Gbps
1518, 9.752925Mpps, 120.000Gbps
---------------
Thread 1 vpp_wk_0 (lcore 2)
Time 45.1, average vectors/node 23.44, last 128 main loops 1.44 per node 23.00
vector rates in 4.6791e6, out 4.6791e6, drop 0.0000e0, punt 0.0000e0
Name State Calls Vectors Suspends Clocks Vectors/Call
TenGigabitEtherneta/0/1-output active 9003498 211054648 0 1.63e1 23.44
TenGigabitEtherneta/0/1-tx active 9003498 211054648 0 7.94e1 23.44
cop-input active 9003498 211054648 0 2.23e1 23.44
dpdk-input polling 45658750 211054648 0 1.52e2 4.62
ip4-cop-whitelist active 9003498 211054648 0 4.34e1 23.44
ip4-input active 9003498 211054648 0 4.98e1 23.44
ip4-lookup active 9003498 211054648 0 6.25e1 23.44
ip4-rewrite-transit active 9003498 211054648 0 3.43e1 23.44
---------------
Thread 24 vpp_wk_23 (lcore 29)
Time 45.1, average vectors/node 27.04, last 128 main loops 1.75 per node 28.00
vector rates in 4.6791e6, out 4.6791e6, drop 0.0000e0, punt 0.0000e0
Name State Calls Vectors Suspends Clocks Vectors/Call
TenGigabitEthernet88/0/0-outpu active 7805705 211055503 0 1.54e1 27.04
TenGigabitEthernet88/0/0-tx active 7805705 211055503 0 7.75e1 27.04
cop-input active 7805705 211055503 0 2.12e1 27.04
dpdk-input polling 46628961 211055503 0 1.60e2 4.53
ip4-cop-whitelist active 7805705 211055503 0 4.35e1 27.04
ip4-input active 7805705 211055503 0 4.86e1 27.04
ip4-lookup active 7805705 211055503 0 6.02e1 27.04
ip4-rewrite-transit active 7805705 211055503 0 3.36e1 27.04

## Slide 13
VPP Cores Not Completely Busy
VPP Vectors Have Space For More Services and More Packets!!
PCIe 3.0 and NICs Are The Limit
And How Do We Know This?
Simples – A Well Engineered Telemetry
In Linux and VPP Tells Us So
========
TC5 120ge.vpp.24t24pc.ip4.cop
TC5.0 120ge.2pnic.6nic.rss2.vpp.24t24pc.ip4.cop
d. testcase-vpp-ip4-cop-scale
120ge.2pnic.6nic.rss2.vpp.24t24pc.ip4.2m.cop.2.copip4dst.2k.match.100
64B, 138.000Mpps, 92,736Gbps
IMIX, 40.124832Mpps, 120.000Gbps
1518, 9.752925Mpps, 120.000Gbps
---------------
Thread 1 vpp_wk_0 (lcore 2)
Time 45.1, average vectors/node 23.44, last 128 main loops 1.44 per node 23.00
vector rates in 4.6791e6, out 4.6791e6, drop 0.0000e0, punt 0.0000e0
Name State Calls Vectors Suspends Clocks Vectors/Call
TenGigabitEtherneta/0/1-output active 9003498 211054648 0 1.63e1 23.44
TenGigabitEtherneta/0/1-tx active 9003498 211054648 0 7.94e1 23.44
cop-input active 9003498 211054648 0 2.23e1 23.44
dpdk-input polling 45658750 211054648 0 1.52e2 4.62
ip4-cop-whitelist active 9003498 211054648 0 4.34e1 23.44
ip4-input active 9003498 211054648 0 4.98e1 23.44
ip4-lookup active 9003498 211054648 0 6.25e1 23.44
ip4-rewrite-transit active 9003498 211054648 0 3.43e1 23.44
---------------
Thread 24 vpp_wk_23 (lcore 29)
Time 45.1, average vectors/node 27.04, last 128 main loops 1.75 per node 28.00
vector rates in 4.6791e6, out 4.6791e6, drop 0.0000e0, punt 0.0000e0
Name State Calls Vectors Suspends Clocks Vectors/Call
TenGigabitEthernet88/0/0-outpu active 7805705 211055503 0 1.54e1 27.04
TenGigabitEthernet88/0/0-tx active 7805705 211055503 0 7.75e1 27.04
cop-input active 7805705 211055503 0 2.12e1 27.04
dpdk-input polling 46628961 211055503 0 1.60e2 4.53
ip4-cop-whitelist active 7805705 211055503 0 4.35e1 27.04
ip4-input active 7805705 211055503 0 4.86e1 27.04
ip4-lookup active 7805705 211055503 0 6.02e1 27.04
ip4-rewrite-transit active 7805705 211055503 0 3.36e1 27.04
VPP average vector size below shows 23-to-27
This indicates VPP program worker threads are not busy
Busy VPP worker threads should be showing 255
This means that VPP worker threads operate at 10% capacity
It’s like driving 1,000hp car at 100hp power – lots of space
for adding (service) acceleration and (sevice) speed.

## Slide 14
VPP Cores Not Completely Busy
VPP Vectors Have Space For More Services and More Packets!!
PCIe 3.0 and NICs Are The Limit
And How Do We Know This?
Simples – A Well Engineered Telemetry
In Linux and VPP Tells Us So
========
TC5 120ge.vpp.24t24pc.ip4.cop
TC5.0 120ge.2pnic.6nic.rss2.vpp.24t24pc.ip4.cop
d. testcase-vpp-ip4-cop-scale
120ge.2pnic.6nic.rss2.vpp.24t24pc.ip4.2m.cop.2.copip4dst.2k.match.100
64B, 138.000Mpps, 92,736Gbps
IMIX, 40.124832Mpps, 120.000Gbps
1518, 9.752925Mpps, 120.000Gbps
---------------
Thread 1 vpp_wk_0 (lcore 2)
Time 45.1, average vectors/node 23.44, last 128 main loops 1.44 per node 23.00
vector rates in 4.6791e6, out 4.6791e6, drop 0.0000e0, punt 0.0000e0
Name State Calls Vectors Suspends Clocks Vectors/Call
TenGigabitEtherneta/0/1-output active 9003498 211054648 0 1.63e1 23.44
TenGigabitEtherneta/0/1-tx active 9003498 211054648 0 7.94e1 23.44
cop-input active 9003498 211054648 0 2.23e1 23.44
dpdk-input polling 45658750 211054648 0 1.52e2 4.62
ip4-cop-whitelist active 9003498 211054648 0 4.34e1 23.44
ip4-input active 9003498 211054648 0 4.98e1 23.44
ip4-lookup active 9003498 211054648 0 6.25e1 23.44
ip4-rewrite-transit active 9003498 211054648 0 3.43e1 23.44
---------------
Thread 24 vpp_wk_23 (lcore 29)
Time 45.1, average vectors/node 27.04, last 128 main loops 1.75 per node 28.00
vector rates in 4.6791e6, out 4.6791e6, drop 0.0000e0, punt 0.0000e0
Name State Calls Vectors Suspends Clocks Vectors/Call
TenGigabitEthernet88/0/0-outpu active 7805705 211055503 0 1.54e1 27.04
TenGigabitEthernet88/0/0-tx active 7805705 211055503 0 7.75e1 27.04
cop-input active 7805705 211055503 0 2.12e1 27.04
dpdk-input polling 46628961 211055503 0 1.60e2 4.53
ip4-cop-whitelist active 7805705 211055503 0 4.35e1 27.04
ip4-input active 7805705 211055503 0 4.86e1 27.04
ip4-lookup active 7805705 211055503 0 6.02e1 27.04
ip4-rewrite-transit active 7805705 211055503 0 3.36e1 27.04
VPP average vector size below shows 23-to-27
This indicates VPP program worker threads are not busy
Busy VPP worker threads should be showing 255
This means that VPP worker threads operate at 10% capacity
It’s like driving 1,000bhp car at 100bhp power – lots of space
for adding (service) acceleration and (sevice) speed.
VPP is also counting the cycles-per-packet (CPP)
We know exactly what feature, service, packet processing activity is using the CPU cores
We can engineer, we can capacity plan, we can automate service placement
We can scale across many many CPU cores and computers
And AUTOMATE it easily – as it is after all just SOFTWARE

## Slide 15: Implementation Example: VPP as a vRouter/vSwitch
Out of the box vSwitch/vRouter
  Including CLI
Switching
  Can Create
  Bridge Domains
  Ports (including tunnel ports)
  Connect ports to bridge domains
  Program ARP termination
  etc
Routing
  Can Create
  VRFs - thousands
  Routes - millions
Linux Host
Kernel
DPDK
VPP App
Switch-1
Switch-2
VRF-1
VRF-2

## Slide 16: VPP vRouter/vSwitch: Local Programmability
Linux Host
Kernel
DPDK
VPP App
External App
Low Level API
  Complete
  Feature Rich
  High Performance
    Example: 500k routes/s
  Shared memory/message queue
  Box local
  All CLI tasks can be done via API
Generated Low Level Bindings - existing today
  C clients
  Java clients
  Others can be done

## Slide 17: VPP vRouter/vSwitch: Remote Programmability
Linux Host
Kernel
DPDK
VPP App
Data Plane Management Agent
High Level API: An approach
  Data Plane Management Agent
  Speaks low level API to VPP
  Box (or VM or container) local
  Exposes higher level API via some binding
Flexibility:
  VPP does not force a particular Data Plane Management Agent
  VPP does not force only *one* High Level API
  Anybody can bring a Data Plane Management Agent
  High Level API/Data Plane Management Agent
  Match VPP app needs
netconf/yang
REST
Other (BGP)

## Slide 18: Honeycomb Data Plane Management Agent
Linux Host
Kernel
DPDK
VPP App
ODL Honeycomb Agent
High Level API: An Approach
  Yang Models via netconf/restconf
  Box local ODL instance (Honeycomb) using low level API over generated Java Bindings to talk to VPP App, and exposing yang models over netconf/restconf NB
  Initial example: Bridge Domains
netconf/yang
REST
Other (BGP)

## Slide 19: VPP & ODL in Openstack
Working on installer changes needed to add ODL & VPP as the networking stack for Openstack
Provides a programmable interface to include ‘edge’ network programming into a virtual environment
Allows for multiple data plane forwarders to be active
VPP
OVS
Control Plane
Data Plane
Openstack
Neutron
ODL
Plugin
HC

## Slide 20: Continuous Performance Lab (CPL)
Fully automated testing infrastructure
  Covers both programmability and data planes
Continuous verification of code/feature
  Functionality and performance
Code breakage and performance degradations identified before patch review
  Review, commit and release resource protected
Fully open sourced test framework to be included at launch
Submit Patch
Automated Testing
Deploy
Develop

## Slide 21: Continuous Performance Lab (CPL)
Continuous Functional Testing
  VM based virtual testbeds (3-node/3-VM topologies)
  Continuous verification of feature conformance
  Highly parallel test execution
  Membership dues can donate VMs …. to the CPL
Continuous Benchmark Testing
  Server based hardware testbeds (3-node/3-server topologies)
  Continuous integration process with real hardware verification
    Server models, CPU models, NIC models
  Platinum Members can donate hardware to the CPL
Submit Patch
Automated Testing
Deploy
Develop

## Slide 22: Governance – At a Glance
Anyone May Participate – Not just members
  Anyone can contribute code
  Anyone can rise to being a committer via meritocracy
  Anyone can propose a subproject
Subprojects:
  Composed of the committers to that subproject – those who can merge code
  Responsible for sub project oversight and autonomous releases
  Make technical decisions for that subproject by consensus, or failing that, majority vote.
Technical Steering Committee
  Fosters collaboration among subprojects, but is not involved in day to day management of sub-projects
  Approves new subprojects, sets development process guidelines for the community, sets release guidelines for multi-project or simultaneous releases, etc.
  Initial TSC will be seeded with representatives from Platinum Membership and core project PTLs with the goal of replacing representatives with Project Leads after the first year
Governing Board will Oversee Business Decision Making
  Set Scope and Policy of Consortium
  Composed of Platinum member appointees, elected Gold, Silver, and Committer member representatives
  Examples of business needs include: budgeting, planning for large meetings (e.g. a Summit, Hackfest), marketing, websites, developer infrastructure, test infrastructure, etc.

## Slide 23: Additional subprojects on their way
  Honeycomb Agent
    Available now
    Netconf/yang/restconf bridge domain yang models
    More yang models to follow
  LISP xTR
    New subproject shortly post launch with initial code
  NSH
    New subproject shortly post launch
  Netlink agent
vSwitch

## Slide 24: Next Steps – Get Involved
We invite you to Participate in fd.io
Attend “fd.io Meetup” Wed 5:00pm in Napa
Attend Packet Processed Storage in a Software Defined World Thu 3:15pm in Grand Ballroom F
Register for fd.io Training/Hackfest April 4-7, 2016 in Santa Clara
Get the Code, Build the Code, Run the Code
Read/Watch the Tutorials
Join the Mailing Lists
Join the IRC Channels
Explore the wiki