## Slide 1: ODL SFC and VPP Integration
Yi Yang @ Intel
Keith Burns @ CISCO
Hongjun Ni @ Intel

## Slide 2: Agenda
SFC Introduction
FD.io Work for SFC Support
ODL SFC VPP Renderer
NSH_SFC (Keith Burns)
ODL SFC and VPP Integration Architecture
ODL SFC and VPP Integration Demo Overview
DEMO
Q & A
Future Work to Do

## Slide 3: SFC (Service Function Chaining) Introduction
SFF1
SF1
(Firewall)
SFF2
SF2
(DPI)
Classifier1
Classifier2
Client1
Client2
Client3
Server
Legend
SFC Component
SFF: Service Function Forwarder NSI: Network Service Index
SF : Service Function NSP: Network Service Path
RSP: Rendered Service Path, SFC Instance
NSH: Network Service Header
Service Function Chain

## Slide 4: Work in VPP and NSH_SFC and Honeycomb
VPP: VxLAN-gpe (Keith Burns@CISCO)
VPP: Plugin Infrastructure, JVPP core for VxLAN-gpe, JVPP NSH for NSH_SFC (Marek@CISCO)
NSH_SFC: NSH implementation (Keith Burns@CISCO, Hongjun Ni@Intel)
Honeycomb: REST and Netconf interface to ODL SFC (VxLAN-gpe v3po YANG, NSH Yang Model, Hongjun Ni@Intel)
Honeycomb: Plugin Infrastructure (Maros@CISCO) and NSH_SFC plugin (Hongjun Ni@Intel)

## Slide 5: VPP Renderer in ODL SFC Architecture
SFC Provider
Data Store
SFC UI
RESTCONF
OpenFlow Renderer
IOS XE Renderer
VPP Renderer
SFCOVS
Openflowplugin
Netconf
OVSDB
Switch (OVS)
Netconf Device (VPP node)
Devices
ODL
SBI
SFC

## Slide 6: NSH_SFC

## Slide 7: ODL SFC and VPP Integration Architecture
VPP
OpenDaylight SFC
Honeycomb
HC Core
VPP Renderer
Netconf/YANG
VPP Core
JVPP Core
Core Binary APIs
HC NSH Plugin
VxLAN-GPE
NSH_SFC plugin
JVPP NSH Plugin
NSH Entry and NSH Map
JVPP Registry
VPP Connection
NSH Binary APIs
Data Broker
Config Data Tree
Operational Data Tree
Translation Layer
JVPP APIs
JVPP APIs

## Slide 8: ODL SFC and VPP Integration Demo Topology
Classifier1
VPP1/SFF1
BridgeDomain:SFCVPP
VxLANgpe1
SF 1
Web Client
VxLANgpe0
VPP2/SFF2
BridgeDomain:SFCVPP
GigabitEthernet0/9/0
192.168.20.12
VxLANgpe1
VxLANgpe0
Eth2
192.168.20.10
SF 2
veth1
10.0.100.9
Eth2
192.168.20.9
Classifier2
Web Server
veth1
10.0.100.14
Eth2
192.168.20.13
Eth2
192.168.20.14
GigabitEthernet0/9/0
192.168.20.11
VxLANgpe2
VxLANgpe2
ODL SFC
vboxnet2
192.168.10.1
Eth1
192.168.10.11
Eth1
192.168.10.12
Control Plane
Data Plane

## Slide 9: ODL SFC and VPP Integration Demo Topology (cont’d)
Classifier1
VPP1/SFF1
BridgeDomain:SFCVPP
VxLANgpe1
SF 1
Web Client
VxLANgpe0
VPP2/SFF2
BridgeDomain:SFCVPP
GigabitEthernet0/9/0
192.168.20.12
VxLANgpe1
VxLANgpe0
Eth2
192.168.20.10
SF 2
veth1
10.0.100.9
Eth2
192.168.20.9
Classifier2
Web Server
veth1
10.0.100.14
Eth2
192.168.20.13
Eth2
192.168.20.14
GigabitEthernet0/9/0
192.168.20.11
VxLANgpe2
VxLANgpe2
Data Plane
Forward RSP: webclient  Classifier1  VPP1  SF1  VPP1  VPP2  SF2  VPP2  Classifier2  webserver
Reverse RSP: webserver  Classifier2  VPP2  SF2  VPP2  VPP1  SF1  VPP1  Classifier1  webclient

## Slide 10: ODL SFC and VPP Integration Demo
DEMO

## Slide 11
Q & A

## Slide 12: Future Work to Do
VPP Classifier to support SFC
SFC VPP Classifier
VPP NSH Proxy
SFC NSH Proxy
VPP to support Ethernet + NSH
NSH_SFC to support MD Type 2

## Slide 13: References
OVS NSH version: https://github.com/yyang13/ovs_nsh_patches
ODL SFC: https://git.opendaylight.org/gerrit/gitweb?p=sfc.git;a=summary
vxlan-tool.py: python-based NSH-aware service function, https://git.opendaylight.org/gerrit/gitweb?p=sfc.git;a=blob_plain;f=sfc-test/nsh-tools/vxlan_tool.py;h=d7b75316f0e29c1dc09ec63b17a054c2fcdf20af;hb=HEAD
nsh_sfc: https://gerrit.fd.io/r/gitweb?p=nsh_sfc.git;a=summary
Honeycomb overview: https://wiki.fd.io/view/File:Honeycomb_overview.pptx
nsh_sfc and VxLAN-gpe Design: https://drive.google.com/file/d/0B_RDwdFu5VJDRzlZZ1ozRW9faFE/view

## Slide 14: Build & Start Instructions
VPP Build
$ git clone https://gerrit.fd.io/r/p/vpp.git
$ cd vpp/build-root
$ make distclean && ./bootstrap.sh && make V=0 PLATFORM=vpp TAG=vpp install-deb
$ sudo dpkg -i *.deb
$ cd build-vpp-native/vpp-api/java/
$ mvn install:install-file -Dfile=jvpp-registry-16.12.jar -DgroupId=io.fd.vpp -DartifactId=jvpp-registry -Dversion=16.12-SNAPSHOT -Dpackaging=jar
$ mvn install:install-file -Dfile=jvpp-core-16.12.jar -DgroupId=io.fd.vpp -DartifactId=jvpp-core -Dversion=16.12-SNAPSHOT -Dpackaging=jar
$ cd ../../../../..
NSH_SFC Build
$ git clone https://gerrit.fd.io/r/p/nsh_sfc.git
$ cd nsh_sfc/nsh-plugin
$ ./build.sh
$ cd build/java/jvpp
$ mvn package
$ mvn install:install-file -Dfile=./target/nsh-sfc-16.12-SNAPSHOT.jar -DgroupId=io.fd.vpp -DartifactId=nsh-sfc -Dversion=16.12-SNAPSHOT -Dpackaging=jar
$ cd ../../../../..

## Slide 15: Build & Start Instructions (cont.)
Copy nsh_sfc plugin to vpp plugin directory
$ cd nsh_sfc/nsh-plugin
$ sudo cp ./build/.libs/nsh_plugin.so /usr/lib/vpp_plugins/
$ sudo cp ./build/.libs/nsh_test_plugin.so /usr/lib/vpp_api_test_plugins/
$ cd ../..
honeycomb Build
$ git clone https://gerrit.fd.io/r/p/honeycomb.git
$ cd honeycomb
$ mvn clean install -nsu -DskipTests -Dmaven.javadoc.skip=true

## Slide 16: Build & Start Instructions (cont.)
Start VPP
$ sudo start vpp
$ sudo status vpp
Start honeycomb
$ sudo rm -f /var/lib/honeycomb/persist/config/data.json
$ sudo rm -f /var/lib/honeycomb/persist/context/data.json
$ cd honeycomb
$ sudo sh ./nsh/minimal-distribution/target/minimal-distribution-1.16.12-SNAPSHOT-hc/minimal-distribution-1.16.12-SNAPSHOT/honeycomb

## Slide 17: Build & Start Instructions (cont.)
Build ODL SFC
$ git clone https://git.opendaylight.org/gerrit/p/sfc.git
$ mvn clean install -DskipTests
Start ODL SFC
$ export JAVA_HOME=/usr/lib/jvm/java-1.8.0/jre/
$ cd sfc-karaf/target/assembly
$ ./bin/karaf
In karaf console, install the below features
opendaylight-user@root> feature:install odl-sfc-vpp-renderer odl-sfc-ui
curl -v -u admin:admin http://localhost:8181/restconf/streams
Or
http://localhost:8181/index.html
Or
Postman
Can check if ODL SFC is started normally

## Slide 18: Appendix
vagrant@vpp1:~/vpp$ sudo vppctl show vxlan-gpe
[0] local: 192.168.20.11 remote: 192.168.20.10 vxlan VNI 0 next-protocol nsh fibs: (encap 0, decap 0)
[1] local: 192.168.20.11 remote: 192.168.20.12 vxlan VNI 0 next-protocol nsh fibs: (encap 0, decap 0)
[2] local: 192.168.20.11 remote: 192.168.20.9 vxlan VNI 0 next-protocol nsh fibs: (encap 0, decap 0)
vagrant@vpp1:~/vpp$

## Slide 19: Appendix (cont.)
vagrant@vpp1:~/vpp$ sudo vppctl show nsh entry
nsh ver 0 len 6 (24 bytes) md_type 1 next_protocol 3
service path 29 service index 255
c1 0 c2 0 c3 0 c4 0
nsh ver 0 len 6 (24 bytes) md_type 1 next_protocol 3
service path 29 service index 254
c1 0 c2 0 c3 0 c4 0
nsh ver 0 len 6 (24 bytes) md_type 1 next_protocol 3
service path 8388637 service index 254
c1 0 c2 0 c3 0 c4 0
nsh ver 0 len 6 (24 bytes) md_type 1 next_protocol 3
service path 8388637 service index 253
c1 0 c2 0 c3 0 c4 0
vagrant@vpp1:~/vpp$

## Slide 20: Appendix (cont.)
vagrant@vpp1:~/vpp$ sudo vppctl show nsh map
nsh entry nsp: 29 nsi: 255 maps to nsp: 29 nsi: 255 encapped by VXLAN GPE intf: 3
nsh entry nsp: 29 nsi: 254 maps to nsp: 29 nsi: 254 encapped by VXLAN GPE intf: 4
nsh entry nsp: 8388637 nsi: 254 maps to nsp: 8388637 nsi: 254 encapped by VXLAN GPE intf: 3
nsh entry nsp: 8388637 nsi: 253 maps to nsp: 8388637 nsi: 253 encapped by VXLAN GPE intf: 5
vagrant@vpp1:~/vpp$

## Slide 21: Appendix (cont.)
vagrant@classifier1:~$ cat test-flows-odl.txt
table=0,ip,nw_dst=192.168.20.9 actions=NORMAL
table=0,ip,nw_dst=192.168.20.11 actions=output:1
table=0,icmp,in_port=4,nw_src=10.0.100.9,nw_dst=10.0.100.14 actions=push_nsh,
load:0x1->NXM_NX_NSH_MDTYPE[],load:0x3->NXM_NX_NSH_NP[],load:29->NXM_NX_NSP[0..23],
load:0xff->NXM_NX_NSI[],load:0x1->NXM_NX_NSH_C1[],load:0x9->NXM_NX_NSH_C2[],
load:0x3->NXM_NX_NSH_C3[],load:0x4->NXM_NX_NSH_C4[],load:0x4->NXM_NX_TUN_GPE_NP[],
load:9->NXM_NX_TUN_ID[0..31],load:0xc0a8140b->NXM_NX_TUN_IPV4_DST[],output:2
table=0,tcp,in_port=4,nw_src=10.0.100.9,nw_dst=10.0.100.14 actions=push_nsh,
load:0x1->NXM_NX_NSH_MDTYPE[],load:0x3->NXM_NX_NSH_NP[],load:29->NXM_NX_NSP[0..23],
load:0xff->NXM_NX_NSI[],load:0x1->NXM_NX_NSH_C1[],load:0x9->NXM_NX_NSH_C2[],
load:0x3->NXM_NX_NSH_C3[],load:0x4->NXM_NX_NSH_C4[],load:0x4->NXM_NX_TUN_GPE_NP[],
load:9->NXM_NX_TUN_ID[0..31],load:0xc0a8140b->NXM_NX_TUN_IPV4_DST[],output:2
table=0,nsp=8388637,nsi=253 actions=pop_nsh,
set_field:00:00:10:00:64:14->eth_src,set_field:00:00:10:00:64:09->eth_dst,output:4
table=0 actions=NORMAL
vagrant@classifier1:~$