## Slide 1
The Universal Fast Dataplane

## Slide 2: A Fast Data Network Platform For Native Cloud Network Services
2
Superior Performance
Most Efficient on the Planet
Flexible and Extensible
Open Source
Cloud Native
Breaking the Barrier of Software Defined Network Services 1 Terabit Services on a Single Intel® Xeon® Server !!!
The most efficient software packet
Processing on the planet
FD.io on x86 servers outperforms specialized packet processing HW
Foundation for cloud native network services
Software programmable, extendable and flexible
Open source collaborative project in Linux Foundation
EFFICIENCY
PERFORMANCE
SOFTWARE DEFINED NETWORKING
CLOUD NETWORK SERVICES
LINUX FOUNDATION

## Slide 3: FD.io: The Universal Fast Dataplane
Project at Linux Foundation
  Multi-party
  Multi-project
Software Dataplane
  High throughput
  Low Latency
  Feature Rich
  Resource Efficient
  Bare Metal/VM/Container
  Multiplatform
Bare Metal/VM/Container
FD.io Scope
  Network IO – NIC/vNIC <-> cores/threads
  Packet Processing – Classify / Transform / Prioritize / Forward / Terminate
  Dataplane Management Agents – Control Plane
Dataplane Management Agent
Packet Processing
Network IO

## Slide 4: Fd.io in the overall stack
Hardware
Network Controller
Orchestration
Operating System
Data Plane Services
Application Layer/App Server
Packet Processing
Network IO
Dataplane Management Agent

## Slide 5: Multiparty: Broad Membership
Service Providers
Network Vendors
Chip Vendors
Integrators

## Slide 6: Multiparty: Broad Contribution
Universitat Politècnica de Catalunya (UPC)
Yandex
Qiniu

## Slide 7: Code Activity
In the period since its inception, fd.io has more commits than OVS and DPDK combined, and more contributors than OVS
2016-02-11 to 2017-04-03 | Fd.io | OVS | DPDK
Commits | 6283 | 2395 | 3289
Contributors | 163 | 146 | 245
Organizations | 42 | 52 | 78
Chart: Commits
| Commits
fd.io | 6283
OVS | 2395
DPDK | 3289
Chart: Contributors
| Contributors
fd.io | 163
OVS | 146
DPDK | 245
Chart: Organizations
| Organizations
fd.io | 42
OVS | 52
DPDK | 75

## Slide 8: Multiproject: Fd.io Projects
Honeycomb
hc2vpp
Dataplane Management Agent
CSIT
puppet-fdio
trex
Testing/Support
NSH_SFC
ONE
TLDK
odp4vpp
CICN
VPP Sandbox
VPP
Packet Processing
deb_dpdk
rpm_dpdk
Network IO

## Slide 9: Fd.io Integrations
VPP
Control Plane
Data Plane
Honeycomb
Netconf/Yang
VBD app
Lispflowmapping app
LISP Mapping Protocol
SFC
Netconf/yang
Openstack
Neutron
ODL
Plugin
Fd.io
Plugin
Fd.io ML2 Agent
REST
GBP app
Integration work done at

## Slide 10: Vector Packet Processor - VPP
Packet Processing Platform
  High performance
  Linux User space
  Run’s on commodity CPUs: / /
  Shipping at volume in server & embedded products since 2004.
Bare Metal/VM/Container
Dataplane Management Agent
Packet Processing
Network IO

## Slide 11: Aside [1/4]: Computer Evolution For Packet Processing It started with ALU …
An Arithmetic Logic Unit (ALU)
(1) It started simple …
* Intel Top-Down Microarchitecture Analysis Method for tuning applications, https://software.intel.com/en-us/top-down-microarchitecture-analysis-method-win
(3) Then it got much faster …
A modern two CPU socket server
A
C
D
A
B
(4) … but far from simple !
The pipeline of a modern high-performance XEON CPU*
A simple generic purpose computer
(2) Became universal and faster …

## Slide 12: Aside [2/4]: Computer Evolution For Packet Processing … and we arrived to modern multi-socket COTS server …
An Arithmetic Logic Unit (ALU)
(1) It started simple …
* Intel Top-Down Microarchitecture Analysis Method for tuning applications, https://software.intel.com/en-us/top-down-microarchitecture-analysis-method-win
(3) Then it got much faster …
A modern two CPU socket server
(4) … but far from simple !
The pipeline of a modern high-performance XEON CPU*
A simple generic purpose computer
(2) Became universal and faster …
A
C
D
A
B

## Slide 13: Aside [2/4]: Computer Evolution For Packet Processing … and we arrived to modern multi-socket COTS server …
An Arithmetic Logic Unit (ALU)
(1) It started simple …
* Intel Top-Down Microarchitecture Analysis Method for tuning applications, https://software.intel.com/en-us/top-down-microarchitecture-analysis-method-win
(3) Then it got much faster …
A modern two CPU socket server
(4) … but far from simple !
The pipeline of a modern high-performance XEON CPU*
A simple generic purpose computer
(2) Became universal and faster …
CPUs executing the program(s):
  Minimize Instructions per Packet – Efficient software logic to perform needed packet operations.
  Maximize Instructions per CPU core clock cycle – Execution efficiency of an underlying CPU micro-architecture.
Memory bandwidth: Minimize memory bandwidth utilization – Memory access is slow.
Network I/O bandwidth: Make efficient use of PCIe I/O bandwidth – It is a limited resource.
Inter-socket transactions: Minimize cross-NUMA connection utilization – It slows things down.
Four main functional dimensions important for processing packets:
Hint: Start with optimizing the use of CPU micro-architecture => Use vectors !
A
C
D
A
B

## Slide 14: VPP Architecture: Vector Packet Processing
Packet
Vector of n packets
ethernet-input
dpdk-input
vhost-user-input
af-packet-input
ip4-input
ip6-input
arp-input
ip6-lookup
ip4-lookup
ip6-local
ip6-rewrite
ip4-rewrite
ip4-local
mpls-input
…
…
Packet Processing
Graph
Graph Node
Input Graph Node
0
1
3
2
…
n

## Slide 15: VPP Architecture: Splitting the Vector
Packet
Vector of n packets
ethernet-input
dpdk-input
vhost-user-input
af-packet-input
ip4-input
ip6-input
arp-input
ip6-lookup
ip4-lookup
ip6-local
ip6-rewrite
ip4-rewrite
ip4-local
mpls-input
…
…
Packet Processing
Graph
Graph Node
Input Graph Node
2
0
1
3
…
n

## Slide 16: VPP Architecture: Plugins
0
1
3
2
…
n
Packet
Vector of n packets
ethernet-input
dpdk-input
vhost-user-input
af-packet-input
ip4-input
ip6-input
arp-input
ip6-lookup
ip4-lookup
ip6-local
ip6-rewrite
ip4-rewrite
ip4-local
mpls-input
…
…
custom-1
custom-2
custom-3
Packet Processing
Graph
Graph Node
Input Graph Node
/usr/lib/vpp_plugins/foo.so
Plugin
Plugins are:
First class citizens
That can:
Add graph nodes
Add API
Rearrange the graph
Hardware Plugin
hw-accel-input
Skip software nodes
where work is done by
hardware already
Can be built independently
of VPP source tree

## Slide 17: Aside [3/4]: Computer Evolution For Packet Processing … we then optimize software for network workloads ...
An Arithmetic Logic Unit (ALU)
(1) It started simple …
* Intel Top-Down Microarchitecture Analysis Method for tuning applications, https://software.intel.com/en-us/top-down-microarchitecture-analysis-method-win
(3) Then it got much faster …
A modern two CPU socket server
(4) … but far from simple !
The pipeline of a modern high-performance XEON CPU*
A simple generic purpose computer
(2) Became universal and faster …
A
C
D
A
B

## Slide 18: Aside [3/4]: Computer Evolution For Packet Processing … we then optimize software for network workloads ...
An Arithmetic Logic Unit (ALU)
(1) It started simple …
* Intel Top-Down Microarchitecture Analysis Method for tuning applications, https://software.intel.com/en-us/top-down-microarchitecture-analysis-method-win
(3) Then it got much faster …
A modern two CPU socket server
(4) … but far from simple !
The pipeline of a modern high-performance XEON CPU*
A simple generic purpose computer
(2) Became universal and faster …
A
C
D
A
B
Network workloads are very different from compute ones
  They are all about processing packets, at rate.
  At 10GE, 64B packets can arrive at 14.88Mpps => 67 nsec per packet.
  With 2GHz CPU core clock cycle is 0.5nsec => 134 clock cycles per packet.
  To access memory it takes ~70nsec => too slow to do it per packet !
  Packet processing efficiency is essential
  Moving packets
    Packets arrive on physical interfaces (NICs) and virtual interfaces (VNFs) - need CPU optimized drivers for both.
    Drivers and buffer management software must not rely on memory access – see time budget above, MUST use CPU core caching hierarchy well.
  Processing packets
    Need packet processing optimized for CPU platforms.
    Header manipulation, encaps/decaps, lookups, classifiers, counters.

## Slide 19: Aside [3/4]: Computer Evolution For Packet Processing … we then optimize software for network workloads ...
An Arithmetic Logic Unit (ALU)
(1) It started simple …
(3) Then it got much faster …
A modern two CPU socket server
A simple generic purpose computer
(2) Became universal and faster …
A
C
D
A
B
Network workloads are very different from compute ones
  They are all about processing packets, at rate.
  At 10GE, 64B packets can arrive at 14.88Mpps => 67 nsec per packet.
  With 2GHz CPU core clock cycle is 0.5nsec => 134 clock cycles per packet.
  To access memory it takes ~70nsec => too slow to do it per packet !
  Packet processing efficiency is essential
  Moving packets
    Packets arrive on physical interfaces (NICs) and virtual interfaces (VNFs) - need CPU optimized drivers for both.
    Drivers and buffer management software must not rely on memory access – see time budget above, MUST use CPU core caching hierarchy well.
  Processing packets
    Need packet processing optimized for CPU platforms.
    Header manipulation, encaps/decaps, lookups, classifiers, counters.
PCIe
CPU Cores
CPU Socket
Memory Controller
DDR SDRAM
Memory
Channels
LLC
Core operations
NIC packet operations
NIC descriptor operations
1
rxd
txd
packet
2
3
4
5
6
8
7
9
10
11
12
13
NICs
No-to-Minimal memory
bandwidth per packet.
(4a) … let’s make it Simple Again!
AND =>

## Slide 20: Aside [4/4]: Computer Evolution For Packet Processing … and use FD.io VPP to make them fast for packets.
An Arithmetic Logic Unit (ALU)
(1) It started simple …
(3) Then it got much faster …
A modern two CPU socket server
A simple generic purpose computer
(2) Became universal and faster …
A
C
D
A
B
PCIe
CPU Cores
CPU Socket
Memory Controller
DDR SDRAM
Memory
Channels
LLC
Core operations
NIC packet operations
NIC descriptor operations
1
rxd
txd
packet
2
3
4
5
6
8
7
9
10
11
12
13
NICs
No-to-Minimal memory
bandwidth per packet.
(4a) … let’s make it Simple Again!
AND =>
Vector Packet Processing
software worker thread
Core writes Rx descriptor in preparation for receiving a packet.
NIC reads Rx descriptor to get ctrl flags and buffer address.
NIC writes the packet.
NIC writes Rx descriptor.
Core reads Rx descriptor (polling or irq or coalesced irq).
Core reads packet header to determine action.
Core performs action on packet header.
Core writes packet header (MAC swap, TTL, tunnel, foobar..)
Core reads Tx descriptor.
Core writes Tx descriptor and writes Tx tail pointer.
NIC reads Tx descriptor.
NIC reads the packet.
NIC writes Tx descriptor.

## Slide 21: Aside [4/4]: Computer Evolution For Packet Processing … and use FD.io VPP to make them fast for packets.
An Arithmetic Logic Unit (ALU)
(1) It started simple …
(3) Then it got much faster …
A modern two CPU socket server
A simple generic purpose computer
(2) Became universal and faster …
A
C
D
A
B
PCIe
CPU Cores
CPU Socket
Memory Controller
DDR SDRAM
Memory
Channels
LLC
Core operations
NIC packet operations
NIC descriptor operations
1
rxd
txd
packet
2
3
4
5
6
8
7
9
10
11
12
13
NICs
No-to-Minimal memory
bandwidth per packet.
(4a) … let’s make it Simple Again!
AND =>
Vector Packet Processing
software worker thread
Core writes Rx descriptor in preparation for receiving a packet.
NIC reads Rx descriptor to get ctrl flags and buffer address.
NIC writes the packet.
NIC writes Rx descriptor.
Core reads Rx descriptor (polling or irq or coalesced irq).
Core reads packet header to determine action.
Core performs action on packet header.
Core writes packet header (MAC swap, TTL, tunnel, foobar..)
Core reads Tx descriptor.
Core writes Tx descriptor and writes Tx tail pointer.
NIC reads Tx descriptor.
NIC reads the packet.
NIC writes Tx descriptor.
Steps 1-to-13 in a Nutshell:
VPP software worker threads run on CPU cores.
Use local caching with No-to-Minimal memory bandwidth per packet.
Get speed with predictive prefetching and smart algos.
And make CPU cache hierarchy always “Hot” => Packet processing at rate.
Making VPP simply tick the A-B-C-D server optimization points !

## Slide 22
Let’s look at performance data at scale
Packet throughput for
  IPv4 routing,
  IPv6 routing,
  L2 switching,
  L2 switching with VXLAN tunnelling.

## Slide 23: VPP Universal Fast Dataplane: Performance at Scale [1/2] Per CPU core throughput with linear multi-thread(-core) scaling
Hardware: Cisco UCS C240 M4
Intel® C610 series chipset
2 x Intel® Xeon® Processor E5-2698 v3 (16 cores, 2.3GHz, 40MB Cache)
2133 MHz, 256 GB Total
6 x 2p40GE Intel XL710=12x40GE
Topology:
Phy-VS-Phy
Software
Linux: Ubuntu 16.04.1 LTS Kernel: ver. 4.4.0-45-generic
FD.io VPP: VPP v17.01-5~ge234726 (DPDK 16.11)
Resources
1 physical CPU core per 40GE port
Other CPU cores available for other services and other work
20 physical CPU cores available in 12x40GE seupt
Lots of Headroom for much more throughput and features
IPv4 Routing
IPv6 Routing

## Slide 24: VPP Universal Fast Dataplane: Performance at Scale [2/2] Per CPU core throughput with linear multi-thread(-core) scaling
Hardware: Cisco UCS C240 M4
Intel® C610 series chipset
2 x Intel® Xeon® Processor E5-2698 v3 (16 cores, 2.3GHz, 40MB Cache)
2133 MHz, 256 GB Total
6 x 2p40GE Intel XL710=12x40GE
Topology:
Phy-VS-Phy
Software
Linux: Ubuntu 16.04.1 LTS Kernel: ver. 4.4.0-45-generic
FD.io VPP: VPP v17.01-5~ge234726 (DPDK 16.11)
Resources
1 physical CPU core per 40GE port
Other CPU cores available for other services and other work
20 physical CPU cores available in 12x40GE seupt
Lots of Headroom for much more throughput and features
L2 Switching
L2 Switching with VXLAN Tunneling

## Slide 25: Native Cloud Network Services – Sample Use Cases Based on supported FD.io VPP functionality
Substantial Performance and Efficiency Gains vs. Alternatives
SD-WAN and DC Overlays
IPVPN, L2VPN, IPSec/SSL encryption
Scaleable L2 switching and IPv4/IPv6 routing vNFs
Million Routes Scale and Service Features
Performance at Max Network I/O of Intel® Xeon® Server
SECURE PRIVATE NETWORKING
CG-NAT and Softwires
Carrier Grade NAT for Subscriber IPv4 Addressing Control
Softwires for Subscriber IPv4 over IPv6 Transport
Million of Subscribers and Service Features
Performance at Max Network I/O of Intel® Xeon® Server
SUBSCRIBER MANAGEMENT
SECURE PRIVATE
NETWORKING
SUBSCRIBER
MANAGEMENT
PRODUCTION
GRADE

## Slide 26: SD-WAN – with FD.io Universal Fast Data Plane
SERVICE VIEW
Sites 1..N
Enterprise1
Enterprise2
Enterprise3
Software Defined – WAN
Sites 1..N
Sites 1..N
IPVPN and L2VPN Overlays*, IPSec/SSL Crypto
IPVPN and L2VPN Overlays*, IPSec/SSL Crypto
IPVPN and L2VPN Overlays*, IPSec/SSL Crypto
Site 1
Site N
Enterprise1
Enterprise2
Enterprise3
Site 1
Site N
Site 1
Site N
IP Network
Private or Public
Data Center1
Data Center2
SD-WAN Hub
SD-WAN Hub
Server
CPUs
Net I/O
Crypto I/O
Server
CPUs
Net I/O
Crypto I/O
Server
CPUs
Net I/O
Crypto I/O
Server
CPUs
Net I/O
Crypto I/O
FD.io Fast Network Data Plane
HQ-to-HQ
Branch-to-HQ
Branch-to-Branch
Secure and Fast Private Networking
HQ-to-PrivateCloud
Branch-to-PrivateCloud
HomeUser-to-PrivateCloud
FD.io SD-WAN Service Properties:
Native cloud network data plane
Fast and Efficient
Over 20GE of net I/O per CPU core
vRouter vNF
vNF Services
vRouter vNF
vRouter vNF
vNF Services
vNF Services
*Overlay encapsulations: VXLAN, LISP GPE
PHYSICAL VIEW

## Slide 27: SD-WAN – with FD.io Universal Fast Data Plane
FD.io Fast Network Data Plane
SERVICE VIEW
Sites 1..N
Enterprise1
Enterprise2
Enterprise3
Software Defined – WAN
Sites 1..N
Sites 1..N
IPVPN and L2VPN Overlays*, IPSec/SSL Crypto
IPVPN and L2VPN Overlays*, IPSec/SSL Crypto
IPVPN and L2VPN Overlays*, IPSec/SSL Crypto
vRouter vNF
vNF Services
vRouter vNF
vRouter vNF
vNF Services
vNF Services
PHYSICAL VIEW
10GE
1-4
IPv4/v6
Sites 1..N
IPv4/v6
Sites 1..N
IPv4/v6
Sites 1..N
25GE
5-8
100GE
9
2CPU
Network I/O 480 Gbps
Crypto I/O 100 Gbps
10GE
25GE
100GE
4x
4x
1x
100GE
2x
25GE
2x
Host-1 – Server-SKL
2CPU
Network I/O 480 Gbps
Crypto I/O 100 Gbps
100GE
x2
25GE
x2
Host-2 – Server-SKL
10GE
1-4
IPv4/v6
Services
IPv4/v6
Services
IPv4/v6
Services
25GE
5-8
100GE
9
10GE
25GE
100GE
4x
4x
1x
IP Network
Private or Public
IPVPN Service Traffic Simulator
Traffic Generator
*Overlay encapsulations: VXLAN, LISP GPE

## Slide 28: SD-WAN – with FD.io Universal Fast Data Plane
FD.io Fast Network Data Plane
Fast SD-WAN Services – with FD.io Fast Network Data Plane
SERVICE VIEW
Sites 1..N
Enterprise1
Enterprise2
Enterprise3
Software Defined – WAN
Sites 1..N
Sites 1..N
IPVPN and L2VPN Overlays*, IPSec/SSL Crypto
IPVPN and L2VPN Overlays*, IPSec/SSL Crypto
IPVPN and L2VPN Overlays*, IPSec/SSL Crypto
vRouter vNF
vNF Services
vRouter vNF
vRouter vNF
vNF Services
vNF Services
PHYSICAL VIEW
10GE
1-4
IPv4/v6
Sites 1..N
IPv4/v6
Sites 1..N
IPv4/v6
Sites 1..N
25GE
5-8
100GE
9
2CPU
Network I/O 480 Gbps
Crypto I/O 100 Gbps
10GE
25GE
100GE
4x
4x
1x
100GE
2x
25GE
4x
Host-1 – Server-SKL
2CPU
Network I/O 480 Gbps
Crypto I/O 100 Gbps
100GE
x2
25GE
x4
Host-2 – Server-SKL
10GE
1-4
IPv4/v6
Services
IPv4/v6
Services
IPv4/v6
Services
25GE
5-8
100GE
9
10GE
25GE
100GE
4x
4x
1x
IP Network
Private or Public
IPVPN Service Traffic Simulator
Traffic Generator
*Overlay encapsulations: VXLAN, LISP GPE
28
Breaking the Barrier of Software Defined Network Services 1 Terabit Services on a Single Intel® Xeon® Server !!!

## Slide 29: Scaling Up The Packet Throughput with FD.io VPP Can we squeeze more from a single 2RU server ?
VPP enables linear multi-thread(-core) scaling
up to the packet I/O limit per CPU => on a path to one terabit software router (1TFR).
29
Breaking the Barrier of Software Defined Network Services 1 Terabit Services on a Single Intel® Xeon® Server !!!
Today’s Intel® XEON® CPUs (E5 v3/v4):
  Per socket have 40 lanes of PCIe Gen3
  2x 160Gbps of packet I/O per socket
Tomorrow’s Intel® XEON® CPUs:
  Per socket support More lanes of PCIe Gen3
  2x 280Gbps of packet I/O per socket

## Slide 30: VPP Architecture: Programmability
Linux Hosts
Architecture
Example: Honeycomb
Agent
VPP
Shared Memory
…
…
Request Queue
Response Queue
Request Message
900k request/s
Async Response Message
Linux Hosts
Honeycomb
Agent
VPP
Shared Memory
…
…
Request Queue
Response Queue
Request Message
Async Response Message
Netconf/Restconf/Yang
Control Plane Protocol
Can use C/Java/Python/or Lua
Language bindings

## Slide 31: Universal Fast Dataplane: Features
Tunnels/Encaps
  GRE/VXLAN/VXLAN-GPE/LISP-GPE
  NSH, L2TPv3, SRv6
  IPSec Tunnel, Transport
  Including HW offload if present
Interfaces
  DPDK/Netmap/AF_Packet/TunTap
  Vhost-user - multi-queue, reconnect,
  Jumbo Frame Support
MPLS
  MPLS over Ethernet/GRE
  Deep label stacks supported
Segment Routing
  SR MPLS/IPv6
  Including Multicast
Inband iOAM
  Telemetry export infra (raw IPFIX)
  iOAM for VXLAN-GPE (NGENA)
  SRv6 and iOAM co-existence
  iOAM proxy mode / caching
  iOAM probe and responder
LISP
  LISP xTR/RTR
  L2 Overlays over LISP and GRE encaps
  Multitenancy
  Multihome
  Map/Resolver Failover
  Source/Dest control plane support
  Map-Register/Map-Notify/RLOC-probing
  IPSec transport mode
Language Bindings
  C/Java/Python/Lua
Hardware Platforms
  Pure Userspace - X86,ARM 32/64,Power
  Raspberry Pi
Routing
  IPv4/IPv6
  14+ MPPS, single core
  Hierarchical FIBs
  Multimillion FIB entries
  Source RPF
  Thousands of VRFs
  Controlled cross-VRF lookups
  Multipath – ECMP and Unequal Cost
  IP Multicast
Network Services
  DHCPv4 client/proxy
  DHCPv6 Proxy
  MAP/LW46 – IPv4aas
  CGNAT
  MagLev-like Load Balancer
  Identifier Locator Addressing
  NSH SFC SFF’s & NSH Proxy
  LLDP
  BFD
  QoS Policer 1R2C, 2R3C
  Multiple million Classifiers –
  Arbitrary N-tuple
Switching
  VLAN Support
  Single/ Double tag
  L2 forwd w/EFP/BridgeDomain concepts
  VTR – push/pop/Translate (1:1,1:2, 2:1,2:2)
  Mac Learning – default limit of 50k addr
  Bridging
  Split-horizon group support/EFP Filtering
  Proxy Arp
  Arp termination
  IRB - BVI Support with RouterMac assigmt
  Flooding
  Input ACLs
  Interface cross-connect
  L2 GRE over IPSec tunnels
Monitoring
  Simple Port Analyzer (SPAN)
  IP Flow Export (IPFIX)
  Counters for everything
  Lawful Intercept
Security
  Mandatory Input Checks:
  TTL expiration
  header checksum
  L2 length < IP length
  ARP resolution/snooping
  ARP proxy
  NAT
  Ingress Port Range Filtering
  Per interface whitelists
  Policy/Security Groups/GBP (Classifier)

## Slide 32: Rapid Release Cadence – ~3 months
16-02
Fd.io launch
16-06
Release- VPP
16-09
Release:
VPP, Honeycomb, NSH_SFC, ONE
17-01
Release:
VPP, Honeycomb, NSH_SFC, ONE
16-06 New Features
  Enhanced Switching & Routing
  IPv6 SR multicast support
  LISP xTR support
  VXLAN over IPv6 underlay
  per interface whitelists
  shared adjacencies in FIB
  Improves interface support
  vhost-user – jumbo frames
  Netmap interface support
  AF_Packet interface support
  Improved programmability
  Python API bindings
  Enhanced JVPP Java API bindings
  Enhanced debugging cli
  Hardware and Software Support
  Support for ARM 32 targets
  Support for Raspberry Pi
  Support for DPDK 16.04
16-09 New Features
  Enhanced LISP support for
  L2 overlays
  Multitenancy
  Multihoming
  Re-encapsulating Tunnel Routers
  (RTR) support
  Map-Resolver failover algorithm
  New plugins for
  SNAT
  MagLev-like Load
  Identifier Locator Addressing
  NSH SFC SFF’s & NSH Proxy
  Port range ingress filtering
  Dynamically ordered subgraphs
17-01 New Features
  Hierarchical FIB
  Performance Improvements
  DPDK input and output nodes
  L2 Path
  IPv4 lookup node
  IPSEC
  Softwand HWCrypto Support
  HQoS support
  Simple Port Analyzer (SPAN)
  BFD
  IPFIX Improvements
  L2 GRE over IPSec tunnels
  LLDP
  LISP Enhancements
  Source/Dest control plane
  L2 over LISP and GRE
  Map-Register/Map-Notify
  RLOC-probing
  ACL
  Flow Per Packet
  SNAT – Multithread, Flow Export
  LUA API Bindings

## Slide 33: New in 17.04 – Released Apr 19
VPP Userspace Host Stack
  TCP stack
  DHCPv4 relay multi-destination
  DHCPv4 option 82
  DHCPv6 relay multi-destination
  DHPCv6 relay remote-id
  ND Proxy
NAT
  CGN: Configurable port allocation
  CGN: Configurable Address pooling
  CPE: External interface
  DHCP support
  NAT44, NAT64, LW46
Stateful Security Groups
  Routed interface support
  L4 filters with IPv6 Extension Headers
API
  Move to CFFI for Python binding
  Python Packaging improvements
  CLI over API
  Improved C/C++ language binding
Segment Routing v6
  SR policies with weighted SID lists
  Binding SID
  SR steering policies
  SR LocalSIDs
  Framework to expand local SIDs w/plugins
iOAM
  UDP Pinger w/path fault isolation
  IOAM as type 2 metadata in NSH
  IOAM raw IPFIX collector and analyzer
  Anycast active server selection
IPFIX
  Collect IPv6 information
  Per flow state
Images at: https://nexus.fd.io/
Release notes: https://docs.fd.io/vpp/17.04/release_notes_1704.html

## Slide 34: Continuous Quality, Performance, Usability Built into the development process – patch by patch
Submit
Automated
Verify
Code Review
Merge
Publish Artifacts
System Functional Testing
252 Tests/Patch
  DHCP – Client and Proxy
  GRE Overlay Tunnels
  L2BD Ethernet Switching
  L2 Cross Connect Ethernet Switching
  LISP Overlay Tunnels
  IPv4-in-IPv6 Softwire Tunnels
  Cop Address Security
  IPSec
  IPv6 Routing – NS/ND, RA, ICMPv6
  uRPF Security
  Tap Interface
  Telemetry – IPFIX and Span
  VRF Routed Forwarding
  iACL Security – Ingress – IPv6/IPv6/Mac
  IPv4 Routing
  QoS Policer Metering
  VLAN Tag Translation
  VXLAN Overlay Tunnels
Performance Testing
144 Tests/Patch, 841 Tests
  L2 Cross Connect
  L2 Bridging
  IPv4 Routing
  IPv6 Routing
  IPv4 Scale – 20k,200k,2M FIB Entries
  IPv4 Scale - 20k,200k,2M FIB Entries
  VM with vhost-userr
  PHYS-VPP-VM-VPP-PHYS
  L2 Cross Connect/Bridge
  VXLAN w/L2 Bridge Domain
  IPv4 Routing
  COP – IPv4/IPv6 whiteless
  iACL – ingress IPv4/IPv6 ACLs
  LISP – IPv4-o-IPv6/IPv6-o-IPv4
  VXLAN
  QoS Policer
  L2 Cross over
  L2 Bridging
Usability
  Merge-by-merge:
  apt installable deb packaging
  yum installable rpm packaging
  autogenerated code documentation
  autogenerated cli documentation
  Per release:
  autogenerated testing reports
  report perf improvements
  Puppet modules
  Training/Tutorial videos
  Hands-on-usecase documentation
Build/Unit Testing
120 Tests/Patch
  Build binary packaging for
  Ubuntu 14.04
  Ubuntu 16.04
  Centos 7
  Automated Style Checking
  Unit test :
  IPFIX
  BFD
  Classifier
  DHCP
  FIB
  GRE
  IPv4
  IPv4 IRB
  IPv4 multi-VRF
  IPv6
  IP Multicast
  L2 FIB
  L2 Bridge Domain
  MPLS
  SNAT
  SPAN
  VXLAN
Run on real hardware in fd.io Performance Lab
Merge-by-merge packaging feeds
Downstream consumer CI pipelines

## Slide 35: Universal Fast Dataplane: Infrastructure
Server
Kernel/Hypervisor
FD.io
Bare Metal
Server
Kernel/Hypervisor
FD.io
VM
VM
VM
Cloud/NFVi
Server
Kernel
FD.io
Con
Con
Con
Container Infra

## Slide 36: Universal Fast Dataplane: xNFs
Server
Kernel/Hypervisor
VM
FD.io based vNFs
VM
FD.io
FD.io
FD.io
Server
Kernel/Hypervisor
Con
FD.io based cNFs
Con
FD.io
FD.io
FD.io

## Slide 37: Universal Fast Dataplane: Embedded
Device
Kernel/Hypervisor
Embedded Device
FD.io
Hw Accel
Server
Kernel/Hypervisor
SmartNic
SmartNic
FD.io
Hw Accel

## Slide 38: Universal Fast Dataplane: CPE Example
Device
Kernel/Hypervisor
Physical CPE
FD.io
Hw Accel
Server
Kernel/Hypervisor
VM
vCPE in a VM
VM
FD.io
FD.io
FD.io
Server
Kernel/Hypervisor
Con
vCPE in a Container
Con
FD.io
FD.io
FD.io

## Slide 39: A Fast Data Network Platform For Native Cloud Network Services
39
Superior Performance
Most Efficient on the Planet
Flexible and Extensible
Open Source
Cloud Native
Breaking the Barrier of Software Defined Network Services 1 Terabit Services on a Single Intel® Xeon® Server !!!
The most efficient software packet
Processing on the planet
FD.io on x86 servers outperforms specialized packet processing HW
Foundation for cloud native network services
Software programmable, extendable and flexible
Open source collaborative project in Linux Foundation
EFFICIENCY
PERFORMANCE
SOFTWARE DEFINED NETWORKING
CLOUD NETWORK SERVICES
LINUX FOUNDATION

## Slide 40: Opportunities to Contribute
We invite you to Participate in fd.io
Get the Code, Build the Code, Run the Code
Try the vpp user demo
Install vpp from binary packages (yum/apt)
Install Honeycomb from binary packages
Read/Watch the Tutorials
Join the Mailing Lists
Join the IRC Channels
Explore the wiki
Join fd.io as a member
Firewall
IDS
DPI
Flow and user telemetry
Hardware Accelerators
Container Integration
Integration with OpenCache
Control plane – support your favorite SDN Protocol Agent
Test tools
Cloud Foundry Integration
Packaging
Testing
https://wiki.fd.io/view/Main_Page
https://wiki.fd.io/view/VPP
https://wiki.fd.io/view/CSIT
FD.io project wiki pages:
FD.io git repos:
https://git.fd.io/
https://git.fd.io/vpp/
https://git.fd.io/csit/

## Slide 41
Q&A

## Slide 42
Thank You !