## Slide 1: NSH_SFC 17.01 Performance Report FD.io NSH_SFC and CSIT Team

## Slide 2: Background
Measure NSH_SFC 17.01 performance with VPP 17.01 for different SFC ingredients
  Service Function Forwarder
  NSH Proxy
  NSH Classifier
IXIA based PacketGen to be replaced by TREX in the automation test by CSIT team
  Baseline performance will be used to analyze potential negative performance impact introduced by software PacketGen or future patches
As baseline for apple-to-apple performance comparison with DPDK OVS, once NSH patches to OVS are upstreamed
Focus on single core performance currently, scale-up (assign more cores) testing will be covered in the future

## Slide 3: Test Configuration
10G Niantic
IXIA
Port B
2.2GHz
Port 1
Core 2
Core 3
Core 0
Core 1
DIMM 0
DIMM 1
DIMM 2
DIMM 3
IXIA Traffic Configuration
  NSH Classifier: Raw packet in different size
  SFF: VxLAN-GPE + NSH + Raw Packet
  NSH Proxy Inbound: VxLAN-GPE + NSH + Raw Packet
  NSH Proxy Outbound: VxLAN+ Raw Packet
L4 packet
inner
IP header
Inner MAC header
UDP header
Outer
IP header
Outer MAC
header
NSH
VxLAN-GPE
Header
L4 packet
inner
IP header
Inner MAC header
UDP header
Outer
IP header
Outer MAC
header
NSH
VxLAN-GPE
Header
L4 packet
inner
IP header
Inner MAC header
UDP header
Outer
IP header
Outer MAC
header
VxLAN
L4 packet
inner
IP header
Inner MAC header
Port A
Port 0

## Slide 4: BIOS Configuration
Enhanced Intel Speedstep | Disabled
Turbo Boost | Disabled
Processor C3 | Disabled
Processor C6 | Disabled
Hyper-Threading | Disabled
Intel VT-d | Enabled
CPU Power and Performance Policy | Performance
Memory Freq. | 2133 MHz
Total Memory Size | 64 GB
Memory RAS and Performance Configuration -> NUMA Optimized | ENABLED
QPI B/W | 9.6 GT/s
MLC Streamer | ENABLED
MLC Spatial Prefetcher | ENABLED
DCU Data Prefetcher | ENABLED
DCU Instruction Prefetcher | ENABLED
Direct Cache Access (DCA) | ENABLED
Software Configuration
OS | Ubuntu 14.04.1
Kernel version | 4.2.0-27-generic
VPP | vpp v1.0.0-263~gd6f5b96
DPDK | DPDK 16.11
NSH_SFC | 17.01 RC2
Device Under Test
Hardware Configuration
CPU | Intel(R) Xeon(R) CPU E5-2699 v4 @ 2.20GHz
DIMM | 2133 MHz, 64GB Total
NIC | 2x 82599ES 10-Gigabit SFI/SFP+ Network Connection
PacketGen | Ixia* 10 Gigabit Ethernet Traffic Generator (16 ports)

## Slide 5
NSH_SFC Performance in 17.01 Release
Chart: NSH Classifier Throughput For Different Packet Size (1C1T)
| 72 | 84 | 128 | 256
 | 5120 | 5520 | 7088 | 9432
Chart: NSH_SFC Throughput For 128B Packet (1C1T)
| NSH Classifier | NSH Proxy (Inbound) | SFF
 | 7088 | 4250 | 4500
NSH_SFC 17.01 performance drops from 5.8Mpps to 4.25Mpps for NSH Proxy
2 to 3 dedicated cores could achieve 10G line rate for small packet for all NSH_SFC use cases

## Slide 6: Backup

## Slide 7
NSH Proxy Performance in 16.09 Release - As Reference Data
Chart: nsh-proxy uni-direction performance(nsh-decap->vxlan-encap vs. vxlan-decap->nsh-encap)
| 64 | 80 | 114 | 128 | 178 | 306 | 562 | 818 | 1074 | 1330 | 1518
vxlan-gpe-nsh-decap->vxlan-encap | 5.83 | 5.83 | 3.83 | 2.15 | 1.49 | 1.14 | 0.93 | 0.81
vxlan-decap->vxlan-gpe-nsh-encap | 6.01 | 6.01 | 3.83 | 2.15 | 1.49 | 1.14 | 0.93 | 0.81
nsh-proxy-decap for 128B |  | 
CPP | Time (ns) | Mpps
394.9 | 171.7 | 5.83