## Slide 1: Improve Performance of Kube-proxy and GTP-U using VPP
Hongjun Ni (hongjun.ni@intel.com)
Danny Zhou (danny.zhou@intel.com)
Johnson Li (johnson.li@intel.com)
Network Platform Group, DCG, Intel
Acknowledgement: Jianfeng Tan

## Slide 2: Agenda
  Enabling high performance kube-proxy
  Six ways to improve performance of GTP-U
  Key takeaway

## Slide 3
Introducing Vector Packet Processor
Packet processing development platform
Runs on commodity CPUs and leverages DPDK
Runs as a Linux user-space application

## Slide 4
VPP Graph Node and Plugin Framework
dpdk-input
ethernet-input
mpls-ethernet-input
ip6-input
ip4-input
arp-input
ip4-lookup
…
Packet Vector
ip4-udp-lookup
ip4-local
ethernet-output
ip4-rewrite
Kube-proxy
GTP-U
ip4-load-balance

## Slide 5: Enabling high performance kube-proxy
  Introducing kube-proxy
  Current pain point
  Proposed kube-proxy solution
  Kube-proxy dataplane
  GoVPP
  Performance

## Slide 6
Introducing kube-proxy
Watches addition and removal of Service and Endpoints.
Installs iptables rules
Captures traffic and select Pod
Redirects traffic
Reference: https://kubernetes.io/docs/concepts/services-networking/service/

## Slide 7: Current Pain Point
  Supports userspace and iptables
  Uses kernel iptables NAT
  Performance degrades when service/endpoint pairs increase

## Slide 8
Proposed kube-proxy solution
CP: Control Plane
DP: Data Plane

## Slide 9
Kube-proxy Data Plane
Distribute traffic evenly
Per flow stick to a Pod
Three service types:
(1). ClusterIP: Port
(2). NodeIP: NodePort
(3). External LoadBalancer

## Slide 10
Kube-proxy Data Plane Internals
VIP->Pod Table
kp4-nodeport
Supported Graph Nodes
kp4-nat4
Stores VIP->Pod session
udp-lookup
ip4
-lookup
input
Other
Graph nodes
input
Other
Graph nodes
ip6
-lookup
ip-lookup
kp4-nat6
kp6-nat4
kp6-nat6
kp6-nodeport

## Slide 11
Kube-proxy: External LoadBalancer

## Slide 12
GoVPP
Golang toolset for VPP management
VPP binary API (JSON)  Go Structure
Handle 250,000 binary API requests per second
Reference: https://wiki.fd.io/images/f/fa/GoVPP-intro.pdf

## Slide 13
Performance
Chart: Kube-proxy Throughput For 64-Byte Packet
| One-loop | Dual-loop w/o Prefetching | Quad-loop w/o Prefetching | Quad-loop with Prefetching
9.83 6.62 | 9.83 | 6.62
Test Case | Input packet size (bytes) | Output packet size (bytes)
Load balance + DNAT + Routing | 64 | 64
Linux iptables perf:
< 400 kpps
Scaling
Reference: https://people.netfilter.org/kadlec/nftest.pdf

## Slide 14: Six Ways to Improve Performance of GTP-U
  Cache table lookup result
  Bypass second ip-input
  Bypass first route lookup
  Dual-loop and Quad-loop
  Packet prefetching
  Bypass second route lookup

## Slide 15
GTP-U Plugin Internals
L4 header
Inner
IP header
UDP header
Outer
IP header
Outer MAC
header
GTP-U
header
Payload
Typical GTP-U packet processed by VPP and GTP-U plugin
GTP-U Plugin
GTP-U Plugin
GTP-U tunnel
gtpu-bypass
Supported Graph Nodes
gtpu-encap
gtpu-input
Stores PDP context
udp-lookup
IP4
-input
input
Other
Graph nodes
input
Other
Graph nodes
IP6
-input
ip-lookup

## Slide 16: BIOS Configuration
Enhanced Intel Speedstep | Enabled
Turbo Boost | Enabled
Processor C3 | Disabled
Processor C6 | Disabled
Hyper-Threading | Disabled
Intel VT-d | Enabled
CPU Power and Performance Policy | Performance
Memory Freq. | 2133 MHz
Total Memory Size | 64 GB
Memory RAS and Performance Configuration -> NUMA Optimized | ENABLED
QPI B/W | 9.6 GT/s
MLC Streamer | ENABLED
MLC Spatial Prefetcher | ENABLED
DCU Data Prefetcher | ENABLED
DCU Instruction Prefetcher | ENABLED
Direct Cache Access (DCA) | ENABLED
Software Configuration
OS | Ubuntu 16.04.2 LTS
Kernel | Linux version 4.4.0-62-generic
DPDK | 17.08
VPP | 17.10-rc0
GTP-U | 17.10-rc0
Device Under Test for Performance
Hardware Configuration
CPU | Intel(R) Xeon(R) CPU E5-2699 v3 @ 2.30GHz
DIMM | 2133 MHz, 64GB Total
NIC | 2x 82599ES 10-Gigabit SFI/SFP+ Network Connection
PacketGen | Ixia* 10 Gigabit Ethernet Traffic Generator
DUT
(VPP + GTP-U)
Traffic Gen
(Trex)
Port A
Port B
Port A
Port B
Core 0
Legend
Flow A
Flow B
Network Topology

## Slide 17: Cache table lookup result

## Slide 18: Bypass second ip-input
Pros:
Boost performance
Cons :
Security issue
dpdk-input
ethernet-input
ip6-input
ip4-input
arp-input
ip4-lookup
…
Packet Vector
ip4-udp-lookup
ip4-local
gtpu-decap
ethernet-output
ip4-rewrite
ip4-load-balance
ip4-lookup
ip4-input

## Slide 19: Bypass first route lookup
gtpu packet:
accelerate decap processing
none-gtpu packet:
an overhead with about
13 clocks per packet
dpdk-input
ethernet-input
ip6-input
ip4-input
arp-input
ip4-lookup
…
Packet Vector
ip4-udp-lookup
ip4-local
gtpu-bypss
gtpu packet
none-gtpu
packet
ethernet-output
ip4-rewrite
ip4-load-balance
gtpu-decap
ip4-lookup
ip4-input

## Slide 20
GTPU-Decap Performance and Analysis
Test Case | Input packet size (bytes) | Output packet size (bytes)
Transport IP Routing + GTPU-Decap + Inner IP Routing | 98 | 64
Chart: GTPU-Decap Throughput For 64-Byte Packet
| One-loop | Dual-loop w/o Prefetching | Quad-loop w/o Prefetching | Quad-loop with Prefetching
6.84 7.29 8.32 10.4 | 6.84 | 7.29 | 8.32 | 10.4

## Slide 21: Dual-loop and Quad-loop, Packet Prefetching
Reduce read latency
Process packets in parallel

## Slide 22: Bypass second route lookup
dpdk-input
ethernet-input
ip6-input
ip4-input
arp-input
ip4-lookup
…
Packet Vector
ip4-rewrite
gtpu-encap
ethernet-output
ip4-rewrite
ip4-load-balance
ip4-lookup

## Slide 23
GTPU-Encap Performance and Analysis
Test Case | Input packet size (bytes) | Output packet size (bytes)
Inner IP Routing + GTPU-Encap + Transport Routing | 64 | 114
Chart: GTPU-Encap Throughput For 64-Byte Packet
| One-loop | Dual-loop w/o Prefetching | Quad-loop w/o Prefetching | Quad-loop with Prefetching
7.76 7.85 8.13 8.26 8.48 | 7.76 | 7.85 | 8.13 | 8.26 | 8.48

## Slide 24: Key Takeaway
  Easy-to-use and flexible VPP plugin framework
  Kube-proxy plugin to boost DP’s performance in Cloud environment
  Combination of a set of ways to optimize data plane performance
  Better platform for developing open source dataplane ingredients

## Slide 25: Q&A