## Slide 1
VPP overview
Shwetha Bhandari
Developer@Cisco

## Slide 2: Scalar Packet Processing
A fancy name for processing one packet at a time
Traditional, straightforward implementation scheme
Interrupt, a calls b calls c … return return return
Issues:
        thrashing the I-cache (when code path length exceeds the primary I-cache size)
                Dependent read latency (packet headers, forwarding tables, stack, other data structures)
                Each packet incurs an identical set of I-cache and D-Cache misses

## Slide 3: Packet Processing Budget
14 Mpps on 3.5 GHz CPU = 250 cycles per packet

## Slide 4: Memory Read/Write latency

## Slide 5
Introducing VPP: the vector packet processor

## Slide 6: Introducing VPP
Accelerating the dataplane since 2002
Fast, Scalable and consistent
  14+ Mpps per core
  Tested to 1TB
  Scalable FIB: supporting millions of entries
  0 packet drops, ~15µs latency
Optimized
  DPDK for fast I/O
  ISA: SSE, AVX, AVX2, NEON ..
  IPC: Batching, no mode switching, no context switches, non-blocking
  Multi-core: Cache and memory efficient
Network I/O
Packet Processing: VPP
Management Agent
Netconf/Yang
REST
...

## Slide 7: Introducing VPP
Extensible and Flexible modular design
Implement as a directed graph of nodes
Extensible with plugins, plugins are equal citizens.
Configurable via CP and CLI
Developer friendly
Deep introspection with counters and tracing facilities.
Runtime counters with IPC and errors information.
Pipeline tracing facilities, life-of-a-packet.
Developed using standard toolchains.
Network I/O
Packet Processing: VPP
Management Agent
Netconf/Yang
REST
...

## Slide 8: Introducing VPP
Fully featured
  L2: VLan, Q-in-Q, Bridge Domains, LLDP ...
  L3: IPv4, GRE, VXLAN, DHCP, IPSEC …
  L3: IPv6, Discovery, Segment Routing …
  CP: CLI, IKEv2 …
Integrated
  Language bindings
  Open Stack/ODL (Netconf/Yang)
  Kubernetes/Flanel (Python API)
  OSV Packaging
Network I/O
Packet Processing: VPP
Management Agent
Netconf/Yang
REST
...
Notes: https://docs.fd.io/vpp/17.04/release_notes_1704.html

## Slide 9: VPP in the Overall Stack
Hardware
Application Layer / App Server
VM/VIM Management Systems
Network Controller
Operating Systems
Data Plane Services
Orchestration
Network IO
VPP
Packet Processing

## Slide 10
VPP: Dipping into internals..

## Slide 11: VPP Graph Scheduler
  Always process as many packets as possible
  As vector size increases, processing cost per packet decreases
  Amortize I-cache misses
  Native support for interrupt and polling modes
  Node types:
    Internal
    Process
    Input

## Slide 12: Sample Graph
dpdk-input
ethernet
-input
ip6-input
mpls-gre
-input
ip4-input-no-checksum
ip4-lookup
ip4-lookup-multicast
ip4-rewrite
-transit
ip4-local
ip4-classify
ip4-input
mpls
-ethernet
-input

## Slide 13: How does it work?
* approx. 173 nodes in default deployment
ethernet-
input
dpdk-input
af-packet-
input
vhost-user-
input
mpls-input
lldp-input
...-no-
checksum
ip4-input
ip6-input
arp-input
cdp-input
l2-input
ip4-lookup
ip4-lookup-
mulitcast
ip4-rewrite-
transit
ip4-load-
balance
ip4-
midchain
mpls-policy-
encap
interface-
output
Packet 0
Packet 1
Packet 2
Packet 3
Packet 4
Packet 5
Packet 6
Packet 7
Packet 8
Packet 9
Packet 10
1
2
Packet processing is decomposed into a directed graph node …
… packets moved through graph nodes in vector …
Instruction Cache
Data Cache
Microprocessor
… graph nodes are optimized to fit inside the instruction cache …
3
4
… packets are pre-fetched, into the data cache …

## Slide 14: How does it work?
dispatch fn()
Get pointer to vector
PREFETCH #3 and #4
PROCESS #1 and #2
ASSUME next_node same as last packet
Update counters, advance buffers
Enqueue the packet to next_node
<as above but single packet>
while packets in vector
while 4 or more packets
while any packets
Microprocessor
ethernet-input
Packet 1
Packet 2
… packets are processed in groups of four, any remaining packets are processed on by one …
4
… instruction cache is warm with the instructions from a single graph node …
5
… data cache is warm with a small number of packets ..
6

## Slide 15: How does it work?
dispatch fn()
Get pointer to vector
PREFETCH #1 and #2
PROCESS #1 and #2
ASSUME next_node same as last packet
Update counters, advance buffers
Enqueue the packet to next_node
<as above but single packet>
while packets in vector
while 4 or more packets
while any packets
Microprocessor
ethernet-input
Packet 1
Packet 2
… prefetch packets #1 and #2 …
7

## Slide 16: How does it work?
dispatch fn()
Get pointer to vector
PREFETCH #3 and #4
PROCESS #1 and #2
ASSUME next_node same as last packet
Update counters, advance buffers
Enqueue the packet to next_node
<as above but single packet>
while packets in vector
while 4 or more packets
while any packets
Microprocessor
ethernet-input
Packet 1
Packet 2
Packet 3
Packet 4
… process packet #3 and #4 … … update counters, enqueue packets to the next node …
8

## Slide 17: Modularity Enabling Flexible Plugins
Plugins can:
  Introduce new graph nodes
  Rearrange packet processing graph
  Can be built independently of VPP source tree
  Can be added at runtime (drop into plugin directory)
  All in user space
Enabling:
  Ability to take advantage of diverse hardware when present
  Support for multiple processor architectures (x86, ARM, PPC)
  Few dependencies on the OS (clib) allowing easier ports to other Oses/Env
ethernet-input
ip6-input
ip4input
mpls-ethernet-input
arp-input
llc-input
…
ip6-lookup
ip6-rewrite-transmit
ip6-local
…
Packet vector
Plug-in to create new nodes
Custom-A
Custom-B
Plug-in to enable new HW input Nodes

## Slide 18
VPP: performance

## Slide 19: VPP Performance at Scale
Phy-VS-Phy
Chart: 
| 12 routes | 1k routes | 100k routes | 500k routes | 1M routes | 2M routes
64B | 108 | 108 | 108 | 108 | 108 | 108
IMIX | 480 | 480 | 480 | 480 | 480 | 480
1518B | 480 | 480 | 480 | 480 | 480 | 480
[Gbps]]
480Gbps zero frame loss
Chart: 
| 12 routes | 1k routes | 100k routes | 500k routes | 1M routes | 2M routes
64B | 210 | 210 | 210 | 210 | 210 | 210
IMIX | 160 | 160 | 160 | 160 | 160 | 160
1518B | 39 | 39 | 39 | 39 | 39 | 39
[Mpps]
200Mpps zero frame loss
Chart: 
| 1k routes | 500k routes | 1M routes | 2M routes | 4M routes | 8M routes
64B | 199.58 | 199.58 | 199.58 | 199.58 | 199.58 | 199.58
IMIX | 342 | 342 | 342 | 342 | 342 | 342
1518B | 462 | 462 | 462 | 462 | 462 | 462
[Gbps]]
IMIX => 342 Gbps,1518B => 462 Gbps
Chart: 
| 1k routes | 500k routes | 1M routes | 2M routes | 4M routes | 8M routes
64B | 297 | 297 | 297 | 297 | 297 | 297
IMIX | 160 | 160 | 160 | 160 | 160 | 160
1518B | 39 | 39 | 39 | 39 | 39 | 39
[Mpps]
64B => 238 Mpps
IPv6, 24 of 72 cores
IPv4+ 2k Whitelist, 36 of 72 cores
Zero-packet-loss Throughput
for 12 port 40GE
Hardware: Cisco UCS C460 M4
Intel® C610 series chipset
4 x Intel® Xeon® Processor E7-8890 v3 (18 cores, 2.5GHz, 45MB Cache)
2133 MHz, 512 GB Total
9 x 2p40GE Intel XL710 18 x 40GE = 720GE !!
Latency
18 x 7.7trillion packets soak test
Average latency: <23 usec
Min Latency: 7…10 usec
Max Latency: 3.5 ms
Headroom
Average vector size ~24-27
Max vector size 255
Headroom for much more throughput/features
NIC/PCI bus is the limit not vpp

## Slide 20
VPP: integrations

## Slide 21: FD.io Integrations
VPP
Control Plane
Data Plane
Honeycomb
Netconf/Yang
VBD app
Lispflowmapping app
LISP Mapping Protocol
SFC
Netconf/yang
Openstack
Neutron
ODL
Plugin
FD.io
Plugin
FD.io ML2 Agent
REST
GBP app
Integration work done at
Felixv2 (Calico Agent)

## Slide 22
Summary
VPP is a fast, scalable and low latency network stack in user space.
VPP is trace-able, debug-able and fully featured layer 2, 3 ,4 implementation.
VPP is easy to integrate with your data-centre environment for both NFV and Cloud use cases.
VPP is always growing, innovating and getting faster.
VPP is a fast growing community of fellow travellers.
ML: vpp-dev@lists.fd.io Wiki: wiki.fd.io/view/VPP
Join us in FD.io & VPP - fellow travellers are always welcome.
Please reuse and contribute!

## Slide 23: Contributors…
Universitat Politècnica de Catalunya (UPC)
Yandex
Qiniu