## Slide 1: Opnfv Summit 2016 (Berlin) DPACC and DPDK solving NFV acceleration
Keith Wiles
June 2016

## Slide 2: Legal Disclaimer
General Disclaimer:
© Copyright 2016 Intel Corporation. All rights reserved. Intel, the Intel logo, Intel Inside, the Intel Inside logo, Intel. Experience What’s Inside are trademarks of Intel. Corporation in the U.S. and/or other countries. *Other names and brands may be claimed as the property of others.
Technology Disclaimer:
Intel technologies’ features and benefits depend on system configuration and may require enabled hardware, software or service activation. Performance varies depending on system configuration. No computer system can be absolutely secure. Check with your system manufacturer or retailer or learn more at [intel.com].
Performance Disclaimers:
Cost reduction scenarios described are intended as examples of how a given Intel- based product, in the specified circumstances and configurations, may affect future costs and provide cost savings. Circumstances will vary. Intel does not guarantee any costs or cost reduction.
Results have been estimated or simulated using internal Intel analysis or architecture simulation or modeling, and provided to you for informational purposes. Any differences in your system hardware, software or configuration may affect your actual performance.

## Slide 3: DPACC and DPDK overview
DPACC design overview with DPDK
Adding VPP from FD.IO to DPDK to enhance NFV
What is TLDK (Transport Layer Development Kit)?
Enhancements to DPDK to support DPACC
Summary

## Slide 4: DPDK
Simple overview

## Slide 5: DPDK Overview
DPDK API
Traffic Gens
Pktgen, T-Rex, Moongen, …
vSwitch
OVS, Lagopus, …
DPDK example apps
AES-NI
VPP
Applications
Event based program models
Threading Models
lthreads, …
Video
Apps
EAL
MALLOC
MBUF
MEMPOOL
RING
TIMER
Core Libraries
KNI
POWER
IVSHMEM
Platform
LPM
Classification
ACL
Classify
e1000
ixgbe
bonding
af_pkt
i40e
fm10k
Packet Access (PMD)
ETHDEV
xenvirt
enic
ring
METER
SCHED
QoS
cxgbe
vmxnet3
virtio
PIPELINE
mlx4
memnic
others
HASH
Utilities
IP Frag
CMDLINE
JOBSTAT
KVARGS
REORDER
TABLE
Legacy DPDK
Future accelerators
Crypto
Programmable Classifier/Parser
HW
3rd Party
GPU/FPGA
3rd Party
SoC PMD
External mempool manager
SoC HW
SOC model
VNF Apps
DPDK Acceleration Enhancements
DPDK Framework
Network Stacks
libUNS, mTCP, SeaStar, libuinet, TLDK, …
Compression
3rd Party
HW/SW
IPSec
DPI Hyperscan
Proxy Apps, …

## Slide 6: DPACC and DPDK design
Focus on one design as a basic high level view:
Software Acceleration Layer is the software to hardware abstraction layer
Software Acceleration Layer makes possible additional services which can be controlled by the orchestration layer
sio-backend + vHost-user is normally in the SAL or SRL layer, but shown here to illustrate vHost in the host.
A SAL in the guest allows for the best performance selection
  Direct access to hardware acceleration via SR-IOV, SOC-specific interface or other pass-though
  Able to do software acceleration in the guest
SRL or HW vSwitch adds VM2VM routing or switching of packets
A SAL in the host gives scalability for non-accelerated VMs and/or native applications
Accelerator
SAL(DPDK)
Crypto
Application
SAL (DPDK)
sio
hio
SRL(OVS)
Crypto
hio
HW vSwitch/Crypto
host
guest
device
sio-backend + vHost-user

## Slide 7: DPACC: Acceleration Layer for Host (Hypervisor)
SAL: Software Acceleration Layer
  Provides an abstraction between SW and HW, plus able to support multiple devices at the same time
sio-backend: backend of paravirtualized drivers
  vHost-user: User space based VirtIO interface
    optional for VM   host access
s-API: APIs for utilizing an AC (APIs from the AC)
g-drivers: General driver for each device type
  Implemented in software or the frontend to the hardware (may be different for different acceleration functions)
hio: Hardware I/O interface
  Non-virtualized, accessed only by host SAL
AC: Software/Hardware Acceleration Core (DPDK)
SRL: Software Routing Layer (OVS)
AML: Acceleration Management Layer
Acceleration Core (DPDK)
hio
sio-backend (optional vHost-user)
s-API
Acceleration Management Layer
Software Acceleration Layer (SAL)
Software Routing Layer (SRL)
Buffer and memory mgnt, rings/queues, ingress/egress scheduling, tasks, pipeline, …
g-drivers
SW-crypto or drivers for HW-crypto
VM 0
VM 2
VM 1
VM 3
VM 4

## Slide 8: VPP with DPDK
Quick overview

## Slide 9: DPDK enhancements for VPP
DPDK contains HW and SW crypto acceleration support
Add HW/SW crypto support to VPP as a new or modified graph node
  Adding DPDK crypto support to VPP can transparently support a range of hardware and software solutions
DPDK contains many accelerators and accelerated software for a number of system architectures, which can be utilized by VPP transparently

## Slide 10: DPACC and VPP design
Software Routing Layer (SRL) can be VPP (Vector Packet Processing) code for a FastPath design of L2/L3 forwarding
VPP can also be in the guess for location fastpath support
VPP can replace the vSwitch at the SRL layer and provide added functionality to the guess or host
Accelerator
SAL(DPDK)
Crypto
Application
SAL (DPDK)
sio
hio
SRL(VPP FastPath)
Crypto
hio
HW vSwitch/Crypto
host
guest
device
sio-backend + vHost-user

## Slide 11: What do we need to do?
Need to address the patches in VPP to DPDK and reduce the amount of changes required for VPP support
Modify DPDK to pick up some of the enhancements in VPP
  One area is around how data is referenced. VPP uses an 32 bit index based on cache line and DPDK uses a pointer, which could be 64 bits
    Adding more space to some critical structures in DPDK, but we have to understand the performance effect to the system
  Move the RTE_MBUF ‘next’ pointer to the first cache line, but this effects performance by having to move other data to the second cache line
Better support of DPDK devices in VPP can improve the performance and portability of VPP across many different architectures

## Slide 12: TLDK (Transport Layer Development Kit)
Quick overview

## Slide 13: TLDK (Transport Layer Development Kit)
TLDK is an open source FD.IO project (https://wiki.fd.io/view/TLDK)
The TLDK project will implement a set of libraries for L4 protocol processing (UDP, TCP etc.) and VPP graph nodes, plugins, etc Using those libraries to implement a host stack
TLDK works on standalone DPDK or integrated into VPP to provide termination support
Committers are:
  Konstantin Ananyev
  Keith Wiles
  Ed Warnicke (IRC nick: edwarnicke)
The first source code push by Konstantin a few weeks ago
  git clone https://gerrit.fd.io/r/tldk
Creating a UDP only design with clean scaling and performance
  About 10 Mpps for 64 byte frames of terminated UDP traffic (Still more tuning needed)

## Slide 14: TLDK (Transport Layer Development Kit) High Level View
I/O Layer
Fastpath Layer
Application Layer
Transport Layer
Physical Layer
Transport Layer:
A set of libraries to handle packets needing support for UDP/TCP/… which is TLDK
Physical Layer:
Ports and other devices like crypto, compression, …
I/O Layer:
DPDK is contained here as it provides the I/O abstraction to the physical layer
Fastpath Layer:
The fastpath layer is today VPP and its graph nodes handling moving packets to application or back to the I/O layer after some type of processing
Application Layer:
The application has a VPP graph node to send/receive packets to/from the application layer
The application and/or fastpath layer uses TLDK library APIs

## Slide 15: TLDK Uses case #1 with DPDK
DPDK
Physical Layer
Application Layer
TLDK:
Handles packet I/O and protocol processing of packets
Application sets up the UDP/TCP protocol contexts and then calls I/O routines in TLDK to start processing packets
Physical Layer:
Ports and other devices like crypto, compression, …
DPDK:
DPDK is contained here as it provides the I/O abstraction to the physical layer
TLDK
Control or
non-TLDK pkts
TLDK pkts

## Slide 16: TLDK Uses case #2 with VPP
VPP
DPDK
Physical Layer
Application Layer
TLDK:
Handles packet I/O and protocol processing of packets
Application sets up the UDP/TCP protocol contexts and then calls I/O routines in TLDK to start processing packets
VPP Fastpath
Using VPP as the first layer for packet processing before packets are sent to the application layer
Physical Layer:
Ports and other devices like crypto, compression, …
DPDK:
DPDK is contained here as it provides the I/O abstraction to the physical layer
TLDK
Control or
non-TLDK pkts
TLDK pkts

## Slide 17: Classification for DPDK
WIP on adding classification support to DPDK, plus unifying the current APIs

## Slide 18: ETHDEV and PMD layering
HW Handlers
Phase II
PMD
PMD
PMD
PMD
ETHDEV
SW Handlers
HW
Supported?
No
Yes
Classifier API
ETHDEV to PMD API requirements:
Reuse existing APIs if possible with little to no change
If a new API replaces and old API, the old API will be deprecated over time or never TBD
Add new APIs only when required
The ETHDEV to PMD layer interface needs to have as little change as possible, but common across all PMDs
Weather Classifier API is on top of ETHDEV as a library or a new DPDK API along side ETHDEV is TBD
P4 is shown here to state that P4 is above DPDK API and possible also above Classifier API TBD
P4
Version 0.4

## Slide 19: VirtIo
Update on Intel’s work on Virtio

## Slide 20: Lookaside VirtIO-crypto
Intel has begun to define the specification for virtIO-crypto processing from the VNF to the host
The specification currently focuses on the definition of symmetric and asymmetric algorithms
    Specification shall be protocol agnostic but will accelerate compute intensive algorithms
    Shall offer asynchronous and synchronous API invocation
Intel shall work with the QEMU mailing list to gain acceptance of the specification
Request flow:
  VNF application makes crypto requests using the g-API
  The SAL translates between the g-API and the virtIO-crypto interface
  The virtIO-crypto front end driver places requests on a Vring
  The BE virtIO driver removes the request from the Vring and calls the accelerator driver to submit the request to the accelerator
Guest
SAL
Acceleration hardware
VNF
Crypto Application
g-API
Host
virtio-crypto
BE driver
VirtIO-crypto FE driver
virtio-crypto interface
Accelerator Host Driver
SAL

## Slide 21: DPDK Enhancements
Current and future enhancements

## Slide 22: Enhancements to DPDK
New features:
External Memory manager support in DPDK 16.11
Future support:
Event based support for DPDK applications (TBD)
New Virtio support for crypto devices
vSwitch using VPP Fastpath, plus we get a lot of extra features
Add FPGA and GPU support to DPDK for more accelerators
Add compression support to DPDK for storage and other needs

## Slide 23: Summary
Adding VPP to DPACC will enhance the overall design with lots of extra protocol support in the fastpath
Reducing the delta between DPDK and VPP to better support FD.io
Adding termination of UDP and TCP support via TLDK to DPDK/VPP will increase native application performance
Enhancing Virtio for more accelerators like Crypto adds better support for NFV applications with better performance