## Slide 1: Performance Considerations for Packet Processing on Intel® Architecture
Patrick Lu, Intel DCG/NPG/ASE
Acknowledgement: Roman Dementiev, John DiGiglio, Andi Kleen, Maciek Konstantynowicz, Sergio Gonzalez Monroy, Shrikant Shah, George Tkachuk, Vish Viswanathan, Jeremy Williamson

## Slide 2: Agenda
Uncore Performance Monitoring with Hardware Counters
  Measure PCIe Bandwidth
  Measure Memory Bandwidth
Core Performance Monitoring
  IPC revisit
  Intel® Processor Trace for Performance Optimization

## Slide 3
Core:
ALU
L1 cache
L2 cache
“un”core:
(everything not core)
LLC cache
Memory controller
IIO controller
QPI controller
and more!
Terminology sync:
Core = execution units (ALU) + L1 cache + L2 caches
Uncore = everything not core

## Slide 4
Traditional performance analysis is core centric
We need new methodologies to analyze I/O centric workloads
Notes: Network oriented workload analysis is very different than Computed oriented workload (like AI)
a lot of IO is involved and CPU + I/O interaction
addition to widely available CPU side tools (perf, Vtune) we need other tools to cover uncore

## Slide 5: Uncore Side Performance Considerations
PCIe bandwidth
Memory bandwidth
QPI bandwidth (Backup)

## Slide 6: Open Sourced Uncore Performance Tool Options
Processor Counter Monitoring (PCM) – in GitHub*
Linux* perf + pmu-tools – in Linux* kernel
real-time display on metrics, bandwidth
user space tools
cross platforms (Linux*, Windows*, Mac OSx*)
stand alone Linux* perf utility + wrapper

## Slide 7
Measure PCIe Bandwidth

## Slide 8: Measure PCIe Bandwidth
Processor Counter Monitoring (PCM): ./pcm-pcie.x -e
Network Rx (ItoM/RFO)
Inbound PCIe write
Network Tx (PCIeRdCur)
MMIO Read (PRd)
MMIO Write (WiL)
Inbound PCIe read
Outbound CPU read
Outbound CPU write
Match workload I/O throughput1
Avoid MMIO Rd
Optimize batch size
1. Results in number of cache lines (64 Bytes)
Avoid DDIO miss
Reduce RFO
Notes: Avoid DDIO miss
balance descriptor sizes (larger the span, more chance to collide cache sets)
Avoid RFO
disable CRC striping

## Slide 9
Measure
Memory Bandwidth

## Slide 10: Measure Memory Bandwidth
Processor Counter Monitoring (PCM): ./pcm-memory.x
Reason with memory traffic:
Wrong NUMA allocation
DDIO Miss
CPU data structure
No memory traffic: Best
Fix it in the code!
Receive packets ASAP, descriptor ring sizes (needs tuning)
May be okay, but check for latency!
Notes: Look for cross numa traffic
Check if DDIO is utilized optimally
Remember memory latency is x times LLC latency

## Slide 11: Uncore Performance Takeaway
Calibrate I/O bandwidth with expected performance
Check for unexpected cross-NUMA traffic
Avoid MMIO Read
Batch MMIO Write
Optimize Software to make use of DDIO
Easy
Advance

## Slide 12: Core Side Performance Consideration
IPC
Intel® Processor Trace

## Slide 13: Which Workload Has Best Performance?
VPP A
2.63
VPP B
2.12
IPC
Notes: We need visibility into performance, here is an example
code efficiency
compiler efficiency
IPC really very bad, TMAM L1
un-optimzed OpenSSL library

## Slide 14: Workload Performance Reveal: A: Un-optimized VPP IPSec, B: Intel® AES-NI Accelerated VPP IPSec
VPP A
2.63
15733
VPP B
2.12
1865
5982
880
IPC
Instructions/packet
Cycles/packet
6x reduction in cycles
8x reduction in instructions
Notes: We need visibility into performance, here is an example
code efficiency
compiler efficiency
IPC really very bad, TMAM L1
un-optimzed OpenSSL library

## Slide 15: Performance is Determined by Two Factors Instruction per Cycle (IPC) Mystery
Instructions/pkt
Cycles/pkt
IPC
Unless IPC is really poor, instructions/packet or cycles/packet is more realistic Core metrics.
÷
=
Measured | Instructions / sec (M) | 5229
Measured | Cycles / sec (M) | 2103
Derived | IPC | 2.49
Measured | CPU freq. (MHz) | 2100
Measured | Packets / sec (M) | 9.7
Derived | Instructions / packet | 539
Derived | Cycles / packet | 217
Notes: Understand composition of 539 instructions/pkt
Are we using optimal functions?
Can we avoid heavy generic processing?
Can we group the processing by type of works?

## Slide 16: Intel® Processor Trace (Intel® PT) Components
Ring0 Agent
(OS, VMM, BIOS, Driver, …)
Intel PT packet log
(per logical processor)
Intel PT-enabled Tools
Runtime data, including:
Map linear-address to image files
Map CR3 value to application
Log module load/unload and JIT info
Binary
Image Files
Intel® Processor Trace (Intel® PT) packet log, binaries, and software runtime data are used to reconstruct the precise execution flow
Intel
CPU 0..n
Intel PT HW
Configure &
enable Intel PT
Intel PT Software
Decoder
Intel® Processor Trace can reveal exact execution path

## Slide 17: Linux* perf and Intel® Processor Trace
Provides basic framework for trace collection, mining, and visualization
  Kernel driver in 4.1, user tools in 4.2/4.3
Supports full trace and “snapshot” modes
Display tools support histograms, event lists, flame graphs, etc
Linux perf can capture finest detail with Intel® PT.
Post processing is required to reduce trace data.

## Slide 18: Life Cycle of a Packet using Intel® PT
Chart: VPP L2 bridge domain
| i40e_recv_scattered_pkts_vec | i40e_recv_scattered_pkts_vec | i40e_recv_scattered_pkts_vec | i40e_recv_scattered_pkts_vec | i40e_recv_scattered_pkts_vec | i40e_recv_scattered_pkts_vec | i40e_recv_scattered_pkts_vec | i40e_recv_scattered_pkts_vec | dpdk_input_avx2 | ethernet_input_avx2 | l2input_node_fn_avx2 | l2learn_node_fn_avx2 | l2fwd_node_fn_avx2 | l2output_node_fn_avx2 | vnet_interface_output_node | dpdk_interface_tx_avx2 | i40e_xmit_pkts_vec | i40e_xmit_pkts_vec | i40e_xmit_pkts_vec | i40e_xmit_pkts_vec | i40e_xmit_pkts_vec | i40e_xmit_pkts_vec | i40e_xmit_pkts_vec | i40e_xmit_pkts_vec | i40e_xmit_pkts_vec | i40e_xmit_pkts_vec | i40e_xmit_pkts_vec | i40e_xmit_pkts_vec | i40e_xmit_pkts_vec | i40e_xmit_pkts_vec | i40e_xmit_pkts_vec | i40e_xmit_pkts_vec
 | 6.7812 | 6.7773 | 6.7812 | 6.7812 | 6.7812 | 6.7812 | 6.7812 | 6.7812 | 48.5664 | 50.2578 | 52.1992 | 87.4023 | 82.1562 | 46.6055 | 23.1914 | 30.0508 | 2.457 | 2.8125 | 2.457 | 2.8125 | 2.457 | 2.8125 | 2.457 | 2.8125 | 2.457 | 2.8125 | 2.457 | 2.8125 | 2.457 | 2.8242 | 2.457 | 2.8359
256 packets = 32-packet rx burst * 8 loops
256 packets = 16-packet tx burst * 16 loops
Dense packet processing functions
Rx
Processing
Not the most optimal driver path
Tx
Notes: Explain the chart
Identify heavy duty functions
Offload methods
Burst / loop
Part of Linux perf (Intel upstream to kernel)
Code footprint (Coremark example)
Compiler comparison

## Slide 19: Core Performance Takeaway
Use perfmon hardware to baseline workload performance.
  PCM, Linux* Perf (pmu-tools/{toplev.py, ucevents.py}, intel_pt)
Reduce instruction counts per packet
  Create more direct VPP path to process packets
  Consider hardware offload
Reduce cycles per packet
  Follow uncore performance takeaway to reduce latency
  Measure CPU L1 cache miss latency and look for opportunity to prefetch it (not covered)

## Slide 20: References
Xeon® E5-v4 Uncore Performance Monitor Unit (PMU) guide: https://software.intel.com/en-us/blogs/2014/07/11/documentation-for-uncore-performance-monitoring-units
Intel® 64 and IA-32 Architectures Optimization Reference Manual: http://www.intel.com/content/www/us/en/architecture-and-technology/64-ia-32-architectures-optimization-manual.html
Processor Counter Monitoring (PCM): https://github.com/opcm/pcm
pmu-tools: https://github.com/andikleen/pmu-tools
Intel® Processor Trace Linux* perf support: https://github.com/torvalds/linux/blob/master/tools/perf/Documentation/intel-pt.txt

## Slide 22: Backup

## Slide 23
Measure QPI
(Cross Sockets) Bandwidth

## Slide 24: Measure QPI (cross sockets) Bandwidth
Processor Counter Monitoring (PCM): ./pcm.x -nc
Any QPI traffic will inevitably hurt latency, if not throughput.
QPI traffic is determined by placements of CPU, memory and I/O.
If unavoidable, watch for link utilization.

## Slide 25: TMAM
Top-Down Analysis Methodology (TMAM)

## Slide 26: Linux perf + pmu-tools
Perfmon device abstractions layers reside in /sys/devices
#Event not upstreamed yet.
/ucevent.py --scale MEGA CBO.CPU_OUTBOUND_MMIO_READ \
CBO.CPU_OUTBOUND_MMIO_WRITE \
CBO.PCIE_INBOUND_READ_HIT_DDIO \
CBO.PCIE_INBOUND_READ_MISS_DDIO \
CBO.PCIE_INBOUND_WRITE_HIT_DDIO \
CBO.PCIE_INBOUND_WRITE_MISS_DDIO
./ucevent.py --scale MEGA iMC.MEM_BW_READS iMC.MEM_BW_WRITES
./ucevent.py --scale MEGA QPI_LL.QPI_DATA_BW QPI_LL.QPI_LINK_BW
Measure PCIe Bandwidth with Linux perf (events pending upstream):
Measure Memory Bandwidth with Linux perf:
Measure QPI Bandwidth with Linux perf:
Notes: Use –v to see the raw perf encoding.