## Slide 1: Data Plane Development Kit (DPDK) Intro DPDK/FD.io Mini Summit
Tim O’Driscoll
21st June, 2016

## Slide 2: Legal Disclaimer
General Disclaimer:
© Copyright 2016 Intel Corporation. All rights reserved. Intel, the Intel logo, Intel Inside, the Intel Inside logo, Intel. Experience What’s Inside are trademarks of Intel. Corporation in the U.S. and/or other countries. *Other names and brands may be claimed as the property of others.
Technology Disclaimer:
Intel technologies’ features and benefits depend on system configuration and may require enabled hardware, software or service activation. Performance varies depending on system configuration. No computer system can be absolutely secure. Check with your system manufacturer or retailer or learn more at [intel.com].
Performance Disclaimers:
Cost reduction scenarios described are intended as examples of how a given Intel- based product, in the specified circumstances and configurations, may affect future costs and provide cost savings. Circumstances will vary. Intel does not guarantee any costs or cost reduction.
Results have been estimated or simulated using internal Intel analysis or architecture simulation or modeling, and provided to you for informational purposes. Any differences in your system hardware, software or configuration may affect your actual performance.

## Slide 3: DPDK Overview

## Slide 4: DPDK Framework
* Other names and brands may be claimed as the property of others.
User Space
KNI
IGB_UIO
VFIO
EAL
MBUF
MEMPOOL
RING
TIMER
Kernel
UIO_PCI_GENERIC
FM10K
IXGBE
VMXNET3
IGB
E1000
I40E
XENVIRT
PCAP
MLX4
MLX5
ETHDEV
RING
NULL
AF_PKT
BONDING
VIRTIO
ENIC
CXGBE
BNX2X
PMDs: Native & Virtual
SZEDATA2
NFP
MPIPE
HASH
LPM
ACL
JOBSTAT
DISTRIB
IP FRAG
KNI
REORDER
POWER
VHOST
IVSHMEM
SCHED
METER
PIPELINE
PORT
TABLE
Network Functions (Cloud, Enterprise, Comms)
CRYPTO
QAT
AESNI MB
Future
TBD
Accelerators
Core
Classify
Extensions
QoS
Pkt Framework
ENA
AESNI GCM
SNOW 3G
NULL
VHOST

## Slide 5: Multi-Architecture/NIC Support
1.8
2.0
2.1
2.2
16.04
16.07
IGB
IXGBE
E1000
I40E
X86
IA32
POWER 8
ENIC
FM10K
MLX4
TILE-Gx
CXGBE
BNX2X
ARM v7/v8
CPUs
NICs
MLX5
SZEDATA2
NFP-6xxx
* Other names and brands may be claimed as the property of others.
ENA
QEDE
ThunderX
Layerscape

## Slide 6: DPDK Generational Performance Gains
Disclaimer: Software and workloads used in performance tests may have been optimized for performance only on Intel microprocessors. Performance tests, such as SYSmark and MobileMark, are measured using specific computer systems, components, software, operations and functions. Any change to any of those factors may cause the results to vary. You should consult other information and performance tests to assist you in fully evaluating your contemplated purchases, including the performance of that product when combined with other products. For more complete information visit http://www.intel.com/performance.
IPV4 L3 Forwarding Performance of 64Byte Packets
* Other names and brands may be claimed as the property of others.
Broadwell EP System Configuration |  |  | 
Hardware |  |  | 
Platform | SuperMicro® - X10DRX |  | 
CPU | Intel® Xeon® Processor E5-2658 v4 |  | 
Chipset | Intel® C612 chipset |  | 
Sockets | 2 |  | 
Cores per Socket | 14 (28 threads) |  | 
LL CACHE | 30 MB |  | 
QPI/DMI | 9.6GT/s |  | 
PCIe | Gen3x8 |  | 
MEMORY | DDR4 2400 MHz, 1Rx4 8GB (total 64GB), 4 Channel per Socket |  | 
NIC | 10 x Intel® Ethernet CNA XL710-QDA2PCI-Express Gen3 x8 Dual Port 40 GbE Ethernet NIC (1x40G/card) |  | 
NIC Mbps | 40,000 |  | 
BIOS | BIOS version: 1.0c (02/12/2015) |  | 
Software |  |  | 
OS | Debian 8.0 |  | 
Kernel version | 3.18.2 |  | 
Other | DPDK2.2.0 |  | 
Chart: Year
| 2010 (2S WMR) | 2011 (1S SNB) | 2012(2S SNB) | 2013 (2S IVB) | 2014 (2S HSW) | 2015 (2S BDW)
 | 55 | 80.1 | 164.9 | 255 | 279.9 | 346.7
171.4
Gbps
187.2
Gbps
233
Gbps
2010
(2S WMR)
2011
(1S SNB)
2013
(2S IVB)
2012
(2S SNB)
2015
(2S BDW)
2014
(2S HSW)

## Slide 7: Open Source Stats
A fully open source software project with a strong development community:
BSD licensed
Website: http://dpdk.org; Git: http://dpdk.org/browse/dpdk/
Major Contributors
DPDK Release Stats
* Other names and brands may be claimed as the property of others.
Chart: Total Commits
| 1.5 | 1.6 | 1.7 | 1.8 | 2.0 | 2.1 | 2.2 | 16.04
Total Contributors | 22 | 26 | 34 | 70 | 63 | 84 | 100 | 102
Total Commits | 193 | 196 | 320 | 680 | 530 | 827 | 797 | 704

## Slide 8: DPDK In OPNFV

## Slide 9: OPNFV Projects
Doctor
Octopus
SFSQM
Copper
Availability
Escalator
OpenStack Fwd Graph
Promise
Movie
DPACC
Multisite
Resource Scheduler
Prediction
Inspector
Pinpoint
Genesis
ENFV
Models
Domino
NetReady
BGS
IPv6
VSPERF
Pharos
FuncTest
Yardstick
Parser
Qtip
JOID
Apex
Releng
Compass
Fuel
ARMBand
DoveTail
Bottleneck
StorPerf
PolicyTest
CPERF
FDS
ONOSFW
Moon
SFC
OVSNFV
KVM
OVNO
SDNVPN
OPNFV
Doc
Collaborative Development
Integration and Testing
Requirements
Documentation

## Slide 10: DPDK Involvement
Doctor
Octopus
SFSQM
Copper
Availability
Escalator
OpenStack Fwd Graph
Promise
Movie
DPACC
Multisite
Resource Scheduler
Prediction
Inspector
Pinpoint
Genesis
ENFV
Models
Domino
NetReady
BGS
IPv6
VSPERF
Pharos
FuncTest
Yardstick
Parser
Qtip
JOID
Apex
Releng
Compass
Fuel
ARMBand
DoveTail
Bottleneck
StorPerf
PolicyTest
CPERF
FDS
ONOSFW
Moon
SFC
OVSNFV
KVM
OVNO
SDNVPN
OPNFV
Doc
Direct DPDK Involvement
Indirect DPDK Involvement

## Slide 11: DPDK Involvement
Doctor
Octopus
SFSQM
Copper
Availability
Escalator
OpenStack Fwd Graph
Promise
Movie
DPACC
Multisite
Resource Scheduler
Prediction
Inspector
Pinpoint
Genesis
ENFV
Models
Domino
NetReady
BGS
IPv6
VSPERF
Pharos
FuncTest
Yardstick
Parser
Qtip
JOID
Apex
Releng
Compass
Fuel
ARMBand
DoveTail
Bottleneck
StorPerf
PolicyTest
CPERF
FDS
ONOSFW
Moon
SFC
OVSNFV
KVM
OVNO
SDNVPN
OPNFV
Doc
Direct DPDK Involvement
Indirect DPDK Involvement
Data Plane Acceleration (DPACC)
The goal of this project is to specify a general framework for VNF data plane acceleration (or DPA for short), including a common suite of abstract APIs at various OPNFV interfaces, to enable VNF portability and resource management across various underlying integrated SOCs that may include hardware accelerators or standard high volume (or SHV) server platforms that may include attached hardware accelerators.
DPDK Impacts:
Multi-architecture support, especially the addition of ARMv8 in DPDK 2.2.
External Mempool Manager in DPDK 16.07 to provide better inter-working with SoCs.
Addition of cryptodev API to support hardware and software crypto acceleration.
Future support for additional accelerator types.

## Slide 12: DPDK Involvement
Doctor
Octopus
SFSQM
Copper
Availability
Escalator
OpenStack Fwd Graph
Promise
Movie
DPACC
Multisite
Resource Scheduler
Prediction
Inspector
Pinpoint
Genesis
ENFV
Models
Domino
NetReady
BGS
IPv6
VSPERF
Pharos
FuncTest
Yardstick
Parser
Qtip
JOID
Apex
Releng
Compass
Fuel
ARMBand
DoveTail
Bottleneck
StorPerf
PolicyTest
CPERF
FDS
ONOSFW
Moon
SFC
OVSNFV
KVM
OVNO
SDNVPN
OPNFV
Doc
Direct DPDK Involvement
Indirect DPDK Involvement
Software Fastpath Service Quality Metrics (SFQSM)
“Software Fastpath Service Quality Metrics" is focused on the development of utilities and libraries which supports low latency, high performance packet processing paths (fast path) through the NFVI such that VNFs can:
Measure Telco Traffic and Performance KPIs through that software fast path.
Detect and report violations that can be consumed by VNFs and higher level EMS/OSS systems.
DPDK Impacts:
Extended stats (xstats), which allows each PMD to expose a unique set of stats in the form of string-value pairs.
Keep Alive, which demonstrates how to detect ‘failed’ DPDK cores and notify a fault management entity of the failure.

## Slide 13: DPDK Involvement
Doctor
Octopus
SFSQM
Copper
Availability
Escalator
OpenStack Fwd Graph
Promise
Movie
DPACC
Multisite
Resource Scheduler
Prediction
Inspector
Pinpoint
Genesis
ENFV
Models
Domino
NetReady
BGS
IPv6
VSPERF
Pharos
FuncTest
Yardstick
Parser
Qtip
JOID
Apex
Releng
Compass
Fuel
ARMBand
DoveTail
Bottleneck
StorPerf
PolicyTest
CPERF
FDS
ONOSFW
Moon
SFC
OVSNFV
KVM
OVNO
SDNVPN
OPNFV
Doc
Direct DPDK Involvement
Indirect DPDK Involvement
Open vSwitch for NFV (OVSNFV)
This project proposes:
Modifying the OPNFV build to include a deployment option for the software-accelerated userspace Open vSwitch build. This change will significantly improve the performance of the NFVI for network I/O.
Future work that will encompass collaborative development within the Open vSwitch project to improve the performance of the software-accelerated userspace Open vSwitch and increasing its suitability for Telco NFV deployments.
DPDK Impacts:
DPDK enablement of Open vSwitch.
Vhost-Virtio performance optimisations in DPDK which help to further improvement the performance of the DPDK-enables userspace OVS. These include: Vhost-User support (2.0), Vhost Multi-Queue Support (2.2), Virtio 1.0 support (16.04), Vhost-Virtio performance optimisations (2.2, 16.04).

## Slide 14: DPDK Involvement
Doctor
Octopus
SFSQM
Copper
Availability
Escalator
OpenStack Fwd Graph
Promise
Movie
DPACC
Multisite
Resource Scheduler
Prediction
Inspector
Pinpoint
Genesis
ENFV
Models
Domino
NetReady
BGS
IPv6
VSPERF
Pharos
FuncTest
Yardstick
Parser
Qtip
JOID
Apex
Releng
Compass
Fuel
ARMBand
DoveTail
Bottleneck
StorPerf
PolicyTest
CPERF
FDS
ONOSFW
Moon
SFC
OVSNFV
KVM
OVNO
SDNVPN
OPNFV
Doc
Direct DPDK Involvement
Indirect DPDK Involvement
Fault Management (Doctor)
The goal of this project is to build a fault management and maintenance framework for high availability of Network Services on top of virtualized infrastructure. The key feature is immediate notification of unavailability of virtualized resources from VIM, to process recovery of VNFs on them.
DPDK Impacts:
The Extended Statistics and Keep Alive functionality from DPDK, along with the DPDK Ceilometer plugin developed as part of the SFSQM project address some of the requirements of the Doctor project. The SFSQM and Doctor teams are collaborating closely to ensure that these efforts are coordinated.

## Slide 15: DPDK Involvement
Doctor
Octopus
SFSQM
Copper
Availability
Escalator
OpenStack Fwd Graph
Promise
Movie
DPACC
Multisite
Resource Scheduler
Prediction
Inspector
Pinpoint
Genesis
ENFV
Models
Domino
NetReady
BGS
IPv6
VSPERF
Pharos
FuncTest
Yardstick
Parser
Qtip
JOID
Apex
Releng
Compass
Fuel
ARMBand
DoveTail
Bottleneck
StorPerf
PolicyTest
CPERF
FDS
ONOSFW
Moon
SFC
OVSNFV
KVM
OVNO
SDNVPN
OPNFV
Doc
Direct DPDK Involvement
Indirect DPDK Involvement
Characterize vSwitch Performance for Telco NFV Use Cases (VSPERF)
“vSwitch Performance" will develop a generic and architecture agnostic vSwitch testing framework and associated tests, that will serve as a basis for validating the suitability of different vSwitch implementations in a Telco NFV deployment environment.
DPDK Impacts:
This project includes support for DPDK-enabled OVS, as well as MoonGen, which is a DPDK-enabled software traffic generator.

## Slide 16: DPDK Involvement
Doctor
Octopus
SFSQM
Copper
Availability
Escalator
OpenStack Fwd Graph
Promise
Movie
DPACC
Multisite
Resource Scheduler
Prediction
Inspector
Pinpoint
Genesis
ENFV
Models
Domino
NetReady
BGS
IPv6
VSPERF
Pharos
FuncTest
Yardstick
Parser
Qtip
JOID
Apex
Releng
Compass
Fuel
ARMBand
DoveTail
Bottleneck
StorPerf
PolicyTest
CPERF
FDS
ONOSFW
Moon
SFC
OVSNFV
KVM
OVNO
SDNVPN
OPNFV
Doc
Direct DPDK Involvement
Indirect DPDK Involvement
FastDataStacks (FDS)
“FastDataStacks” creates and composes a set of scenarios which include the virtual forwarder supplied by the FD.IO project. The project also provides required enhancements to individual components such as SDN controllers or installers to allow for the scenario composition.
DPDK Impacts:
The focus of this project is on enhancements to FD.io and other components including SDN controllers and installers, but the core component of FD.io, VPP, is based on DPDK.

## Slide 18: FD.io Intro
Ed Warnicke

## Slide 19: Evolution of Programmable Networking
Many industries are transitioning to a more dynamic model to deliver network services
The great unsolved problem is how to deliver network services in this more dynamic environment
Inordinate attention has been focused on the non-local network control plane (controllers)
  Necessary, but insufficient
There is a giant gap in the capabilities that foster delivery of dynamic Data Plane Services
Programmable Data Plane
CLOUD
NFV
SDN

## Slide 20: Introducing Fast Data: fd.io
New project in Linux Foundation
  Multi-party
  Multi-project
What does multi-party mean?
  Multiple members - Open to all
What does multi-project mean?
  Multiple subprojects
  Subproject autonomy
  Cross project synergy
  Open to new subprojects
  Anyone can propose a subproject
  Allows for innovation
Create a Platform that enables Data Plane Services that are:
  Highly performant
  Modular and extensible
  Open source
  Interoperable
  Multi-Vendor
Platform fosters innovation and synergistic interoperability between Data Plane Services
Source of Continuous Integration resources for Data Plane services based on the Consortium’s project/subprojects
Meet the functionality needs of developers, deployers, datacenter operators
fd.io Charter

## Slide 21: Fast Data Scope
Fast Data Scope:
    IO
      Hardware/vHardware <-> cores/threads
  Processing
    Classify
    Transform
    Prioritize
    Forward
    Terminate
  Management Agents
    Control/manage IO/Processing
IO
Processing
Management Agent
Bare Metal/VM/Container

## Slide 22: Fd.io Members

## Slide 23: Fd.io Projects
Network IO
Packet Processing
VPP
Management Agent
NSH_SFC
ONE
VPP Sandbox
TLDK
Honeycomb
Testing/Performance/Support
CSIT
Legend:
- New Projects
- Core Projects
deb_dpdk

## Slide 24: Governance – At a Glance
Anyone May Participate – Not just members
  Anyone can contribute code
  Anyone can rise to being a committer via meritocracy
  Anyone can propose a subproject
Subprojects:
  Composed of the committers to that subproject – those who can merge code
  Responsible for sub project oversight and autonomous releases
  Make technical decisions for that subproject by consensus, or failing that, majority vote.
Technical Steering Committee
  Fosters collaboration among subprojects, but is not involved in day to day management of sub-projects
  Approves new subprojects, sets development process guidelines for the community, sets release guidelines for multi-project or simultaneous releases, etc.
  Initial TSC will be seeded with representatives from Platinum Membership and core project PTLs with the goal of replacing representatives with Project Leads after the first year
Governing Board will Oversee Business Decision Making
  Set Scope and Policy of Consortium
  Composed of Platinum member appointees, elected Gold, Silver, and Committer member representatives
  Examples of business needs include: budgeting, planning for large meetings (e.g. a Summit, Hackfest), marketing, websites, developer infrastructure, test infrastructure, etc.

## Slide 25: VPP: Vector Packet Processing

## Slide 26: Introducing Vector Packet Processor - VPP
VPP is a rapid packet processing development platform for highly performing network applications.
It runs on commodity CPUs and leverages DPDK
It creates a vector of packet indices and processes them using a directed graph of nodes – resulting in a highly performant solution.
Runs as a Linux user-space application
Ships as part of both embedded & server products, in volume
Active development since 2002
Network IO
Packet Processing
Data Plane Management Agent
Bare Metal/VM/Container

## Slide 27: VPP Architecture - Modularity Enabling Flexible Plugins
Plugins == Subprojects
Plugins can:
  Introduce new graph nodes
  Rearrange packet processing graph
  Can be built independently of VPP source tree
  Can be added at runtime (drop into plugin directory)
  All in user space
Enabling:
  Ability to take advantage of diverse hardware when present
  Support for multiple processor architectures (x86, ARM, PPC)
  Few dependencies on the OS (clib) allowing easier ports to other Oses/Env
ethernet-input
ip6-input
ip4input
mpls-ethernet-input
arp-input
llc-input
…
ip6-lookup
ip6-rewrite-transmit
ip6-local
…
Packet vector
Plug-in to create new nodes
Custom-A
Custom-B
Plug-in to enable new HW input Nodes

## Slide 28: VPP Feature Summary
  14+ MPPS, single core
  Multimillion entry FIBs
  Source RPF
  Thousands of VRFs
  Controlled cross-VRF lookups
  Multipath – ECMP and Unequal Cost
  Multiple million Classifiers –
  Arbitrary N-tuple
  VLAN Support – Single/Double tag
  Counters for everything
  Mandatory Input Checks:
  TTL expiration
  header checksum
  L2 length < IP length
  ARP resolution/snooping
  ARP proxy
  IPv4/IPv6
  IPv4
  GRE, MPLS-GRE, NSH-GRE,
  VXLAN
  IPSEC
  DHCP client/proxy
  CG NAT
  IPv6
  Neighbor discovery
  Router Advertisement
  DHCPv6 Proxy
  L2TPv3
  Segment Routing
  MAP/LW46 – IPv4aas
  iOAM
  MPLS
  MPLS-o-Ethernet –
  Deep label stacks supported
  L2
  VLAN Support
  Single/ Double tag
  L2 forwarding with EFP/BridgeDomain concepts
  VTR – push/pop/Translate (1:1,1:2, 2:1,2:2)
  Mac Learning – default limit of 50k addresses
  Bridging – Split-horizon group support/EFP Filtering
  Proxy Arp
  Arp termination
  IRB – BVI Support with RouterMac assignment
  Flooding
  Input ACLs
  Interface cross-connect
Notes: The input checks included by VPP include mandatory networking checks.
Some solutions today either don’t perform these or don’t have them leading to questionable performance numbers

## Slide 29: Code Activity
Fd.io
Fd.io has more code activities (commits, contributors) than other dataplane project (data from openhub)
ovs
dpdk

## Slide 30: Contributor/Committer Diversity
Universitat Politècnica de Catalunya (UPC)

## Slide 31: VPP 16.06 Release
Released 2016-06-17
Enhanced Switching & Routing
  IPv6 Segment Routing multicast support
  LISP xTR support
  VXLAN over IPv6 underlay
  per interface whitelists
  shared adjacencies in FIB
New and improved interface support
  jumbo frame support for vhost-user
  Netmap interface support
  AF_Packet interface support
Expanded and improved programmability
  Python API bindings
  Enhanced JVPP Java API bindings
  Enhanced debugging cli
Expanded Hardware and Software Support
  Support for ARM 32 targets
  Support for Raspberry Pi
  Support for DPDK 16.04

## Slide 32
VPP technology in a nutshell
VPP data plane throughput not impacted by large FIB size
OVSDPDK data plane throughput heavily impacted by FIB size
VPP and OVSDPDK tested on Haswell x86 platform with E5-2698v3 2x16C 2.3GHz (Ubuntu 14.04 trusty)
Chart: 
| 2 MACs | 2k MACs | 20k MACs
OVSDPDK | 20 | 4 | 0.6
VPP | 20 | 20 | 20
NDR rates for 2p10GE, 1 core, L2 NIC-to-NIC
[IMIX Gbps]
Chart: 
| 12 routes | 1k routes | 100k routes | 500k routes | 1M routes | 2M routes
OVSDPDK | 120 | 48 | 3.6 | 0 | 0 | 0
VPP | 120 | 120 | 120 | 120 | 120 | 120
NDR rates for 12 port 10GE, 12 cores, IPv4
[IMIX Gbps]
not tested

## Slide 33: vNet-SLA benchmarking at scale: IPv6 VPP-based vSwitch
Chart: 
| 12 routes | 1k routes | 100k routes | 500k routes | 1M routes | 2M routes
64B | 210 | 210 | 210 | 210 | 210 | 210
IMIX | 160 | 160 | 160 | 160 | 160 | 160
1518B | 39 | 39 | 39 | 39 | 39 | 39
Chart: 
| 12 routes | 1k routes | 100k routes | 500k routes | 1M routes | 2M routes
64B | 108 | 108 | 108 | 108 | 108 | 108
IMIX | 480 | 480 | 480 | 480 | 480 | 480
1518B | 480 | 480 | 480 | 480 | 480 | 480
FD.io VPP data plane throughput not impacted by large size of IPv6 FIB
VPP tested on UCS 4-CPU-socket server with 4 of Intel “Haswell" x86-64 processors E7-8890v3 18C 2.5GHz
24 Cores used – Another 48 cores can be used for other network services!
[Gbps]
Phy-VS-Phy
Zero-packet-loss Throughput for 12 port 40GE, 24 cores, IPv6
[Mpps]
VPP vSwitch IPv4 routed forwarding FIB with 2 milion IPv6 entries 12x40GE (480GE) 64B frames
200Mpps zero frame loss
NIC and PCIe is the limit not VPP
VPP vSwitch IPv4 routed forwarding FIB with 2 milion IPv6 entries
12x40GE (480GE) IMIX frames
480Gbps zero frame loss
“Sky” is the limit not VPP
Zero-packet-loss Throughput for 12 port 40GE, 24 cores, IPv6

## Slide 34: vNet benchmarking at scale: IPv4+SEcurity
FD.io VPP data plane throughput not impacted by large size of IPv4 FIB
VPP tested on UCS 4-CPU server with 4x Intel E7-8890v3 (18C 2.5GHz)
36 Core used – NIC RSS=2 to drive NIC performance, VPP cores not busy!
Another 36 cores available for other services!
Zero-Packet-Loss Throughput for 18 port 40GE, 36 cores, IPv4
64B => 238 Mpps
NIC and PCIe is the limit not VPP
IMIX => 342 Gbps
1518B => 462 Gbps
“Sky” is the limit not VPP
VPP vSwitch IPv4 rtd fwding, FIB up to 8M IPv4, 2k white-list
Zero Packet Loss Measurements
Chart: 
| 1k routes | 500k routes | 1M routes | 2M routes | 4M routes | 8M routes
64B | 199.58 | 199.58 | 199.58 | 199.58 | 199.58 | 199.58
IMIX | 342 | 342 | 342 | 342 | 342 | 342
1518B | 462 | 462 | 462 | 462 | 462 | 462
[Gbps]
That is Right – No Impact on IMIX and 1518B Performance
Chart: 
| 1k routes | 500k routes | 1M routes | 2M routes | 4M routes | 8M routes
64B | 297 | 297 | 297 | 297 | 297 | 297
IMIX | 160 | 160 | 160 | 160 | 160 | 160
1518B | 39 | 39 | 39 | 39 | 39 | 39
[Mpps]

## Slide 35
VPP Cores Not Completely Busy
VPP Vectors Have Space For More Services and More Packets!!
PCIe 3.0 and NICs Are The Limit
And How Do We Know This?
Simples – A Well Engineered Telemetry
In Linux and VPP Tells Us So
========
TC5 120ge.vpp.24t24pc.ip4.cop
TC5.0 120ge.2pnic.6nic.rss2.vpp.24t24pc.ip4.cop
d. testcase-vpp-ip4-cop-scale
120ge.2pnic.6nic.rss2.vpp.24t24pc.ip4.2m.cop.2.copip4dst.2k.match.100
64B, 138.000Mpps, 92,736Gbps
IMIX, 40.124832Mpps, 120.000Gbps
1518, 9.752925Mpps, 120.000Gbps
---------------
Thread 1 vpp_wk_0 (lcore 2)
Time 45.1, average vectors/node 23.44, last 128 main loops 1.44 per node 23.00
vector rates in 4.6791e6, out 4.6791e6, drop 0.0000e0, punt 0.0000e0
Name State Calls Vectors Suspends Clocks Vectors/Call
TenGigabitEtherneta/0/1-output active 9003498 211054648 0 1.63e1 23.44
TenGigabitEtherneta/0/1-tx active 9003498 211054648 0 7.94e1 23.44
cop-input active 9003498 211054648 0 2.23e1 23.44
dpdk-input polling 45658750 211054648 0 1.52e2 4.62
ip4-cop-whitelist active 9003498 211054648 0 4.34e1 23.44
ip4-input active 9003498 211054648 0 4.98e1 23.44
ip4-lookup active 9003498 211054648 0 6.25e1 23.44
ip4-rewrite-transit active 9003498 211054648 0 3.43e1 23.44
---------------
Thread 24 vpp_wk_23 (lcore 29)
Time 45.1, average vectors/node 27.04, last 128 main loops 1.75 per node 28.00
vector rates in 4.6791e6, out 4.6791e6, drop 0.0000e0, punt 0.0000e0
Name State Calls Vectors Suspends Clocks Vectors/Call
TenGigabitEthernet88/0/0-outpu active 7805705 211055503 0 1.54e1 27.04
TenGigabitEthernet88/0/0-tx active 7805705 211055503 0 7.75e1 27.04
cop-input active 7805705 211055503 0 2.12e1 27.04
dpdk-input polling 46628961 211055503 0 1.60e2 4.53
ip4-cop-whitelist active 7805705 211055503 0 4.35e1 27.04
ip4-input active 7805705 211055503 0 4.86e1 27.04
ip4-lookup active 7805705 211055503 0 6.02e1 27.04
ip4-rewrite-transit active 7805705 211055503 0 3.36e1 27.04

## Slide 36
VPP Cores Not Completely Busy
VPP Vectors Have Space For More Services and More Packets!!
PCIe 3.0 and NICs Are The Limit
And How Do We Know This?
Simple – A Well Engineered Telemetry
In Linux and VPP Tells Us So
========
TC5 120ge.vpp.24t24pc.ip4.cop
TC5.0 120ge.2pnic.6nic.rss2.vpp.24t24pc.ip4.cop
d. testcase-vpp-ip4-cop-scale
120ge.2pnic.6nic.rss2.vpp.24t24pc.ip4.2m.cop.2.copip4dst.2k.match.100
64B, 138.000Mpps, 92,736Gbps
IMIX, 40.124832Mpps, 120.000Gbps
1518, 9.752925Mpps, 120.000Gbps
---------------
Thread 1 vpp_wk_0 (lcore 2)
Time 45.1, average vectors/node 23.44, last 128 main loops 1.44 per node 23.00
vector rates in 4.6791e6, out 4.6791e6, drop 0.0000e0, punt 0.0000e0
Name State Calls Vectors Suspends Clocks Vectors/Call
TenGigabitEtherneta/0/1-output active 9003498 211054648 0 1.63e1 23.44
TenGigabitEtherneta/0/1-tx active 9003498 211054648 0 7.94e1 23.44
cop-input active 9003498 211054648 0 2.23e1 23.44
dpdk-input polling 45658750 211054648 0 1.52e2 4.62
ip4-cop-whitelist active 9003498 211054648 0 4.34e1 23.44
ip4-input active 9003498 211054648 0 4.98e1 23.44
ip4-lookup active 9003498 211054648 0 6.25e1 23.44
ip4-rewrite-transit active 9003498 211054648 0 3.43e1 23.44
---------------
Thread 24 vpp_wk_23 (lcore 29)
Time 45.1, average vectors/node 27.04, last 128 main loops 1.75 per node 28.00
vector rates in 4.6791e6, out 4.6791e6, drop 0.0000e0, punt 0.0000e0
Name State Calls Vectors Suspends Clocks Vectors/Call
TenGigabitEthernet88/0/0-outpu active 7805705 211055503 0 1.54e1 27.04
TenGigabitEthernet88/0/0-tx active 7805705 211055503 0 7.75e1 27.04
cop-input active 7805705 211055503 0 2.12e1 27.04
dpdk-input polling 46628961 211055503 0 1.60e2 4.53
ip4-cop-whitelist active 7805705 211055503 0 4.35e1 27.04
ip4-input active 7805705 211055503 0 4.86e1 27.04
ip4-lookup active 7805705 211055503 0 6.02e1 27.04
ip4-rewrite-transit active 7805705 211055503 0 3.36e1 27.04
VPP average vector size below shows 23-to-27
This indicates VPP program worker threads are not busy
Busy VPP worker threads should be showing 255
This means that VPP worker threads operate at 10% capacity
It’s like driving 1,000hp car at 100hp power – lots of space
for adding (service) acceleration and (sevice) speed.

## Slide 37
VPP Cores Not Completely Busy
VPP Vectors Have Space For More Services and More Packets!!
PCIe 3.0 and NICs Are The Limit
And How Do We Know This?
Simples – A Well Engineered Telemetry
In Linux and VPP Tells Us So
========
TC5 120ge.vpp.24t24pc.ip4.cop
TC5.0 120ge.2pnic.6nic.rss2.vpp.24t24pc.ip4.cop
d. testcase-vpp-ip4-cop-scale
120ge.2pnic.6nic.rss2.vpp.24t24pc.ip4.2m.cop.2.copip4dst.2k.match.100
64B, 138.000Mpps, 92,736Gbps
IMIX, 40.124832Mpps, 120.000Gbps
1518, 9.752925Mpps, 120.000Gbps
---------------
Thread 1 vpp_wk_0 (lcore 2)
Time 45.1, average vectors/node 23.44, last 128 main loops 1.44 per node 23.00
vector rates in 4.6791e6, out 4.6791e6, drop 0.0000e0, punt 0.0000e0
Name State Calls Vectors Suspends Clocks Vectors/Call
TenGigabitEtherneta/0/1-output active 9003498 211054648 0 1.63e1 23.44
TenGigabitEtherneta/0/1-tx active 9003498 211054648 0 7.94e1 23.44
cop-input active 9003498 211054648 0 2.23e1 23.44
dpdk-input polling 45658750 211054648 0 1.52e2 4.62
ip4-cop-whitelist active 9003498 211054648 0 4.34e1 23.44
ip4-input active 9003498 211054648 0 4.98e1 23.44
ip4-lookup active 9003498 211054648 0 6.25e1 23.44
ip4-rewrite-transit active 9003498 211054648 0 3.43e1 23.44
---------------
Thread 24 vpp_wk_23 (lcore 29)
Time 45.1, average vectors/node 27.04, last 128 main loops 1.75 per node 28.00
vector rates in 4.6791e6, out 4.6791e6, drop 0.0000e0, punt 0.0000e0
Name State Calls Vectors Suspends Clocks Vectors/Call
TenGigabitEthernet88/0/0-outpu active 7805705 211055503 0 1.54e1 27.04
TenGigabitEthernet88/0/0-tx active 7805705 211055503 0 7.75e1 27.04
cop-input active 7805705 211055503 0 2.12e1 27.04
dpdk-input polling 46628961 211055503 0 1.60e2 4.53
ip4-cop-whitelist active 7805705 211055503 0 4.35e1 27.04
ip4-input active 7805705 211055503 0 4.86e1 27.04
ip4-lookup active 7805705 211055503 0 6.02e1 27.04
ip4-rewrite-transit active 7805705 211055503 0 3.36e1 27.04
VPP average vector size below shows 23-to-27
This indicates VPP program worker threads are not busy
Busy VPP worker threads should be showing 255
This means that VPP worker threads operate at 10% capacity
It’s like driving 1,000bhp car at 100bhp power – lots of space
for adding (service) acceleration and (sevice) speed.
VPP is also counting the cycles-per-packet (CPP)
We know exactly what feature, service, packet processing activity is using the CPU cores
We can engineer, we can capacity plan, we can automate service placement
We can scale across many many CPU cores and computers
And AUTOMATE it easily – as it is after all just SOFTWARE

## Slide 38
Compute Node Hardware | Cisco UCS C460 M4
Chipset | Intel® C610 series chipset
CPU | 4 x Intel® Xeon® Processor E7-8890 v3 (18 cores, 2.5GHz, 45MB Cache)
Memory | 2133 MHz, 512 GB Total
NICs | 9 x 2p40GE Intel XL710 18 x 40GE = 720GE !!
Compute Node Software | Version
Host Operating System | Ubuntu 14.04.3 LTS Kernel version: 3.13.0-63-generic
DPDK | DPDK 2.2.0
FD.io VPP | vpp v1.0.0-174~g57a90e5
The Fast Data Project (FD.io)
18 x 7.7trillion packets forwarded.
Max Packet Delay <3.5 msec incl. the outliers!!
The Soak Test Proof:
Low long-term max packet delay with FD.io VPP
>>120 msec long-term max packet delay measured by others for other vSwitches
But it is just not not there with VPP and stock Ubuntu 14.04 (no Linux tuning!)
ONE MORE THING – THE LONG TERM MAX DELAY
Min Packet Delay 7..10 usec, Avg Packet Delay <23 usec.
Max
Delay
Min
Delay
Avg
Delay

## Slide 39: Implementation Example: VPP as a vRouter/vSwitch
Out of the box vSwitch/vRouter
  Including CLI
Switching
  Can Create
  Bridge Domains
  Ports (including tunnel ports)
  Connect ports to bridge domains
  Program ARP termination
  etc
Routing
  Can Create
  VRFs - thousands
  Routes - millions
Linux Host
Kernel
DPDK
VPP App
Switch-1
Switch-2
VRF-1
VRF-2

## Slide 40: VPP vRouter/vSwitch: Local Programmability
Linux Host
Kernel
DPDK
VPP App
External App
Low Level API
  Complete
  Feature Rich
  High Performance
    Example: 900k routes/s
  Shared memory/message queue
  Box local
  All CLI tasks can be done via API
Generated Low Level Bindings - existing today
  C clients
  Java clients
  Others can be done

## Slide 41: VPP vRouter/vSwitch: Remote Programmability
Linux Host
Kernel
DPDK
VPP App
Data Plane Management Agent
High Level API: An approach
  Data Plane Management Agent
  Speaks low level API to VPP
  Box (or VM or container) local
  Exposes higher level API via some binding
Flexibility:
  VPP does not force a particular Data Plane Management Agent
  VPP does not force only *one* High Level API
  Anybody can bring a Data Plane Management Agent
  High Level API/Data Plane Management Agent
  Match VPP app needs
netconf/yang
REST
Other (BGP)

## Slide 42: Broader Ecosystem

## Slide 43: OpenDaylight Virtual Bridge Domain
Working on installer changes needed to add ODL & VPP as the networking stack for Openstack
Provides a programmable interface to include ‘edge’ network programming into a virtual environment
Allows for multiple data plane forwarders to be active
Integration happening in OpNFV “Fast Data Stacks” project
VPP
OVS
Control Plane
Data Plane
HC
VBD app

## Slide 44: OpNFV FDS: Integrating OpenStack/ODL/fdio
Working on installer changes needed to add ODL & VPP as the networking stack for Openstack
Provides a programmable interface to include ‘edge’ network programming into a virtual environment
Allows for multiple data plane forwarders to be active
Integration happening in OpNFV “Fast Data Stacks” project
VPP
OVS
Control Plane
Data Plane
Openstack
Neutron
ODL
Plugin
HC

## Slide 45: Next Steps – Get Involved
We invite you to Participate in fd.io
Get the Code, Build the Code, Run the Code
Read/Watch the Tutorials
Join the Mailing Lists
Join the IRC Channels
Explore the wiki
Join fd.io as a member
Come to fd.io breakout session at 5pm in Bellevue