## Slide 1: fd.io is the future
Ed Warnicke

## Slide 2: The Future of IO
Fast Data
Fast Innovation
Convergence

## Slide 3: Fd.io Core: VPP – The Future of IO
VPP is a rapid packet processing development platform for highly performing network applications.
It runs on commodity CPUs and leverages DPDK
It creates a vector of packet indices and processes them using a directed graph of nodes – resulting in a highly performant solution.
Runs as a Linux user-space application
Ships as part of both embedded & server products, in volume
Active development since 2002
Network IO
Packet Processing
Data Plane Management Agent
Bare Metal/VM/Container

## Slide 4: VPP in the Overall Stack
Hardware
Application Layer / App Server
VM/VIM Management Systems
Network Controller
Operating Systems
Data Plane Services
Orchestration
Network IO
VPP
Packet Processing

## Slide 5: VPP Feature Summary – Fully Programmable
  14+ MPPS, single core
  Multimillion entry FIBs
  Source RPF
  Thousands of VRFs
  Controlled cross-VRF lookups
  Multipath – ECMP and Unequal Cost
  Multiple million Classifiers –
  Arbitrary N-tuple
  VLAN Support – Single/Double tag
  Counters for everything
  Mandatory Input Checks:
  TTL expiration
  header checksum
  L2 length < IP length
  ARP resolution/snooping
  ARP proxy
  IPv4/IPv6
  IPv4
  GRE, MPLS-GRE, NSH-GRE,
  VXLAN
  IPSEC
  DHCP client/proxy
  CG NAT
  IPv6
  Neighbor discovery
  Router Advertisement
  DHCPv6 Proxy
  L2TPv3
  Segment Routing
  MAP/LW46 – IPv4aas
  iOAM
  MPLS
  MPLS-o-Ethernet –
  Deep label stacks supported
  L2
  VLAN Support
  Single/ Double tag
  L2 forwarding with EFP/BridgeDomain concepts
  VTR – push/pop/Translate (1:1,1:2, 2:1,2:2)
  Mac Learning – default limit of 50k addresses
  Bridging – Split-horizon group support/EFP Filtering
  Proxy Arp
  Arp termination
  IRB – BVI Support with RouterMac assignment
  Flooding
  Input ACLs
  Interface cross-connect
Notes: The input checks included by VPP include mandatory networking checks.
Some solutions today either don’t perform these or don’t have them leading to questionable performance numbers

## Slide 6: Fast Data

## Slide 7: vNet-SLA benchmarking at scale: IPv6 VPP-based vSwitch
Chart: 
| 12 routes | 1k routes | 100k routes | 500k routes | 1M routes | 2M routes
64B | 210 | 210 | 210 | 210 | 210 | 210
IMIX | 160 | 160 | 160 | 160 | 160 | 160
1518B | 39 | 39 | 39 | 39 | 39 | 39
Chart: 
| 12 routes | 1k routes | 100k routes | 500k routes | 1M routes | 2M routes
64B | 108 | 108 | 108 | 108 | 108 | 108
IMIX | 480 | 480 | 480 | 480 | 480 | 480
1518B | 480 | 480 | 480 | 480 | 480 | 480
FD.io VPP data plane throughput not impacted by large size of IPv6 FIB
VPP tested on UCS 4-CPU-socket server with 4 of Intel “Haswell" x86-64 processors E7-8890v3 18C 2.5GHz
24 Cores used – Another 48 cores can be used for other network services!
[Gbps]
Phy-VS-Phy
Zero-packet-loss Throughput for 12 port 40GE, 24 cores, IPv6
[Mpps]
VPP vSwitch IPv4 routed forwarding FIB with 2 milion IPv6 entries 12x40GE (480GE) 64B frames
200Mpps zero frame loss
NIC and PCIe is the limit not VPP
VPP vSwitch IPv4 routed forwarding FIB with 2 milion IPv6 entries
12x40GE (480GE) IMIX frames
480Gbps zero frame loss
“Sky” is the limit not VPP
Zero-packet-loss Throughput for 12 port 40GE, 24 cores, IPv6

## Slide 8
VPP Cores Not Completely Busy
VPP Vectors Have Space For More Services and More Packets!!
PCIe 3.0 and NICs Are The Limit
And How Do We Know This?
Simples – A Well Engineered Telemetry
In Linux and VPP Tells Us So
========
TC5 120ge.vpp.24t24pc.ip4.cop
TC5.0 120ge.2pnic.6nic.rss2.vpp.24t24pc.ip4.cop
d. testcase-vpp-ip4-cop-scale
120ge.2pnic.6nic.rss2.vpp.24t24pc.ip4.2m.cop.2.copip4dst.2k.match.100
64B, 138.000Mpps, 92,736Gbps
IMIX, 40.124832Mpps, 120.000Gbps
1518, 9.752925Mpps, 120.000Gbps
---------------
Thread 1 vpp_wk_0 (lcore 2)
Time 45.1, average vectors/node 23.44, last 128 main loops 1.44 per node 23.00
vector rates in 4.6791e6, out 4.6791e6, drop 0.0000e0, punt 0.0000e0
Name State Calls Vectors Suspends Clocks Vectors/Call
TenGigabitEtherneta/0/1-output active 9003498 211054648 0 1.63e1 23.44
TenGigabitEtherneta/0/1-tx active 9003498 211054648 0 7.94e1 23.44
cop-input active 9003498 211054648 0 2.23e1 23.44
dpdk-input polling 45658750 211054648 0 1.52e2 4.62
ip4-cop-whitelist active 9003498 211054648 0 4.34e1 23.44
ip4-input active 9003498 211054648 0 4.98e1 23.44
ip4-lookup active 9003498 211054648 0 6.25e1 23.44
ip4-rewrite-transit active 9003498 211054648 0 3.43e1 23.44
---------------
Thread 24 vpp_wk_23 (lcore 29)
Time 45.1, average vectors/node 27.04, last 128 main loops 1.75 per node 28.00
vector rates in 4.6791e6, out 4.6791e6, drop 0.0000e0, punt 0.0000e0
Name State Calls Vectors Suspends Clocks Vectors/Call
TenGigabitEthernet88/0/0-outpu active 7805705 211055503 0 1.54e1 27.04
TenGigabitEthernet88/0/0-tx active 7805705 211055503 0 7.75e1 27.04
cop-input active 7805705 211055503 0 2.12e1 27.04
dpdk-input polling 46628961 211055503 0 1.60e2 4.53
ip4-cop-whitelist active 7805705 211055503 0 4.35e1 27.04
ip4-input active 7805705 211055503 0 4.86e1 27.04
ip4-lookup active 7805705 211055503 0 6.02e1 27.04
ip4-rewrite-transit active 7805705 211055503 0 3.36e1 27.04

## Slide 9
VPP Cores Not Completely Busy
VPP Vectors Have Space For More Services and More Packets!!
PCIe 3.0 and NICs Are The Limit
And How Do We Know This?
Simples – A Well Engineered Telemetry
In Linux and VPP Tells Us So
========
TC5 120ge.vpp.24t24pc.ip4.cop
TC5.0 120ge.2pnic.6nic.rss2.vpp.24t24pc.ip4.cop
d. testcase-vpp-ip4-cop-scale
120ge.2pnic.6nic.rss2.vpp.24t24pc.ip4.2m.cop.2.copip4dst.2k.match.100
64B, 138.000Mpps, 92,736Gbps
IMIX, 40.124832Mpps, 120.000Gbps
1518, 9.752925Mpps, 120.000Gbps
---------------
Thread 1 vpp_wk_0 (lcore 2)
Time 45.1, average vectors/node 23.44, last 128 main loops 1.44 per node 23.00
vector rates in 4.6791e6, out 4.6791e6, drop 0.0000e0, punt 0.0000e0
Name State Calls Vectors Suspends Clocks Vectors/Call
TenGigabitEtherneta/0/1-output active 9003498 211054648 0 1.63e1 23.44
TenGigabitEtherneta/0/1-tx active 9003498 211054648 0 7.94e1 23.44
cop-input active 9003498 211054648 0 2.23e1 23.44
dpdk-input polling 45658750 211054648 0 1.52e2 4.62
ip4-cop-whitelist active 9003498 211054648 0 4.34e1 23.44
ip4-input active 9003498 211054648 0 4.98e1 23.44
ip4-lookup active 9003498 211054648 0 6.25e1 23.44
ip4-rewrite-transit active 9003498 211054648 0 3.43e1 23.44
---------------
Thread 24 vpp_wk_23 (lcore 29)
Time 45.1, average vectors/node 27.04, last 128 main loops 1.75 per node 28.00
vector rates in 4.6791e6, out 4.6791e6, drop 0.0000e0, punt 0.0000e0
Name State Calls Vectors Suspends Clocks Vectors/Call
TenGigabitEthernet88/0/0-outpu active 7805705 211055503 0 1.54e1 27.04
TenGigabitEthernet88/0/0-tx active 7805705 211055503 0 7.75e1 27.04
cop-input active 7805705 211055503 0 2.12e1 27.04
dpdk-input polling 46628961 211055503 0 1.60e2 4.53
ip4-cop-whitelist active 7805705 211055503 0 4.35e1 27.04
ip4-input active 7805705 211055503 0 4.86e1 27.04
ip4-lookup active 7805705 211055503 0 6.02e1 27.04
ip4-rewrite-transit active 7805705 211055503 0 3.36e1 27.04
VPP average vector size below shows 23-to-27
This indicates VPP program worker threads are not busy
Busy VPP worker threads should be showing 255
This means that VPP worker threads operate at 10% capacity
It’s like driving 1,000hp car at 100hp power – lots of space
for adding (service) acceleration and (sevice) speed.

## Slide 10
VPP Cores Not Completely Busy
VPP Vectors Have Space For More Services and More Packets!!
PCIe 3.0 and NICs Are The Limit
And How Do We Know This?
Simples – A Well Engineered Telemetry
In Linux and VPP Tells Us So
========
TC5 120ge.vpp.24t24pc.ip4.cop
TC5.0 120ge.2pnic.6nic.rss2.vpp.24t24pc.ip4.cop
d. testcase-vpp-ip4-cop-scale
120ge.2pnic.6nic.rss2.vpp.24t24pc.ip4.2m.cop.2.copip4dst.2k.match.100
64B, 138.000Mpps, 92,736Gbps
IMIX, 40.124832Mpps, 120.000Gbps
1518, 9.752925Mpps, 120.000Gbps
---------------
Thread 1 vpp_wk_0 (lcore 2)
Time 45.1, average vectors/node 23.44, last 128 main loops 1.44 per node 23.00
vector rates in 4.6791e6, out 4.6791e6, drop 0.0000e0, punt 0.0000e0
Name State Calls Vectors Suspends Clocks Vectors/Call
TenGigabitEtherneta/0/1-output active 9003498 211054648 0 1.63e1 23.44
TenGigabitEtherneta/0/1-tx active 9003498 211054648 0 7.94e1 23.44
cop-input active 9003498 211054648 0 2.23e1 23.44
dpdk-input polling 45658750 211054648 0 1.52e2 4.62
ip4-cop-whitelist active 9003498 211054648 0 4.34e1 23.44
ip4-input active 9003498 211054648 0 4.98e1 23.44
ip4-lookup active 9003498 211054648 0 6.25e1 23.44
ip4-rewrite-transit active 9003498 211054648 0 3.43e1 23.44
---------------
Thread 24 vpp_wk_23 (lcore 29)
Time 45.1, average vectors/node 27.04, last 128 main loops 1.75 per node 28.00
vector rates in 4.6791e6, out 4.6791e6, drop 0.0000e0, punt 0.0000e0
Name State Calls Vectors Suspends Clocks Vectors/Call
TenGigabitEthernet88/0/0-outpu active 7805705 211055503 0 1.54e1 27.04
TenGigabitEthernet88/0/0-tx active 7805705 211055503 0 7.75e1 27.04
cop-input active 7805705 211055503 0 2.12e1 27.04
dpdk-input polling 46628961 211055503 0 1.60e2 4.53
ip4-cop-whitelist active 7805705 211055503 0 4.35e1 27.04
ip4-input active 7805705 211055503 0 4.86e1 27.04
ip4-lookup active 7805705 211055503 0 6.02e1 27.04
ip4-rewrite-transit active 7805705 211055503 0 3.36e1 27.04
VPP average vector size below shows 23-to-27
This indicates VPP program worker threads are not busy
Busy VPP worker threads should be showing 255
This means that VPP worker threads operate at 10% capacity
It’s like driving 1,000bhp car at 100bhp power – lots of space
for adding (service) acceleration and (sevice) speed.
VPP is also counting the cycles-per-packet (CPP)
We know exactly what feature, service, packet processing activity is using the CPU cores
We can engineer, we can capacity plan, we can automate service placement
We can scale across many many CPU cores and computers
And AUTOMATE it easily – as it is after all just SOFTWARE

## Slide 11: Fast Innovation

## Slide 12: Fast Innovation - Modularity Enabling Flexible Plugins
Plugins == Subprojects
Plugins can:
  Introduce new graph nodes
  Rearrange packet processing graph
  Can be built independently of VPP source tree
  Can be added at runtime (drop into plugin directory)
  All in user space
Enabling:
  Ability to take advantage of diverse hardware when present
  Support for multiple processor architectures (x86, ARM, PPC)
  Few dependencies on the OS (clib) allowing easier ports to other Oses/Env
ethernet-input
ip6-input
ip4input
mpls-ethernet-input
arp-input
llc-input
…
ip6-lookup
ip6-rewrite-transmit
ip6-local
…
Packet vector
Plug-in to create new nodes
Custom-A
Custom-B
Plug-in to enable new HW input Nodes

## Slide 13: Convergence

## Slide 14: Fast Data Scope
Fast Data Scope:
    IO
      Hardware/vHardware <-> cores/threads
  Processing
    Classify
    Transform
    Prioritize
    Forward
    Terminate
  Management Agents
    Control/manage IO/Processing
IO
Processing
Management Agent
Bare Metal/VM/Container

## Slide 15: Next Steps – Get Involved
We invite you to Participate in fd.io
Attend “fd.io Intro” talk Wed 4:10-4:50pm in Grand Ballroom B
Attend “fd.io Meetup” Wed 5:00pm in Napa
Attend Packet Processed Storage in a Software Defined World Thu 3:15pm in Grand Ballroom F
Register for fd.io Training/Hackfest April 4-7, 2016 in Santa Clara
Get the Code, Build the Code, Run the Code
Read/Watch the Tutorials
Join the Mailing Lists
Join the IRC Channels
Explore the wiki