## Slide 1: fd.io Intro
Ed Warnicke

## Slide 2: Evolution of Programmable Networking
Many industries are transitioning to a more dynamic model to deliver network services
The great unsolved problem is how to deliver network services in this more dynamic environment
Inordinate attention has been focused on the non-local network control plane (controllers)
  Necessary, but insufficient
There is a giant gap in the capabilities that foster delivery of dynamic Data Plane Services
Programmable Data Plane
CLOUD
NFV
SDN

## Slide 3: Introducing Fast Data: fd.io
New project in Linux Foundation
  Multi-party
  Multi-project
What does multi-party mean?
  Multiple members - Open to all
What does multi-project mean?
  Multiple subprojects
  Subproject autonomy
  Cross project synergy
  Open to new subprojects
  Anyone can propose a subproject
  Allows for innovation
Create a Platform that enables Data Plane Services that are:
  Highly performant
  Modular and extensible
  Open source
  Interoperable
  Multi-Vendor
Platform fosters innovation and synergistic interoperability between Data Plane Services
Source of Continuous Integration resources for Data Plane services based on the Consortium’s project/subprojects
Meet the functionality needs of developers, deployers, datacenter operators
fd.io Charter

## Slide 4: Fast Data Scope
Fast Data Scope:
    IO
      Hardware/vHardware <-> cores/threads
  Processing
    Classify
    Transform
    Prioritize
    Forward
    Terminate
  Management Agents
    Control/manage IO/Processing
IO
Processing
Management Agent
Bare Metal/VM/Container

## Slide 5: Fd.io Members

## Slide 6: Fd.io Projects
Network IO
Packet Processing
VPP
Management Agent
NSH_SFC
ONE
VPP Sandbox
TLDK
Honeycomb
Testing/Performance/Support
CSIT
Legend:
- New Projects
- Core Projects
deb_dpdk

## Slide 7: Governance – At a Glance
Anyone May Participate – Not just members
  Anyone can contribute code
  Anyone can rise to being a committer via meritocracy
  Anyone can propose a subproject
Subprojects:
  Composed of the committers to that subproject – those who can merge code
  Responsible for sub project oversight and autonomous releases
  Make technical decisions for that subproject by consensus, or failing that, majority vote.
Technical Steering Committee
  Fosters collaboration among subprojects, but is not involved in day to day management of sub-projects
  Approves new subprojects, sets development process guidelines for the community, sets release guidelines for multi-project or simultaneous releases, etc.
  Initial TSC will be seeded with representatives from Platinum Membership and core project PTLs with the goal of replacing representatives with Project Leads after the first year
Governing Board will Oversee Business Decision Making
  Set Scope and Policy of Consortium
  Composed of Platinum member appointees, elected Gold, Silver, and Committer member representatives
  Examples of business needs include: budgeting, planning for large meetings (e.g. a Summit, Hackfest), marketing, websites, developer infrastructure, test infrastructure, etc.

## Slide 8: VPP: Vector Packet Processing

## Slide 9: Introducing Vector Packet Processor - VPP
VPP is a rapid packet processing development platform for highly performing network applications.
It runs on commodity CPUs and leverages DPDK
It creates a vector of packet indices and processes them using a directed graph of nodes – resulting in a highly performant solution.
Runs as a Linux user-space application
Ships as part of both embedded & server products, in volume
Active development since 2002
Network IO
Packet Processing
Data Plane Management Agent
Bare Metal/VM/Container

## Slide 10: VPP Architecture - Modularity Enabling Flexible Plugins
Plugins == Subprojects
Plugins can:
  Introduce new graph nodes
  Rearrange packet processing graph
  Can be built independently of VPP source tree
  Can be added at runtime (drop into plugin directory)
  All in user space
Enabling:
  Ability to take advantage of diverse hardware when present
  Support for multiple processor architectures (x86, ARM, PPC)
  Few dependencies on the OS (clib) allowing easier ports to other Oses/Env
ethernet-input
ip6-input
ip4input
mpls-ethernet-input
arp-input
llc-input
…
ip6-lookup
ip6-rewrite-transmit
ip6-local
…
Packet vector
Plug-in to create new nodes
Custom-A
Custom-B
Plug-in to enable new HW input Nodes

## Slide 11: VPP Feature Summary at launch 2016-02-11
  14+ MPPS, single core
  Multimillion entry FIBs
  Source RPF
  Thousands of VRFs
  Controlled cross-VRF lookups
  Multipath – ECMP and Unequal Cost
  Multiple million Classifiers –
  Arbitrary N-tuple
  VLAN Support – Single/Double tag
  Counters for everything
  Mandatory Input Checks:
  TTL expiration
  header checksum
  L2 length < IP length
  ARP resolution/snooping
  ARP proxy
  IPv4/IPv6
  IPv4
  GRE, MPLS-GRE, NSH-GRE,
  VXLAN
  IPSEC
  DHCP client/proxy
  CG NAT
  IPv6
  Neighbor discovery
  Router Advertisement
  DHCPv6 Proxy
  L2TPv3
  Segment Routing
  MAP/LW46 – IPv4aas
  iOAM
  MPLS
  MPLS-o-Ethernet –
  Deep label stacks supported
  L2
  VLAN Support
  Single/ Double tag
  L2 forwarding with EFP/BridgeDomain concepts
  VTR – push/pop/Translate (1:1,1:2, 2:1,2:2)
  Mac Learning – default limit of 50k addresses
  Bridging – Split-horizon group support/EFP Filtering
  Proxy Arp
  Arp termination
  IRB – BVI Support with RouterMac assignment
  Flooding
  Input ACLs
  Interface cross-connect
Notes: The input checks included by VPP include mandatory networking checks.
Some solutions today either don’t perform these or don’t have them leading to questionable performance numbers

## Slide 12: Contributor/Committer Diversity
Universitat Politècnica de Catalunya (UPC)

## Slide 13: VPP 16.06 Release
Released 2016-06-17
Enhanced Switching & Routing
  IPv6 Segment Routing multicast support
  LISP xTR support
  VXLAN over IPv6 underlay
  per interface whitelists
  shared adjacencies in FIB
New and improved interface support
  jumbo frame support for vhost-user
  Netmap interface support
  AF_Packet interface support
Expanded and improved programmability
  Python API bindings
  Enhanced JVPP Java API bindings
  Enhanced debugging cli
Expanded Hardware and Software Support
  Support for ARM 32 targets
  Support for Raspberry Pi
  Support for DPDK 16.04

## Slide 14: Upcoming: VPP 16.09 Release
Release Planned: 2016-09-14
Enhanced LISP support for
  L2 overlays
  Multitenancy
  Multihoming
  Re-encapsulating Tunnel Routers (RTR) support
  Map-Resolver failover algorithm
New plugins for
  SNAT
  MagLev-like Load
  Identifier Locator Addressing
  NSH SFC SFF’s & NSH Proxy
High performance port range ingress filtering
Dynamically ordered subgraphs
  Allows registration of node ‘before’ another node

## Slide 15
VPP technology in a nutshell
VPP data plane throughput not impacted by large FIB size
OVSDPDK data plane throughput heavily impacted by FIB size
VPP and OVSDPDK tested on Haswell x86 platform with E5-2698v3 2x16C 2.3GHz (Ubuntu 14.04 trusty)
Chart: 
| 2 MACs | 2k MACs | 20k MACs
OVSDPDK | 20 | 4 | 0.6
VPP | 20 | 20 | 20
NDR rates for 2p10GE, 1 core, L2 NIC-to-NIC
[IMIX Gbps]
Chart: 
| 12 routes | 1k routes | 100k routes | 500k routes | 1M routes | 2M routes
OVSDPDK | 120 | 48 | 3.6 | 0 | 0 | 0
VPP | 120 | 120 | 120 | 120 | 120 | 120
NDR rates for 12 port 10GE, 12 cores, IPv4
[IMIX Gbps]
not tested

## Slide 16: vNet-SLA benchmarking at scale: IPv6 VPP-based vSwitch
Chart: 
| 12 routes | 1k routes | 100k routes | 500k routes | 1M routes | 2M routes
64B | 210 | 210 | 210 | 210 | 210 | 210
IMIX | 160 | 160 | 160 | 160 | 160 | 160
1518B | 39 | 39 | 39 | 39 | 39 | 39
Chart: 
| 12 routes | 1k routes | 100k routes | 500k routes | 1M routes | 2M routes
64B | 108 | 108 | 108 | 108 | 108 | 108
IMIX | 480 | 480 | 480 | 480 | 480 | 480
1518B | 480 | 480 | 480 | 480 | 480 | 480
FD.io VPP data plane throughput not impacted by large size of IPv6 FIB
VPP tested on UCS 4-CPU-socket server with 4 of Intel “Haswell" x86-64 processors E7-8890v3 18C 2.5GHz
24 Cores used – Another 48 cores can be used for other network services!
[Gbps]
Phy-VS-Phy
Zero-packet-loss Throughput for 12 port 40GE, 24 cores, IPv6
[Mpps]
VPP vSwitch IPv4 routed forwarding FIB with 2 milion IPv6 entries 12x40GE (480GE) 64B frames
200Mpps zero frame loss
NIC and PCIe is the limit not VPP
VPP vSwitch IPv4 routed forwarding FIB with 2 milion IPv6 entries
12x40GE (480GE) IMIX frames
480Gbps zero frame loss
“Sky” is the limit not VPP
Zero-packet-loss Throughput for 12 port 40GE, 24 cores, IPv6

## Slide 17: vNet benchmarking at scale: IPv4+SEcurity
FD.io VPP data plane throughput not impacted by large size of IPv4 FIB
VPP tested on UCS 4-CPU server with 4x Intel E7-8890v3 (18C 2.5GHz)
36 Core used – NIC RSS=2 to drive NIC performance, VPP cores not busy!
Another 36 cores available for other services!
Zero-Packet-Loss Throughput for 18 port 40GE, 36 cores, IPv4
64B => 238 Mpps
NIC and PCIe is the limit not VPP
IMIX => 342 Gbps
1518B => 462 Gbps
“Sky” is the limit not VPP
VPP vSwitch IPv4 rtd fwding, FIB up to 8M IPv4, 2k white-list
Zero Packet Loss Measurements
Chart: 
| 1k routes | 500k routes | 1M routes | 2M routes | 4M routes | 8M routes
64B | 199.58 | 199.58 | 199.58 | 199.58 | 199.58 | 199.58
IMIX | 342 | 342 | 342 | 342 | 342 | 342
1518B | 462 | 462 | 462 | 462 | 462 | 462
[Gbps]
That is Right – No Impact on IMIX and 1518B Performance
Chart: 
| 1k routes | 500k routes | 1M routes | 2M routes | 4M routes | 8M routes
64B | 297 | 297 | 297 | 297 | 297 | 297
IMIX | 160 | 160 | 160 | 160 | 160 | 160
1518B | 39 | 39 | 39 | 39 | 39 | 39
[Mpps]

## Slide 18
VPP Cores Not Completely Busy
VPP Vectors Have Space For More Services and More Packets!!
PCIe 3.0 and NICs Are The Limit
And How Do We Know This?
Simples – A Well Engineered Telemetry
In Linux and VPP Tells Us So
========
TC5 120ge.vpp.24t24pc.ip4.cop
TC5.0 120ge.2pnic.6nic.rss2.vpp.24t24pc.ip4.cop
d. testcase-vpp-ip4-cop-scale
120ge.2pnic.6nic.rss2.vpp.24t24pc.ip4.2m.cop.2.copip4dst.2k.match.100
64B, 138.000Mpps, 92,736Gbps
IMIX, 40.124832Mpps, 120.000Gbps
1518, 9.752925Mpps, 120.000Gbps
---------------
Thread 1 vpp_wk_0 (lcore 2)
Time 45.1, average vectors/node 23.44, last 128 main loops 1.44 per node 23.00
vector rates in 4.6791e6, out 4.6791e6, drop 0.0000e0, punt 0.0000e0
Name State Calls Vectors Suspends Clocks Vectors/Call
TenGigabitEtherneta/0/1-output active 9003498 211054648 0 1.63e1 23.44
TenGigabitEtherneta/0/1-tx active 9003498 211054648 0 7.94e1 23.44
cop-input active 9003498 211054648 0 2.23e1 23.44
dpdk-input polling 45658750 211054648 0 1.52e2 4.62
ip4-cop-whitelist active 9003498 211054648 0 4.34e1 23.44
ip4-input active 9003498 211054648 0 4.98e1 23.44
ip4-lookup active 9003498 211054648 0 6.25e1 23.44
ip4-rewrite-transit active 9003498 211054648 0 3.43e1 23.44
---------------
Thread 24 vpp_wk_23 (lcore 29)
Time 45.1, average vectors/node 27.04, last 128 main loops 1.75 per node 28.00
vector rates in 4.6791e6, out 4.6791e6, drop 0.0000e0, punt 0.0000e0
Name State Calls Vectors Suspends Clocks Vectors/Call
TenGigabitEthernet88/0/0-outpu active 7805705 211055503 0 1.54e1 27.04
TenGigabitEthernet88/0/0-tx active 7805705 211055503 0 7.75e1 27.04
cop-input active 7805705 211055503 0 2.12e1 27.04
dpdk-input polling 46628961 211055503 0 1.60e2 4.53
ip4-cop-whitelist active 7805705 211055503 0 4.35e1 27.04
ip4-input active 7805705 211055503 0 4.86e1 27.04
ip4-lookup active 7805705 211055503 0 6.02e1 27.04
ip4-rewrite-transit active 7805705 211055503 0 3.36e1 27.04

## Slide 19
VPP Cores Not Completely Busy
VPP Vectors Have Space For More Services and More Packets!!
PCIe 3.0 and NICs Are The Limit
And How Do We Know This?
Simple – A Well Engineered Telemetry
In Linux and VPP Tells Us So
========
TC5 120ge.vpp.24t24pc.ip4.cop
TC5.0 120ge.2pnic.6nic.rss2.vpp.24t24pc.ip4.cop
d. testcase-vpp-ip4-cop-scale
120ge.2pnic.6nic.rss2.vpp.24t24pc.ip4.2m.cop.2.copip4dst.2k.match.100
64B, 138.000Mpps, 92,736Gbps
IMIX, 40.124832Mpps, 120.000Gbps
1518, 9.752925Mpps, 120.000Gbps
---------------
Thread 1 vpp_wk_0 (lcore 2)
Time 45.1, average vectors/node 23.44, last 128 main loops 1.44 per node 23.00
vector rates in 4.6791e6, out 4.6791e6, drop 0.0000e0, punt 0.0000e0
Name State Calls Vectors Suspends Clocks Vectors/Call
TenGigabitEtherneta/0/1-output active 9003498 211054648 0 1.63e1 23.44
TenGigabitEtherneta/0/1-tx active 9003498 211054648 0 7.94e1 23.44
cop-input active 9003498 211054648 0 2.23e1 23.44
dpdk-input polling 45658750 211054648 0 1.52e2 4.62
ip4-cop-whitelist active 9003498 211054648 0 4.34e1 23.44
ip4-input active 9003498 211054648 0 4.98e1 23.44
ip4-lookup active 9003498 211054648 0 6.25e1 23.44
ip4-rewrite-transit active 9003498 211054648 0 3.43e1 23.44
---------------
Thread 24 vpp_wk_23 (lcore 29)
Time 45.1, average vectors/node 27.04, last 128 main loops 1.75 per node 28.00
vector rates in 4.6791e6, out 4.6791e6, drop 0.0000e0, punt 0.0000e0
Name State Calls Vectors Suspends Clocks Vectors/Call
TenGigabitEthernet88/0/0-outpu active 7805705 211055503 0 1.54e1 27.04
TenGigabitEthernet88/0/0-tx active 7805705 211055503 0 7.75e1 27.04
cop-input active 7805705 211055503 0 2.12e1 27.04
dpdk-input polling 46628961 211055503 0 1.60e2 4.53
ip4-cop-whitelist active 7805705 211055503 0 4.35e1 27.04
ip4-input active 7805705 211055503 0 4.86e1 27.04
ip4-lookup active 7805705 211055503 0 6.02e1 27.04
ip4-rewrite-transit active 7805705 211055503 0 3.36e1 27.04
VPP average vector size below shows 23-to-27
This indicates VPP program worker threads are not busy
Busy VPP worker threads should be showing 255
This means that VPP worker threads operate at 10% capacity
It’s like driving 1,000hp car at 100hp power – lots of space
for adding (service) acceleration and (sevice) speed.

## Slide 20
VPP Cores Not Completely Busy
VPP Vectors Have Space For More Services and More Packets!!
PCIe 3.0 and NICs Are The Limit
And How Do We Know This?
Simples – A Well Engineered Telemetry
In Linux and VPP Tells Us So
========
TC5 120ge.vpp.24t24pc.ip4.cop
TC5.0 120ge.2pnic.6nic.rss2.vpp.24t24pc.ip4.cop
d. testcase-vpp-ip4-cop-scale
120ge.2pnic.6nic.rss2.vpp.24t24pc.ip4.2m.cop.2.copip4dst.2k.match.100
64B, 138.000Mpps, 92,736Gbps
IMIX, 40.124832Mpps, 120.000Gbps
1518, 9.752925Mpps, 120.000Gbps
---------------
Thread 1 vpp_wk_0 (lcore 2)
Time 45.1, average vectors/node 23.44, last 128 main loops 1.44 per node 23.00
vector rates in 4.6791e6, out 4.6791e6, drop 0.0000e0, punt 0.0000e0
Name State Calls Vectors Suspends Clocks Vectors/Call
TenGigabitEtherneta/0/1-output active 9003498 211054648 0 1.63e1 23.44
TenGigabitEtherneta/0/1-tx active 9003498 211054648 0 7.94e1 23.44
cop-input active 9003498 211054648 0 2.23e1 23.44
dpdk-input polling 45658750 211054648 0 1.52e2 4.62
ip4-cop-whitelist active 9003498 211054648 0 4.34e1 23.44
ip4-input active 9003498 211054648 0 4.98e1 23.44
ip4-lookup active 9003498 211054648 0 6.25e1 23.44
ip4-rewrite-transit active 9003498 211054648 0 3.43e1 23.44
---------------
Thread 24 vpp_wk_23 (lcore 29)
Time 45.1, average vectors/node 27.04, last 128 main loops 1.75 per node 28.00
vector rates in 4.6791e6, out 4.6791e6, drop 0.0000e0, punt 0.0000e0
Name State Calls Vectors Suspends Clocks Vectors/Call
TenGigabitEthernet88/0/0-outpu active 7805705 211055503 0 1.54e1 27.04
TenGigabitEthernet88/0/0-tx active 7805705 211055503 0 7.75e1 27.04
cop-input active 7805705 211055503 0 2.12e1 27.04
dpdk-input polling 46628961 211055503 0 1.60e2 4.53
ip4-cop-whitelist active 7805705 211055503 0 4.35e1 27.04
ip4-input active 7805705 211055503 0 4.86e1 27.04
ip4-lookup active 7805705 211055503 0 6.02e1 27.04
ip4-rewrite-transit active 7805705 211055503 0 3.36e1 27.04
VPP average vector size below shows 23-to-27
This indicates VPP program worker threads are not busy
Busy VPP worker threads should be showing 255
This means that VPP worker threads operate at 10% capacity
It’s like driving 1,000bhp car at 100bhp power – lots of space
for adding (service) acceleration and (sevice) speed.
VPP is also counting the cycles-per-packet (CPP)
We know exactly what feature, service, packet processing activity is using the CPU cores
We can engineer, we can capacity plan, we can automate service placement
We can scale across many many CPU cores and computers
And AUTOMATE it easily – as it is after all just SOFTWARE

## Slide 21
Compute Node Hardware | Cisco UCS C460 M4
Chipset | Intel® C610 series chipset
CPU | 4 x Intel® Xeon® Processor E7-8890 v3 (18 cores, 2.5GHz, 45MB Cache)
Memory | 2133 MHz, 512 GB Total
NICs | 9 x 2p40GE Intel XL710 18 x 40GE = 720GE !!
Compute Node Software | Version
Host Operating System | Ubuntu 14.04.3 LTS Kernel version: 3.13.0-63-generic
DPDK | DPDK 2.2.0
FD.io VPP | vpp v1.0.0-174~g57a90e5
The Fast Data Project (FD.io)
18 x 7.7trillion packets forwarded.
Max Packet Delay <3.5 msec incl. the outliers!!
The Soak Test Proof:
Low long-term max packet delay with FD.io VPP
>>120 msec long-term max packet delay measured by others for other vSwitches
But it is just not not there with VPP and stock Ubuntu 14.04 (no Linux tuning!)
ONE MORE THING – THE LONG TERM MAX DELAY
Min Packet Delay 7..10 usec, Avg Packet Delay <23 usec.
Max
Delay
Min
Delay
Avg
Delay

## Slide 22: Implementation Example: VPP as a vRouter/vSwitch
Out of the box vSwitch/vRouter
  Including CLI
Switching
  Can Create
  Bridge Domains
  Ports (including tunnel ports)
  Connect ports to bridge domains
  Program ARP termination
  etc
Routing
  Can Create
  VRFs - thousands
  Routes - millions
Linux Host
Kernel
DPDK
VPP App
Switch-1
Switch-2
VRF-1
VRF-2

## Slide 23: VPP vRouter/vSwitch: Local Programmability
Linux Host
Kernel
DPDK
VPP App
External App
Low Level API
  Complete
  Feature Rich
  High Performance
    Example: 900k routes/s
  Shared memory/message queue
  Box local
  All CLI tasks can be done via API
Generated Low Level Bindings - existing today
  C clients
  Java clients
  Others can be done

## Slide 24: VPP vRouter/vSwitch: Remote Programmability
Linux Host
Kernel
DPDK
VPP App
Data Plane Management Agent
High Level API: An approach
  Data Plane Management Agent
  Speaks low level API to VPP
  Box (or VM or container) local
  Exposes higher level API via some binding
Flexibility:
  VPP does not force a particular Data Plane Management Agent
  VPP does not force only *one* High Level API
  Anybody can bring a Data Plane Management Agent
  High Level API/Data Plane Management Agent
  Match VPP app needs
netconf/yang
REST
Other (BGP)

## Slide 25: Honeycomb

## Slide 26: Fd.io Projects
Network IO
Packet Processing
VPP
Dataplane Management Agents
NSH_SFC
ONE
VPP Sandbox
TLDK
Testing/Performance
Legend:
- New Projects
- Core Projects
CSIT
Honeycomb

## Slide 27: Honeycomb Data Plane Management Agent
Linux Host
Kernel
DPDK
VPP App
ODL Honeycomb Agent
High Level API: An Approach
  Yang Models via netconf/restconf
  Box local ODL instance (Honeycomb) using low level API over generated Java Bindings to talk to VPP App, and exposing yang models over netconf/restconf NB
  Initial example: Bridge Domains
netconf/yang
REST
Other (BGP)

## Slide 28: CSIT: Continuous System & Integration Testing

## Slide 29: Fd.io Projects
Network IO
Packet Processing
VPP
Dataplane Management Agents
NSH_SFC
ONE
VPP Sandbox
TLDK
Honeycomb
Testing/Performance
Legend:
- New Projects
- Core Projects
deb_dpdk
CSIT

## Slide 30: FD.io Continuous Performance Lab a.k.a. The CSIT Project (Continuous System Integration and Testing)
What it is all about – CSIT aspirations
  FD.io VPP benchmarking
    VPP functionality per specifications (RFCs1)
    VPP performance and efficiency (PPS2, CPP3) – Throughput Non-Drop Rate (Bandwidth, PPS), Delay
      Network Data plane, Network Control Plane, Management Plane Interactions (memory leaks!)
    Performance baseline references for HW + SW stack (PPS2, CPP3)
    Range of deterministic operation for HW + SW stack (SLA4)
  Provide testing platform and tools to FD.io VPP dev and usr community
    Automated functional and performance tests
    Automated telemetry feedback with conformance, performance and efficiency metrics
  Help to drive good practice and engineering discipline into FD.io VPP dev community
    Drive innovative optimizations into the source code – verify they work
    Enable innovative functional, performance and efficiency additions & extensions
    Make progress faster
    Prevent unnecessary code “harm”
Legend:
1 RFC – Request For Comments – IETF Specs basically
2 PPS – Packets Per Second
3 CPP – Cycles Per Packet (metric of packet processing efficiency)
4 SLA – Service Level Agreement
Submit Patch
Automated Testing
Deploy
Develop

## Slide 31: CSIT Platform System Design in a Nutshell

## Slide 32: Broader Ecosystem

## Slide 33: OpenDaylight Virtual Bridge Domain
OpenDaylight Virtual Bridge Domain (VBD) app allows users to program distributed bridge domain in the controller
VBD app speaks Netconf/Yang to Honeycomb dataplane management agent on box with vpp dataplane using a *semantic* model (not flow based)
Honeycomb agent speaks low level api to vpp expressing *semantic concepts*
VPP
Control Plane
Data Plane
Honeycomb
VBD app
Netconf/Yang

## Slide 34: OpenDaylight Lispflowmapping
LISP (Locator Identifier Seperation) allows the construction of dynamic tunnels over a wide variety of encapsulations:
  LISP encap
  VXLAN gpe
  GRE
  etc
VPP dataplane acquires information about encapsulations dynamically via LISP mapping protocol from mapping server
VPP dataplane informs LISP mapping server of new endpoints dynamically
Go to Programmable Overlays with VPP
  Wed (today): 4:35-5:25pm today in ‘Marine’
VPP
Control Plane
Data Plane
Lispflowmapping app
LISP Mapping Protocol

## Slide 35: OpenDaylight SFC
SFC (Service Function Chaining) moves traffic along a ‘service function chain’ in the network
Service function chain is programmed in controller
SFC app configures service function forwarders in honeycomb agent
Honeycomb agent programs vpp with low level API.
VPP
Control Plane
Data Plane
SFC
Netconf/yang
Honeycomb

## Slide 36: OpNFV FDS: Integrating OpenStack/ODL/fdio
End to end support from neutron via ODL to VPP
Connects vpp to vhost-user interfaces to VMs
Integration happening in OpNFV “Fast Data Stacks” project
  Targeting Colorado OpNFV Release
  Apex installer support
VPP
Control Plane
Data Plane
Openstack
Neutron
ODL
Plugin
Honeycomb

## Slide 37: OpNFV FDS: Direct OpenStack/fdio
Direct Neutron plugin for fd.io
Uses low level vpp api python bindings
Connects vpp to vhost-user interfaces to VMs
Integration happening in OpNFV “Fast Data Stacks” project
  Targeting Colorado OpNFV Release
  Apex installer support
VPP
Data Plane
Openstack
Neutron
Fd.io
Plugin

## Slide 38: POC: Calico & Contiv Integration
Demo of VPP as dataplane for Calico
Calico or Contiv agent uses vpp low level api to control vpp
Tuntap interface between vpp and container
  Using network namespaces
VPP
container
kernel
Calic or Contiv Agent
AF_PACKET int/netns
Low level vpp api

## Slide 39: Future: TLDK: Host Stack
Linux Host
Kernel
DPDK
VPP
Linux Process 1
TLDK has just started
  Building transport layer libraries
    TCP/UDP/etc
  Building VPP plugin to provide user space host stack
  Building Netlink Agent+LDPRELOAD
    Allows Linux Process to use userspace hoststack instead of kernel host stack without modifying the app
  Any process or group of processes could get their own v6 address
  Bypass Kernel Network Stack
NetlinkAgent+LDPRELOAD
Linux Process 2
Linux Process 3
Host Stack Plugin
Userspace interface 1
Userspace interface 2

## Slide 40: Next Steps – Get Involved
We invite you to Participate in fd.io
Get the Code, Build the Code, Run the Code
Try the vpp user demo
Install vpp from binary packages (yum/apt)
Install Honeycomb from binary packages
Read/Watch the Tutorials
Join the Mailing Lists
Join the IRC Channels
Explore the wiki
Join fd.io as a member
Go to Programmable Overlays with VPP
  Wed (today): 4:35-5:25pm today in ‘Marine’