## Slide 1: Fd.io DPDK vSwitch mini-summit
Discussion of vSwitches, VSwitch requirements and how this fits into the cloud
Christopher Price (Ericsson), Mark D Gray (Intel), Thomas F Herbert (Red Hat)

## Slide 2: Chris Price -- Introduction Mark D. Gray vSwitch Requirements Thomas F. Herbert -- OVS and fd.io

## Slide 3: Fd.io why another vswitch?

## Slide 4: Other vswitches
Competition is good, so it’s good we have an alternative to OVS right?
  http://www.openswitch.net/
  http://www.opendataplane.org/
  http://www.projectfloodlight.org/indigo/
  https://opennetlinux.org
  https://azure.github.io/SONiC/
  …

## Slide 5: So… Let’s start another one!
But Why?
The best in breed vSwitches:
  Already have fast-path processing
  Already have advanced classification
  Already have multithreading
  Are monolithic purpose built…
  Have sequential packet pipelines...
  Are feature constrained...

## Slide 6: Comes integrated in opnfv
FDS – fast data stacks
  Delivers an integrated openstack deployment using fd.io
  Provides an “in context” apples to apples comparison with other solutions
  Establishes a VNFi platform for advanced VPP application development and deployment
Available in the Colorado release this Autumn
  https://wiki.opnfv.org/display/fds

## Slide 7: Other requirements
Stateful ACL
SFC/NSH
Tunnelling
Performance
multiqueue vhost
OTHERS?
vhost reconnect
Service Assurance
Notes: Openstack, the cloud and NFV impose a number of requirements on virtual switches used in the NFVI

## Slide 8: Other requirements
Stateful ACL
SFC/NSH
Tunnelling
Performance
multiqueue vhost
OTHERS?
vhost reconnect
Service Assurance
Notes: Openstack, the cloud and NFV impose a number of requirements on virtual switches used in the NFVI

## Slide 9: Service Function Chaining
Client
A
SF A
Server B
Client
B
Server A
SF B
SF C
SF D
SFC
Service Path 1
Notes: Service Function Chaining provides the ability to define an ordered list of a network services (e.g. firewalls, NAT, QoS). These service are then "stitched" together in the network to create a service chain.

## Slide 10: Service Function Chaining
Client
A
SF A
Server B
Client
B
Server A
SF B
SF C
SF D
SFC
Service Path 2

## Slide 11: Service Function Chaining
Client
A
SF A
Server B
Client
B
Server A
SF B
SF C
SF D
SFC
Service Path 3

## Slide 12: Network Service Header (NSH)
Header Format
Reduces lookup cost by avoiding costly classifications
Requires transport protocol
    VxLAN-GPE
    Ethernet
May require tunnel termination inside the virtual machine
SFF/Virtual Switch
SF A
SF B
Can provide a mechanism to share of metadata between service functions using “Type 2 metadata “
Inner Frame
NSH
VxLAN-GPE
Inner Frame
NSH
VxLAN-GPE
Notes: NSH is a header that can be inserted into packets to realise service function paths.

## Slide 13: Stateful ACL
VM Instance
PORT
Security groups and security group rules allows administrators and tenants the ability to specify the type of traffic and direction (ingress/egress) that is allowed to pass through a port.
Security groups require stateful ACLs which allow related flows for allowed flows
Network
Security Group
direction = ingress
protocol = tcp
remote ip = 1.2.3.4
remote port = 80
Allow
Related Flow
protocol = tcp
dest IP = 5.5.5.5
dest port = 12345
source IP = 1.2.3.4
source port = 80
Allow Flow
protocol = tcp
dest IP = 1.2.3.4
dest port = 80
source IP = 5.5.5.5
source port = 12345
Notes: Stateful classification is required in order to implement security groups

## Slide 14: Multiqueue Vhost
VM
vNic
vSwitch
PMD 0
NIC
Rx
Tx
Rx
Tx
Rx
Tx
Rx
Tx
Q3
Q2
Q1
Q0
Rx
Tx
Rx
Tx
Rx
Tx
Rx
Tx
Q3
Q2
Q1
Q0
PMD 1
PMD 2
PMD 3
Guest
Host
Hardware
Improves the throughput into virtual machines by providing way to scale out performance when using vhost ports.
Notes: Multiqueue vhost is required in order to get better performance into a virtual machine

## Slide 15: Vhost reconnect
Qemu
vSwitch
Unix Domain Socket
vHost
User
Guest
OS
vNic
Rx
Tx
Reconnect
Ensures virtual machine network connectivity is maintained even across restarts of the virtual switch.
Notes: Connectivity between VM and Vswitch must be maintained between reboots of the virtual machine and the vswitch.

## Slide 16: Network Service Assurance
vSwitch
Qemu
Guest Operating System
Provide differentiated classes of service for high priority dataflows ensuring end-to-end Quality of Service SLAs are met. One example shown here.
Performance monitoring at the network level.
Reactive and Proactive responses to faults
vNic
vNic
Classify
Q
Application
Q
Low Priority
Traffic (e.g. bulk
data transfer)
High Priority Traffic (e.g. voice)

## Slide 17: Open vSwitch dataplane FD.IO/VPP
Open Flow Protocol matches and actions
Fast Path -- Linux Kernel Module
or
Accelerated
Fast Path Exact Match Cache -- Fastest
About 8K matches using linear search
Misses go to Slower MiniFlow Match -- Slower
Misses go to OFP Match Slowest
VPP fd.io
Graph based vector Processing Engine
Extensible via plugins
Includes complete IPv4 and IPv6 stack
Uses DPDK as packet engine
Being extended for vxLAN VTEP
DPDK

## Slide 18: Open vSwitch control plane differences FD.IO/VPP
Based on Open Flow
System of matches and tables with actions
Supports common packet header fields
Actions
Change fields with some pushes and pops
Generally ODL/Netvirt/OVSDB
Open Stack - Neutron
VPP Plugin API
Restconf
ODL HoneyComb Agent
NetConf
Open Stack Neutron ML2
Management via OFP and OVSDB
Management via Netconf/REST ODL Honecomb Agent

## Slide 19: OVS and FD.IO similarities
DPDK based
Both are virtualized switch fabrics
Implemented in Software on Commodity Processors
Deployable in Compute node
Host to VM uses vhost-user
Container Support is through kernel via TAP

## Slide 20: Open vSwitch Architecture
DPDK User Space Summit 2015 Dublin

## Slide 21: Open vSwitch Architecture
DPDK User Space Summit 2015 Dublin

## Slide 22: Open vSwitch Architecture
DPDK User Space Summit 2015 Dublin

## Slide 23: How VPP Works
Packet Vector is Input to DPDK
Nodes on Graph Pipeline Process Packets According to Registered Dependencies
Additional Plugins can be Introduced to Create New Nodes
Examples of Plugins
NSH and VTEP
Parallelism -- determism in throughput and latency.

## Slide 24: Backup

## Slide 25: What does Fd.io offer?
  14+ MPPS, single core
  Multimillion entry FIBs
  Source RPF
  Thousands of VRFs
  Controlled cross-VRF lookups
  Multipath – ECMP and Unequal Cost
  Multiple million Classifiers –
  Arbitrary N-tuple
  VLAN Support – Single/Double tag
  Counters for everything
  Mandatory Input Checks:
  TTL expiration
  header checksum
  L2 length < IP length
  ARP resolution/snooping
  ARP proxy
  IPv4/IPv6
  IPv4
  GRE, MPLS-GRE, NSH-GRE,
  VXLAN
  IPSEC
  DHCP client/proxy
  CG NAT
  IPv6
  Neighbor discovery
  Router Advertisement
  DHCPv6 Proxy
  L2TPv3
  Segment Routing
  MAP/LW46 – IPv4aas
  iOAM
  MPLS
  MPLS-o-Ethernet –
  Deep label stacks supported
  L2
  VLAN Support
  Single/ Double tag
  L2 forwarding with EFP/BridgeDomain concepts
  VTR – push/pop/Translate (1:1,1:2, 2:1,2:2)
  Mac Learning – default limit of 50k addresses
  Bridging – Split-horizon group support/EFP Filtering
  Proxy Arp
  Arp termination
  IRB – BVI Support with RouterMac assignment
  Flooding
  Input ACLs
  Interface cross-connect

## Slide 26: What does fd.io offer?
Modularity
Plugins == Subprojects
Plugins can:
  Introduce new graph nodes
  Rearrange packet processing graph
  Can be built independently of VPP source tree
  Can be added at runtime (drop into plugin directory)
  All in user space
Enabling:
  Ability to take advantage of diverse hardware when present
  Support for multiple processor architectures (x86, ARM, PPC)
  Few dependencies on the OS (clib) allowing easier ports to other Oses/Env
ethernet-input
ip6-input
ip4input
mpls-ethernet-input
arp-input
llc-input
…
ip6-lookup
ip6-rewrite-transmit
ip6-local
…
Packet vector
Plug-in to create new nodes
Custom-A
Custom-B
Plug-in to enable new HW input Nodes

## Slide 27: Continuous performance lab
Continuous Functional Testing
  VM based virtual testbeds (3-node/3-VM topologies)
  Continuous verification of feature conformance
  Highly parallel test execution
  Membership dues can donate VMs …. to the CPL
Continuous Benchmark Testing
  Server based hardware testbeds (3-node/3-server topologies)
  Continuous integration process with real hardware verification
  Server models, CPU models, NIC models
  Platinum Members can donate hardware to the CPL
Develop
Submit Patch
Automated Testing
Deploy

## Slide 28: Looks pretty good!
VPP technology in a nutshell
VPP data plane throughput not impacted by large FIB size
OVSDPDK data plane throughput heavily impacted by FIB size
VPP and OVSDPDK tested on Haswell x86 platform with E5-2698v3 2x16C 2.3GHz (Ubuntu 14.04 trusty)
NDR rates for 2p10GE, 1 core, L2 NIC-to-NIC
[IMIX Gbps]
NDR rates for 12 port 10GE, 12 cores, IPv4
[IMIX Gbps]
not tested

## Slide 29: Not just another vswitch
VPP is a rapid packet processing development platform for highly performing network applications.
Create a Platform that enables Data Plane Services that are:
  Highly performant
  Modular and extensible
  Open source
  Interoperable
  Multi-Vendor
Platform fosters innovation and synergistic interoperability between Data Plane Services
Source of Continuous Integration resources for Data Plane services based on the Consortium’s project/subprojects
Meet the functionality needs of developers, deployers, datacenter operators
fd.io Charter
Network IO
Packet Processing
Data Plane Management Agent
Bare Metal/VM/Container