## Slide 1: TLDK Transport Layer Development Kit
Keith Wiles
Principal Engineer @ Intel

## Slide 2: Legal Disclaimer
General Disclaimer:
© Copyright 2016 Intel Corporation. All rights reserved. Intel, the Intel logo, Intel Inside, the Intel Inside logo, Intel. Experience What’s Inside are trademarks of Intel. Corporation in the U.S. and/or other countries. *Other names and brands may be claimed as the property of others.
Technology Disclaimer:
Intel technologies’ features and benefits depend on system configuration and may require enabled hardware, software or service activation. Performance varies depending on system configuration. No computer system can be absolutely secure. Check with your system manufacturer or retailer or learn more at [intel.com].
Performance Disclaimers:
Cost reduction scenarios described are intended as examples of how a given Intel- based product, in the specified circumstances and configurations, may affect future costs and provide cost savings. Circumstances will vary. Intel does not guarantee any costs or cost reduction.
Results have been estimated or simulated using internal Intel analysis or architecture simulation or modeling, and provided to you for informational purposes. Any differences in your system hardware, software or configuration may affect your actual performance.

## Slide 3: TLDK (Transport Layer Development Kit)
TLDK is to provide a clean set of ‘C’ libraries to enable network protocol handling at the application layer
TLDK will provide IPv4/v6 and TCP/UDP protocols along with others as required for normal network operation
Goal is to provide a very high performance network stack with termination support for applications using VPP and DPDK
TLDK will provide a set of libraries to allow for applications to build a complete network stack support
  Including a high performance non-socket type application interface
  Including a socket layer for applications linked with the application
  Including a LD_PRELOAD socket layer to run native Linux applications

## Slide 4: TLDK (Transport Layer Development Kit)
TLDK is not a normal network designed stack!
  TLDK has turned the network stack upside down for better performance
Network protocols stack is driven by the application needs
Normal network stack designs drive packet into the protocols, then to the application
  In TLDK the packets are per-filtered to a given DPDK core/thread
  The application then drives the packets into the stack when it needs the data not before
  The design attempts to keep the CPU cache warm and only consume processor cycles when needed
The goal is to move multiple packets thru the stack at a time similar to DPDK and VPP vector like processing of packets to utilize the cache correctly
Normal stacks drive data from the bottom up and TLDK drives the data from the top down
  Vector packet processing method reduces cycle overhead per packet

## Slide 5: TLDK Uses case with VPP
VPP
DPDK
Physical Layer
Application Layer
TLDK:
Handles packet I/O and protocol processing of packets
Application sets up the UDP/TCP protocol contexts and then calls I/O routines in TLDK to start processing packets
VPP Fastpath
Using VPP as the first layer for packet processing before packets are sent to the application layer
Physical Layer:
Ports and other devices like crypto, compression, …
DPDK:
DPDK provides the I/O abstraction to the physical layer for the network devices. The DPDK could be optional here only if some other I/O layer is used.
TLDK
Control or
non-TLDK pkts
TLDK pkts
Control Plane

## Slide 6: TLDK Application Layer break down
VPP
optional
DPDK
Physical Layer
Socket Application
Application Layer:
The application layer utilizes the TLDK library to process packets for UDP and TCP
Purpose Built Application:
A purpose built application is one that uses TLDK APIs directly and is built to use these APIs
Highest performance is expected with this design
BSD Socket Layer:
A standard BSD socket layer for applications using sockets in its design
A lower performance is expected, but allows for current socket type applications to be ported to the system
LD_PRELOAD Socket Layer:
LD_PRELOAD is used to allow a ‘native binary Linux’ application to use the accelerated path of VPP/DPDK
The performance should be a bit better, but does allow these native binary applications to work without any change
TLDK
Control or
non-TLDK pkts
TLDK pkts
BSD Socket layer
LD_PRELOAD
Socket layer
Native Linux Application
Purpose built TLDK Application

## Slide 7: Current Status of TLDK
The project is under the FD.io a Linux Foundation project
  FD.io Wiki Page (https://wiki.fd.io/view/Main_Page)
  TLDK is located at: https://wiki.fd.io/view/TLDK
  Source Code at: git clone https://gerrit.fd.io/r/tldk
Current code base includes an optimized UDP implementation
Currently working on TCP implementation
Each Wednesday at 10am CST is the TLDK community meeting
  Meeting info: https://wiki.fd.io/view/TLDK/Meeting
Additional ideas and contributions welcomed!

## Slide 8: TLDK - Status Update
Thank you for attending, any questions?