## Slide 1: High Speed Solutions in VPP to Accelerate Container Networking: -Howto and Deep Dive
Tan,Jianfeng (jianfeng.tan@intel.com)
Xu,qian (qian.q.xu@intel.com)

## Slide 2: Agenda
Motivations
Solutions introduction – what and howto
  SSVM, Vhost/virtio, Netmap pipes
Solutions comparison
  Performance
  Features…
Summary and next step

## Slide 3: Motivations
  Challenges in container networking
    High performance packet processing
    Linearly scalability
    Flexibility
  Discussions in VPP community
  VPP thread model
    Now, multi threads share the nodes graph
    How to run 3rd party plugins securely?
      Spread nodes into containers
dpdk-input
ethernet-input
ip6-input
ip4-input
arp-input
mpls-ethernet-input
Packet Vector
Pkt-1
Pkt-2
Pkt-n
…
Plugin Node
Container
Cross container IPC.
Container

## Slide 4: What’s SSVM
  SSVM: Structured Shared Virtual memory
    Specified for VPP project
    Shared memory based
queue
Element
pool
Shared memory
Container1
(master)
Container2
(slave)
Only one process
can get the lock

## Slide 5: SSVM Ring Layout and Memory access (1)
elt_idx_0
elt_idx_1
…
elt_idx_a
elt_idx_c
…
elt_idx_n
…
elt_idx_b
…
head
(tx side r, rx side w)
tail
(tx side r, rx side w)
cursize
(race)
type
…
total_len
len
next_idx
data
pad
ssvm_elt_0
ssvm_elt_1
…
ssvm_elt_i
…
ssvm_elt_m
Metadata
(16 B)
(2048 + 128 B)
Queue
elts pool
elt
Queue metadata
This lock can be avoided!

## Slide 6: SSVM Ring Layout and Memory access (2)
  Tx
    SpinLock elt pool to get one elt
    Fill metadata of elt
    Copy data from clib_buf -> elt
    SpinLock Tx queue to set idx
  Rx
    SpinLock Rx queue to get idx
    Copy data from elt -> clib_buf
    Fill metadata of clib_buf
    SpinLock elt pool to return elt
Batching

## Slide 7: What’s Vhost/virtio-user
  As a DPDK virtual device
  Talk to backend by embedded adapter w/o device emulation
  Share PMD with virtio (PCI)
  Single consistent vhost PMD on the backend
  Frontend shares mem with backend

## Slide 8: Vhost/Virtio Ring Layout and Memory Access
  Prepare at virtio side
    Prepare desc table entry
    update avail ring
  Tx at vhost side
    Get avail ring idx and entry
    Locate buf in desc table
    Copy data: vlib_buf (of vhost) -> vlib_buf (of virtio)
    Update used ring entry and idx
  Rx at virtio side
    Get used ring idx and entry
Batching

## Slide 9: What’s Netmap pipes
  A framework for high speed packet I/O
    Netmap
    Netmap/VALE (switch)
    Netmap pipes (p2p communication)

## Slide 10: Netmap Ring Layout and Memory access
  Tx
    Get some slots (tail -> head)
    Copy data: vlib_buf -> netmap_buf
    Update head, cur
    Syscall: tx_sync
  Rx
    Get some slots to consume
    Copy data: from netmap_buf -> vlib_buf
    Syscall: rx_sync
    Update head, cur
SWAP

## Slide 11: An inaccurate summary

## Slide 12: Performance: Test Setup
1. Create Docker images and run containers:
$ docker pull fedora
$ (For netmap, insert netmap kernel module)
$ docker run –v /dev/netmap:/dev/netmap … -v /dev/uio0:/dev/uio0 --privileged --cap-add SYS_ADMIN
$ docker run –v /dev/shm/ssvmtest1:/dev/shm/ssvmtest1 …
$ docker run –v /unix_sock_dir:/unix_sock_dir …
2. Start VPP instance in each container
$ vpp unix {…} ssvm_eth {…} dpdk {…} cpu {…} &
$ vpp unix {…} dpdk {… --extra “--vdev=eth_vhost0,path=…”} cpu {…} &
$ vpp unix {…} dpdk {… --extra “--vdev=virtio_user0,path=…”} cpu {…} &
3. Create devices
$ vppctl create netmap name vale00:vpp0 hw-addr 02:FE:3F:34:15:9B pipe master
4. Start the devices and send the traffic
$ set int state xxx up
$ set int ip address xxx [ip_addr]
$ set interface l2 xconnect xxx yyy
Patches not
upstreamed yet !!!

## Slide 13: Performance
  No difference after pkt size >= 256
  For small pkts, there is room for improvement in ssvm and virtio
Ssvm is not stable.

## Slide 14: Features
 | Offloading | Coupling | Compatibility (w/ container) | Notification/Lock
ssvm | N/A | High coupled with VPP | VPP app | Polling mode; spinlock
Vhost/virtio | TSO, checksum | Decoupled with VPP with Standard spec | DPDK app | Polling mode; lockless
Netmap pipes | N/A | Decoupled with VPP | Pcap app Netmap app | Syscall w/ POSIX poll; Lockless

## Slide 15: Summary and next step
Summary
A survey on running VPP in containers
Analysis on ssvm, virtio_user and netmap pipes
Next step
Continue virtio evolution for containers
Support notification of virtio_user
Virtio 1.1, virtio 1.1, virtio 1.1
Bring best I/O engine for VPP