## Slide 1: TLDK overview
Konstantin Ananyev
05/08/2016

## Slide 2: Legal Disclaimer
General Disclaimer:
© Copyright 2016 Intel Corporation. All rights reserved. Intel, the Intel logo, Intel Inside, the Intel Inside logo, Intel. Experience What’s Inside are trademarks of Intel Corporation in the U.S. and/or other countries. *Other names and brands may be claimed as the property of others.
Technology Disclaimer:
Intel technologies’ features and benefits depend on system configuration and may require enabled hardware, software or service activation. Performance varies depending on system configuration. No computer system can be absolutely secure. Check with your system manufacturer or retailer or learn more at [intel.com].
Performance Disclaimers:
Cost reduction scenarios described are intended as examples of how a given Intel- based product, in the specified circumstances and configurations, may affect future costs and provide cost savings. Circumstances will vary. Intel does not guarantee any costs or cost reduction.
Results have been estimated or simulated using internal Intel analysis or architecture simulation or modeling, and provided to you for informational purposes. Any differences in your system hardware, software or configuration may affect your actual performance.

## Slide 3: Transport Layer Development Kit (TLDK)
Project web-site: https://wiki.fd.io/view/TLDK
The scope of the project:
  implement a set of libraries for L4 protocol processing (UDP, TCP etc.) for both IPv4 and IPv6.
  create VPP graph nodes, plugins, etc. using those libraries to implement a host stack.
  mechanisms (netlink agents, packaging, etc.) necessary to make the resulting host stack easily usable by existing non-vpp aware software.

## Slide 4: TLDK libraries
  The goal is – a lightweight, high performance and easily adaptable implementation for L4(UDP, TCP etc.) protocol processing.
  Built on top of DPDK.
    Use DPDK API/features across the libraries.
    Follow DPDK concepts (process packets in bulks, non blocking API, etc).
  The provided API is not compatible with BSD socket API.
    Though keep similar semantics (whenever possible).
  Not a complete ‘host’ stack.

## Slide 5: Current status
  libtle_udp - implementation of the UDP datagram processing.
    Operates over both IPv4 and IPv6 packets.
  udpfwd - sample app to demonstrate and test libtle_udp usage.
    can do simple send/recv or both over opened udp streams.
    ability to do UDP datagram forwarding between different streams (“UDP proxy”).
    reassemble/fragment IP packets (based on DPDK librte_ip_frag).

## Slide 6: In Development
  TCP processing implementation.
    libtle_tcp.
    sample application.
  libtle_udp/udpfwd enhancements.
    Extra features (RSS/FD HW offloads, etc).

## Slide 7: TLDK API overview
STREAM API
CONFIG API
PKT IO API
tle_dev
  Each TLDK context operates independently.
  API can be logically divided into:
    Back-End (BE):
      Config API (dev add/remove).
      PKT IO (RX/TX bulk).
    Front-End (FE):
      stream control and IO (open(), close(), listen(), recv(), send(), etc.).
  BE API is not thread-safe.
  FE API is thread-safe.
tle_dev
tle_dev
DPDK + L2/L3 SW
init/configure
Application level
tle_stream
tle_stream
tle_stream
tle_stream
FRONT END
BACK END

## Slide 8: Possible deployment scenarios
CORE 1
BE ctx 0
stream
stream
CORE 0
eth 0
eth 1
1. one TLDK ctx, BE and FE on the same core
BE ctx 0
stream
stream
CORE 0
eth 0
eth 1
2. one TLDK ctx, BE and FE on different cores
BE ctx 0
stream
CORE 0
eth 0
3. two TLDK ctxs, for each BE and FE on the same core
stream
BE ctx 1
stream
CORE 1
eth 1
stream
BE ctx 0
stream
CORE 0
eth 0
4. two TLDK ctxs, BE and FE on different cores
stream
CORE 2
BE ctx 1
stream
CORE 1
eth 1
stream
CORE 3

## Slide 9: UDPFWD peak performance numbers (echo mode, ipv4/udp)
System Configuration |  |  | 
Hardware |  |  | 
CPU | E3-1285 v3 |  | 
Sockets | 1 |  | 
Cores per Socket | 4 (8 threads) |  | 
LL CACHE | 8MB |  | 
MEMORY | DDR3 1600 MHz, 2X4GB (total 8GB), 2 Channel per Socket |  | 
PCIe | Gen3x8 |  | 
NIC | Intel® XL710 for 40GbE QSFP+ Ethernet NIC (1x40G/card) |  | 
NIC Mbps | 40,000 |  | 
BIOS | BIOS Revision: 4.6 |  | 
Software |  |  | 
OS | Fedora 22 |  | 
Kernel version | 4.4.13-200 |  | 
Other | DPDK 16.07 |  | 
Chart: SINGLE STREAM
| 64 | 128 | 256 | 512 | 1024
fe+be@1core, 1HW queue | 20.4963 | 33.1824 | 60.9992 | 85.9757 | 99.8121

## Slide 10: UDPFWD peak performance numbers (echo mode, ipv4/udp)
Chart: Multiple streams, 64B pKT
| 32 streams (mpps) | 256 streams (mpps) | 1K streams (mpps)
1) fe+be@1core, 1HW queue | 9.6 | 9.21 | 9.09
2) fe and be@separate cores, 1HW queue | 13.11 | 15.86 | 13.54
3) 2x(fe+be@1core), 2HW queues | 19.15 | 18.39 | 17.71
System Configuration |  |  | 
Hardware |  |  | 
CPU | E3-1285 v3 |  | 
Sockets | 1 |  | 
Cores per Socket | 4 (8 threads) |  | 
LL CACHE | 8MB |  | 
MEMORY | DDR3 1600 MHz, 2X4GB (total 8GB), 2 Channel per Socket |  | 
PCIe | Gen3x8 |  | 
NIC | Intel® XL710 for 40GbE QSFP+ Ethernet NIC (1x40G/card) |  | 
NIC Mbps | 40,000 |  | 
BIOS | BIOS Revision: 4.6 |  | 
Software |  |  | 
OS | Fedora 22 |  | 
Kernel version | 4.4.13-200 |  | 
Other | DPDK 16.07 |  |